## Slide 1
Nanocrete
Background Information

## Slide 2: Overview
In today’s lesson we will turn the most common & most used materials into a Nanocomposite
Concrete pumper
Credit: AllMix UK

## Slide 3: In a Conventional Lab
This nanotechnology…
Cryo-crushing
Micro-grinding
Powder milling
Is normally achieved using equipment & supplies like this…
Powder mill
Credit: Shanghai Clirik Machinery Co., Ltd
Notes: Title: Conventional Lab
Explains the conventional equipment found in nanoprocessing:
Ultra fine micro-grinder – reduces the particle size of the materials) by 60%
Cryo (freeze) chamber – used for freezing material (makes it easier to crush)
Tensometer – used for tensile testing, the most fundamental mechanical test performed on materials, with results normally reported in Pascals (a unit of pressure). Related topics: Hooke’s law, Young’s modulus (elasticity), and the stress-strain curve.

## Slide 4: In a “Kitchen Lab”
This nanotechnology…
Cryo-crushing
Micro-grinding
Powder milling
Can be achieved (emulated) using equipment & supplies like this…
Notes: Title: Kitchen Lab
Explains equipment to be used in the Nanocrete module:
Coffee grinder to reduce the size of the material
Testing scenario (for tensile strength testing)

## Slide 5: Tensile Testing
 | Perlite | NanoPerlite
Mass (cured) | 152 g | 147 g
Cure Time | 6 days | 6 days
Load (to failure) | 36 Lbs. | 43 Lbs
Mix ratio | 6:4:4 | 6:4:4
Subsequent testing achieved similar results
Rules:
  Excessive water decreases concrete strength… PROPER amount enables flow & workability.
  Cure time affects everything… PROPER curing improves ALL properties of concrete.
  Concrete hardens as time passes, and with age… fractures and cracks.
Notes: Title: Tensile Testing
Introduces possible testing observations.

## Slide 6: Analysis/Conclusions?
Perlite “nanosized”
Although the aggregate (crushed Perlite) could only be reduced to an average of 25μm (using our “kitchen lab” methods), the material was changed significantly and results achieved were in line with predictions and/or the desired nano effect: a light, yet strong nano composite.
Surface area to volume
  Fine particles fill voids between cement grains
  Fine particles dispersed better
Priorities of forces
    Contact Zone – Hydration increases (a good thing) because dispersed, more reactivity
Extend activity by varying:
  Curing conditions
  Curing time
  Mix
23.4μm
2.92mm
Photomicrography provided by Nano-Link
Electron Micrographs
Notes: Title: Analysis/Conclusions?
Discusses the nano-effect observations.
Discuss the scale bars and the measurements achieved by micro-grinding the Perlite.
There is a question on the evaluation that requires conversion of the two measurements in the electro micrograph to nanometers. Discuss that our particle is not at the nanolevel, but it is 1-one thousandth away and significantly reduced from the bulk aggregate.

## Slide 7: The Nanomechanism
The nanomechanism is a principle/system that can explain the nano-effect (in this case, particle to particle contact and enhanced hydration) observed.
  View model/explanation of hydration. Hydration of Cement, National Science Foundation - video
    https://archive.org/details/gov.fhwa.ttp.vh-438
  Refer to the SEM of increase surface area to volume.
  Describe how cement particles might react with the nanosized particle i.e.: more surface area
Notes: Title: The Nanomechanism
Discusses the possible nano-effect observations.

## Slide 8: Where’s the Nanotechnology?
Nanocrete
Nanoprocesses: Grinding and Crushing one component, Perlite (the aggregate), to reduce its size
Material Processing: Mix ratios for components, hydration, curing, slump testing
Material Properties:
  Tensile test consistently yields positive results: a strong, light nanocomposite
  Slump, flow, density
Nanoconcepts:
  Sense of Scale – pre and post-crushed Perlite
  Surface Area to Volume Ratio – wasted air space removed, dispersion
  Priority of Forces – Hydration@smaller size particle, Hydrogen bonds, van der Waals
Notes: Title: Where’s the Nanotechnology?
This is background information; it can be used to reinforce what was learned during the activities.

## Slide 9: Nanocrete Terms to Know
Cementitious – being of/like cement
Mix ratio or Mix design: Always reported as aggregate:water:cement in terms of units, e.g.: 3:2:1 is a common mix design for bulk concrete (units can vary).
Concrete and cement are very different. Cement consists of a mixture of oxides of calcium, silicon and aluminum. Portland cement and similar materials are made by heating limestone (a source of calcium) with clay and grinding this product (called clinker) with a source of sulfate (most commonly gypsum).
Constituents - Cement is only one constituent of concrete. Other constituents are water and aggregate.
Micro-grinding and powder milling are nano-processes used to reduce a material.
Admixtures in the form of powder or fluids can be added to the concrete to give it certain characteristics not obtainable with plain concrete mixes.
Viscosity – resistance to flow
Curing & Hydration: Concrete solidifies and hardens after mixing with water and placement due to a chemical process known as hydration. The water reacts with the cement, which bonds the other components together, eventually creating a stone-like material. The reactions are highly exothermic (meaning heat generating) and care must be taken that the build-up in heat does not affect the integrity of the material.
Workability is the ability of a fresh (plastic) concrete mix to fill the form/mold properly (with vibration). Workability depends on water content, aggregate (shape and size distribution), cementitious content, and age (level of hydration). Raising the water content or adding chemical admixtures increases concrete workability. Excessive water leads to increased bleeding (surface water) and/or segregation of aggregates (when the cement and aggregates start to separate), with the resulting concrete having reduced quality.
Slump is the capacity of a concrete to deform under its own weight without any restraint, except from the friction of the surface.
Hydration Mechanics – process of removing water
Notes: Title: Nanocrete Terms to Know
Use this slide as a primer or for review of terminology encountered in the module. Add terms as needed.

## Slide 10: Nanocrete… What’s the Future?
Waterless Concrete Building on the Moon
Credit: NASA
Civil Engineering
Structural engineering
Architecture
Mechanical engineering
Aerospace!
Notes: Title: Nanocrete…What’s the Future?
Concludes the module or initiates further research/study about Nanocrete.
Concrete is unique in construction in that it is the only material exclusive to the concrete industry (it’s their business) and is therefore the beneficiary of a large proportion of the research and development money available from the industry.
Discuss jobs/areas of future study in this technical area. News feeds are a good source for this information. Some of the most promising areas for research/employment are listed on the slide. Go over each one, concluding with the most current/exciting developments in construction/defense/aerospace/medicine/etc. regarding the content covered in this module.
Example: during development of this module, new advancements included those reported in the referenced articles: “How nanotechnology can change the concrete world” and “Waterless concrete for the moon.” Imagine… building your concrete house on the moon!

## Slide 11
Pre-Activity
Set-up
Introduce topics: Concrete, composite, Nanotechnology used in processing
Nano-Effect
Set-up
Learners perform tensile test on the nanoparticle sample and the bulk sample and record results using a camera
Discuss and illustrate the nanomechanism that took place (hydration, surface area)
Learners work in teams to process and create a nano-particle based cementitious material
Nanosizing It
Set-up
Review Big Ideas