## Slide 1
Photolithography
Background Information

## Slide 2: Overview
The following slides present an outline of the process by which integrated circuits are made, of which photolithography is a crucial part. They may be presented as part of a lecture introducing the lithography activity.

## Slide 3: Introduction to Photolithography
http://www.ichaus.de/news/72

## Slide 4: Photolithography is the central technology in fabricating integrated circuits (ICs)
http://www.extremetech.com/computing/85304-intelmicron-fabrication-plant-tour?print
Here is a photo tour of an IC fabrication plant

## Slide 5
Idealized transistor design
Typical Integrated Circuit Element: A MOSFET Transistor
With permission from: Andrew Barron Applications for Silica Thin Films http://cnx.org/content/m24883/1.5/

## Slide 6
http://www.computerhistory.org/
Actual CMOS transistors as made on a wafer
Transistor dimensions are less than 100 nanometers

## Slide 7: Microfabrication Step 1: Circuit Design
Photo – courtesy IBM http://www.kasap.usask.ca/photos/
Into this: 3-D layout of
components
Design the 3D circuit structure.
Turn this: Schematic diagram

## Slide 8: Microfabrication Step 2: Mask Design
  Divide the structure
  into horizontal layers
  Capture the design of
  each 2-D layer in a
  photomask
Figures from www.technologystudent.com/elec1/ic2.htm, © 2006, V. Ryan

## Slide 9: The Circuit Photomask
  The photomask is the “master” pattern for all the circuit elements across the whole wafer for one layer
  Used repeatedly to make many, many copies
http://www.electrooptics.com/features/feature.php?feature_id=126

## Slide 10: Microfabrication
Using a mask and photolithography, we can replicate complicated circuits with millions of components in a very small space.
Hundreds of circuits made on each wafer; cut up, packaged, and tested
Basis for relatively inexpensive, powerful electronics
http://amath.colorado.edu/cmsms/index.php?page=an-immersed-interface-method-for-modeling-semiconductor-devices

## Slide 11: Making the Photomask
Photo: James Marti, University of Minnesota
Photomask generator, University of Minnesota Nanofabrication Center

## Slide 12: Microfabrication Step 3: Set up Process Steps
  Determine how to form each layer
    add material (deposition): build up a thin film of metal, insulator, or semiconductor material
    remove material (etching): take away previously deposited material from selected areas. This is similar to sculpting a block of stone or machining a block of metal to produce a structure to match the design.
    modify a layer:
      Doping: intentionally adding ionized impurities to tailor the layer’s electrical properties
      Oxidation: exposing a previously deposited layer (e.g., silicon, a semiconductor) to oxygen to make an oxide (e.g., silicon dioxide, a good insulator).

## Slide 13: Deposition Processes
Depositing metal films
Thermal Evaporation e-Beam Evaporation Sputtering
Figures from: http://www.vacuum-guide.com/english/equipment/ae_thin_film_deposition.htm

## Slide 14: Deposition Processes
Items to be coated (substrates) are placed in a vacuum chamber. A vapor of metal atoms is created in the chamber, which will coat all exposed surfaces in the chamber including the substrates.
In thermal evaporation, a block or wire of metal is heated with a resistive heating element to form the metal vapor.
In electron-beam evaporation, a block of metal is heated when a beam of energetic electrons is caused to impact the metal.
In sputtering, an ionized gas (a plasma) is formed and electrically attracted to a solid sheet of metal. This causes metal atoms to enter the vapor phase and move to the substrate, coating it.

## Slide 15: Deposition Processes
Depositing semiconductors and insulators.
Sputtering can be used
Also used is Chemical
Vapor Deposition. Reactive
chemicals (precursors) are
introduced into the vacuum chamber
where they react in the vapor phase.
The reaction products form a
condensing compound that coats the
substrate with a thin, regular film.
http://www.mechanicalengineeringblog.com/tag/graphene-properties/

## Slide 16: Layer Modification
Doping
  To make a useful component like a transistor or diode, a semiconductor like silicon must have certain impurities added. These are called dopants.
  Common dopants include boron, aluminum, gallium, nitrogen, phosphorus, and arsenic.
Oxidation
  A pure layer of silicon can have its surface turned into silicon dioxide (a very good insulator) by placing it into a hot oven with a pure oxygen atmosphere.

## Slide 17: Dopant introduction
Dopant atoms are introduced into a silicon substrate by either
  Vapor deposition
    Diffusion of gas-phase atoms
  Ion Implantation
    Accelerating a beam of dopant ions at the surface

## Slide 18: Dopants by ion implantation
  A beam of energetic dopant ions is impacted into the silicon surface, implanting the ion in the solid. These impacts introduce undesirable flaws in the silicon crystal, which must be repaired by annealing the materials at high temperature.
http://eng.thesaurus.rusnano.com/upload/iblock/1ba/ion%20implantation1.jpg with permission

## Slide 19
http://www.memsnet.org/mems/processes/deposition.html
Dopants by vapor diffusion
  Gas-phase atoms are introduced into a vacuum chamber where they can diffuse into the solid silicon. Elevated temperatures must be used to speed up the diffusion.

## Slide 20: Microfabrication Step 4: Pattern Transfer
The pattern is contained in the photomask. To replicate this pattern on a wafer substrate:
Deposit liquid photoresist on wafer by spin coating
Pattern the resist via exposure to light through the photomask
Develop the photoresist
Expose wafer to etchant. This attacks any exposed areas and “sculpts’ the wafer according to the pattern.
Wash the wafer
Repeat for next layer

## Slide 21: Photolithography process schematic
http://ahshonorschemistry.wikispaces.com/A-Silicon+Wafer+Patterned with permission

## Slide 22: Applying the Photoresist to a Substrate
Photoresist is a liquid chemical. It may be applied to the silicon wafer in many ways, but is most commonly spin coated.
A spin coater is a small, enclosed turntable that can spin at around 3000 rpm. It holds the wafer on its platter with a vacuum.

## Slide 23: Applying the Photoresist to a Substrate
First, a small amount of photoresist is applied to the wafer, then the wafer is spun to spread out the resist.
Typically only 1% of the resist ends up on the wafer; the rest is spun off.

## Slide 24: Applying the Photoresist to a Substrate
The photoresist dries by solvent loss as it thins out via spinning.
The result is a thin, uniform layer.

## Slide 25: Baking the Photoresist
The photoresist will still have some solvent left in it after spinning. It is heated slightly (the “soft bake”) to drive off any remaining solvent.
The wafer is now ready for exposure.
Hot plate

## Slide 26: Photoresist Exposure
In the simplest form of lithography, called contact lithography, the photomask is placed on the photoresist-coated wafer, and intense light is applied. Wherever the mask has openings, the resist is exposed and undergoes a chemical change.
Unexposed photoresist
Exposure Light
Photomask with openings

## Slide 27: Photochemistry
When light strikes the photoresist, its molecules under go a chemical reaction. The type of reaction depends on the type of resist used, either a negative or positive resist.
In a negative resist, the areas exposed to light become less soluble in a water-based solution called developer. The exposed areas remain while the rest of the resist is dissolved away.
In a positive resist, the areas exposed to light become more soluble in the developer. These areas are dissolved away in the developer, leaving everything else untouched.

## Slide 28: Negative and Positive Photoresists
Negative resist: open space in mask becomes an opaque feature on the wafer.
Positive resist: open space in mask remains an open feature on the wafer.
Exposed photoresist on wafer

## Slide 29: Photoresist Chemistry
Photoresists consist of polymer molecules dissolved in a solvent. Three very simple polymer molecules are shown here.
The C’s represent carbon atoms, the H’s are hydrogen atoms, and the hexagon is a 6-carbon ring. The pattern can repeat many thousands of times in a polymer.

## Slide 30: Photoresist Chemistry
When light strikes these polymer molecules, they undergo a chemical reaction. The type of reaction depends on the type of resist used.
In a negative resist, light exposure may make the polymers crosslink, which means they bond to neighboring molecules to form a strong network, like this:
These larger polymer molecules are much less soluble in a solvent (like the developer). So any spot on the resist-coated wafer that was exposed to light will not dissolve when the wafer is immersed in the developer solution. The unexposed (and thus un-reacted) molecules, on the other hand, will dissolve away in the developer.

## Slide 31: Photoresist Chemistry
When a positive resist is exposed to light, the polymer molecules tend to break into smaller fragments.
These smaller, lighter molecules are more likely to dissolve (or will dissolve more quickly) in the developer. The reaction with light may also create polar regions on the molecule, making it more likely to dissolve in water or water –based solutions.
So any spot on the resist-coated wafer that was exposed to light will readily dissolve when the wafer is immersed in the developer solution. The unexposed resist molecules will remain on the wafer.

## Slide 32: Developer Chemistry
After the photoresist-coated wafer has been exposed to light, it is immersed in a water-based solution called developer.
Photoresists are formulated so that the areas to be removed are acidic. If these acidic areas are exposed to a basic (or alkaline) solution, they will react and dissolve in the developer.
Developers are often basic solutions, such as potassium hydroxide (KOH) or sodium hydroxide (NaOH) in water.
Acidic group
Base
Molecule soluble in water

## Slide 33: Optical Systems for Exposing the Photoresist
Exposure systems must have intense light sources and precision optics to focus the light
This mercury arc lamp produces intense light in the blue, violet, and ultraviolet wavelengths
Photo: Osram Sylvania

## Slide 34: Contact and Projection Systems
In contact lithography, the mask is laid on the photoresist-covered wafer.
The mask pattern is directly reproduced in the resist—no change in size.
Mask in contact with wafer

## Slide 35: Contact and Projection Systems
In projection lithography, the mask patern is reduced in size using lenses.
The mask pattern is reduced by 5-10x in the resist, which allows much smaller features to be made.
Mask
Lens
Lens
Exposed pattern in resist is much smaller than in the mask

## Slide 36: Step 5: Etching Processes
Wet (chemical) etching
  Use a chemical that will dissolve the material that needs to be removed, while not interacting (as much) with the masking layer
  For Si, SiO2, hydrofluoric acid is used
Dry Etching
  Uses reactive ions/plasma to attack material
  Material is forced into vapor phase and pumped away

## Slide 37: Results of Etching
Wet (chemical) etching
  Rapid, isotropic (etches out as fast as down, may under-etch a feature)
Dry Etching
  Slower, anisotropic (can etch straight walls with a high aspect ratio)
Photo:
Futurrex Inc.
Photo:
University of Minnesota
Nanofabrication Center
Wet etching.
Dry reactive ion (DRIE) etching.

## Slide 38: Step 6: Repeat
Wafer is washed, and the next layer is built using same series of steps:
  Deposit film layer
  Modify if desired
  Transfer pattern using photomask and resist
  Etch
A typical IC can have over 15 layers

## Slide 39: An animated summary of the making of an integrated circuit can be found here:
The making of a chip - Youtube video
www.youtube.com/watch?v=d9SWNLZvA8g