## Slide 1
Nanocellulose
Background Information

## Slide 2: Overview
In today’s lesson we will turn one of the most common & most used materials into a Nanocomposite
Cellulose
Found in all Plant Cells

## Slide 3: In a Conventional Lab
This nanotechnology…
Emulsification
Fibrillation
Cryocrushing
Homogenization
Microfluidization
Micro-grinding
That is normally achieved using equipment & supplies like this…
Notes: Title: In a Conventional Lab
Explains the conventional equipment found in nanoprocessing cellulose:
Pulps are difficult to degrade; the trick is to separate (liberate) the cellulose molecule from lignin. Lignin has been called the “cement” it’s what holds everything together within the plant cell wall. Generally, mechanical processes that beat/agitate the bulk material (recycled paper) to separate the fibers are used. Many processes have been identified for producing micro or nanofibers. These processes include cryocrushing (feed material is frozen using liquid nitrogen prior to high impact forces being applied), homogenization, microfluidization (using extreme pressure to emulsify a fluid), and micro-grinding.
Typical equipment used to separate the fibrils from the cell wall:
• The ultra-fine friction grinder “Supermasscolloider” destroys fiber wall structure very efficiently to liberate cellulose microfibrils.
• The homogenizer is also used for this purpose (particularly in paper recycling,) but is less effective.
Because pulp is difficult to degrade, harsh chemicals (such as acids) are required.

## Slide 4: In a “Kitchen Lab”
This nanotechnology…
Emulsification
Fibrillation
Cryocrushing
Homogenization
Microfluidization
Micro-grinding
Plus
Screening
Pressing
That can be achieved (emulated) using equipment & supplies like this…
Notes: Title: In a Kitchen Lab
Explains equipment to be used in the Nanocellulose module:
In the activity, we are emulating a nanoprocess (fibrillation) being used to change cellulose.
As it turns out the process for creating micro/nanofibers is almost identical to that of paper making. We will use simple equipment found in our kitchen to emulate the nanoprocess and technology used to create nanofibers, plus a screening and pressing process used in paper recycling to create our nanocomposite.
Decades ago, researchers discovered that enzymes might be useful in processing cellulose. Enzymes are less harmful than acids in the processing (but care still needs to be used). Only recently have they been explored in the treatment of pulp and paper. The process is called fibrillation; adding the enzyme increases the inter-fiber bonding and literally pulls the fibers apart.

## Slide 5: Nanocellulose Test
 | Fibrillated Cellulose |  |  | 
Mass (dry) | .4 ozs | .7 ozs | .8 ozs | 1 oz
Dry Time* | 5 days De-mold in 1 | 5 days De-mold in 1 | 5 days De-mold in 1 | 5 days De-mold in 1
Mix ratio | 1:9:0 | 1:9:2 | 1:9:4 | 1:9:6
Results reported (conditions have been varied)
Rules:
  Dry time environment can vary*
  No known perfect mix ratio OR limits to what can be added
  Bulk material: 1:9 (Aggregate (wet):Water (1 unit = 1 oz.) + Fibrillation medium (1 unit = 1 Tbls.)
  Consistency standards: only decreased viscosity of the end pulp
Notes: Title: Nanocellulose Test
Results presented here were formed during making this module. Modify with your data and use this slide to review team results and findings.

## Slide 6: Analysis/Conclusions?
Photomicrography provided by Nano-Link
Electron Micrographs
It is very difficult to measure properties experimentally, but the material (paper) was changed significantly and results achieved were in line with predictions and/or the desired nanoscale effect: fibers in the substance (when wet) and varying states of rigidity when dry
Big Ideas to point out:
Sense of Scale
  Differences between samples
  Things you can point out:
    Cellulose fibers measure tens of microns wide (human hair) and about a millimeter long
    Cellulose nanofibers are about 1,000 times smaller than fibers
    Cellulose nanocrystals measure about 3 nanometers wide by 500nm long (about 1/1000th the width of a grain of sand)
Surface area to Volume Ratio – liberated fibers
  Treatment morphology - Characterization (via SEM) is critical to understanding the morphology
Self Assembly – fiber orientation
From Woody fiber-Microfibril to Nanofibril
Notes: Title: Analysis/Conclusions?
Discusses the scale bars on the SEM image and the measurements achieved by fibrillation. Not quite nanoscale, but…there is a difference between the samples. NOTE that further processing and equipment is needed to achieve nanocrystals.

## Slide 7: The Nanomechanism
The nanomechanism is a principle/system that can explain the nanoscale effect.
In this case, the nano-scale effect is the liberation of the fibrils and rigidity of the paper observed.
The nanomechanism is enzymatic hydrolysis, the breakdown of cellulose.
Notes: Title: The Nanomechanism
Discusses the nanoscale effect observations.
Usually hydrolysis is a chemical process in which a molecule of water is added to a substance. Sometimes this addition causes both substance and water molecule to split into two parts. In such reactions, one fragment of the target molecule (or parent molecule) gains a hydrogen ion.
A.K.A Enzymatic binding and degradation.

## Slide 8: Where’s the Nanotechnology?
Nanoprocessing: Emulsifying, fibrillation of wood/paper pulp to create a “gel” like substance (cellulose fiber and lignin* are separated)
Material Processing: Water-based processing of cellulose, coagulation, then pressing and drying (paper making)
Material Property Testing/Observation – the Nano-effect:
  General characterization/classification tests
  Track morphology (woody pulp to fibril to crystal) - SEM
Nanomechanism
  Enzymatic hydrolysis
Nanoscience Concepts:
  Sense of scale – fiber vs. nanofiber
  Surface area to volume ratio – liberated fibers, more contact
  Nature/structure of matter – cellulose (glucose) and enzyme (protein)
  Self assembly – fiber orientation (treatment morphology)
  Tools of nanoscience – fibrillation, SEM
Nanocellulose
Notes: Title: Where’s the Nanotechnology?
This is background information; it can be used to reinforce what was learned and emulated during the activities; use it as a primer for the quiz.

## Slide 9
Sample Observation Made for: | 0 | 2 | 4 | 6
Color |  |  |  | 
Odor |  |  |  | 
State |  |  |  | 
Material Characterization
Example Material Properties
Physical |  | Chemical | 
Density Thermal Electrical Magnetic |  | Oxidation Corrosion | 
Mechanical |  |  | 
Tensile Compression Shear Ductility Brittleness | Hardness Creep Toughness Fatigue Melting point |  | Strength Specific weight Elasticity Solubility Luster
Worksheet EXAMPLE for Characterizing a Nanomaterial
Material Classifications
Metal
Polymers
Ceramics
Composites
Notes: Title: Worksheet EXAMPLE for Characterizing a Nanomaterial
This is a student handout; modify as needed.

## Slide 10: Nanocellulose Terms to Know
Biological polymer: consist of long chains of glucose and is found in the cell walls of plants and bacteria. Cellulose is an example. Cellulose is made up of lignin and a glucose.
Glucose: a sugar.
Lignin is one of the constituents of cellulose, it acts as the “cement” that holds everything together within the plant cell wall.
Fibrillation is a nano-process used to liberate/extract fibers.
Composite: the combination of 2 or more materials that together exhibit improved proprties than when alone. An example is an airplane wing, typically construted of layers of wood, foam, and fiberglass glued together.
Wood as a composite: the main constituents are cellulose and lignin.
Nanocomposite contains one or more nanoscale constituents, i.e., materials with at least one dimension in the 100 nm range. These nanoscale additives are typically particles or fibers such as nanotubes.
Feedstock: the source material from which fibers are extracted (typically wood chips/recycled newspaper).
Viscosity: resistance to fluid flow.
Fibrillation: a process used to disintegrate a material into its constituent parts.
Enzyme: protein that catalyzes chemical reactions to breakdown or synthesize more complex chemical compounds.
Nanofibrils can be in the 5 to 20 nm range across and in the 10 nm to several microns range long, about 1,000 times smaller than conventional cellulose fiber.
Enzymatic hydrolysis: a degradation of a compound into its constituent parts. In this case: lignin and glucose molecules. Result is increase in fiber-to-fiber contact (bonding).
Catalyst: something that increases the rate of a reaction (chemical/molecular, etc.)
Permeability (a material property) refers to how much water can get in, solubility, porosity are similar terms.
Treatment morphology: refers to the change in size, alignment, and composition (liberation) when the lignin and cellulose molecules are separated.
Notes: Title: Nanocellulose Terms to Know
Use this slide as a primer or for review of terminology encountered in the module. Add terms as needed. Can be a handout.
Suggested definitions:
Nanoscience is the ability to observe, manipulate and measure things at the atomic and molecular level.
Nanotechnology is the ability to use what is learned from nanoscience to create, modify or improve things on a basic level.
Nanocomposite – having one or more constituents with nano dimensions 100nm or smaller.

## Slide 11: Nanocellulose… What’s the Future?
The U.S. Forest Service is producing 1 ton of nanocellulose per day
Customers include:
  Computing technology – flexible displays
  Health industry – super absorbent, antimicrobial films
  Manufacturing – aerogels for foams, injection molding, as a reinforcement fiber
  Food – low calorie “filler” found in processed foods (e.g., Eggo waffles)
Notes: Title: Nanocellulose…What’s the Future?
Concludes the module or to initiate further research/study about Nanocellulose.
Jobs/areas of future study in this technical area. News feeds are a good source for this information. The wide use of cellulose makes it a material for many areas from health care to construction. Some of the most promising areas for research/employment are listed in the following section.

## Slide 12
Review nanoscience
concepts
Pre-Activity
Set-up
Introduce topics: Cellulose nanofiber, Nanotechnology, used in processing
Nanosizing it
Set-up
Learner work in teams to
process and create cellulose
nanofiber paper
Nano-Effect
Set-up
Learners observe and
record observations in
property changes of each
of the nanofiber paper
samples
Discuss and illustrate the
nanomechanism that took
place (enzymatic hydrolysis)