## Slide 1: First Five 05c
If a 5 volt battery is attached to terminals A and C, how much current is flowing through the 220 resistor?
How much voltage is dropped across the 470 resistor? (i.e. what is the potential difference between node A and node B?)
470
220
A
C
B

## Slide 2: Kirchhoff’s Current Law

## Slide 3: Kirchhoff’s Current Law
Measure current through a DC motor.
Measure current from a power source.
Measure current through a resistor in a circuit.
Verify Kirchhoff’s Current Law.
Use KCL to analyze a circuit.

## Slide 4: Measure the Current through a DC motor
Red lead is plugged into DC10A jack.
Dial is set to DC10A position
Jumper wire is used to connect multimeter to circuit
The multimeter is part of the circuit when measuring current
5V
+
-
M
TIP: Connect everything but the jumper wire (blue wire pictured) first. Hold the motor at the base and then connect the jumper wire last. The fan will turn fast, do not touch the blades with your fingers when it is rotating.
5V
+
-
M

## Slide 5: Measure Total Current from Power Source
Step 3: Connect multimeter leads to where current flows through the multimeter as part of the circuit.
Red lead is plugged into multi jack.
Dial is set to DCmA position
470Ω
220Ω
5V
+
-
Step 2: Pull out one wire in section where current is being measured. Place one end of jumper wire at that location.
  To measure current, multimeter must be part of circuit
470Ω
220Ω
5V
Step 1: Build Circuit
Connection Point (node)
5V
Ground

## Slide 6: Measure Current through Each Resistor in Series Circuit
470Ω
220Ω
5V
Current leaves the power source at a value and stays the same through each component in the loop
Compare with calculations. What is the total current from the power source?
Use Ohm’s law:
Notice the units are mA
1000mA = 1A
Why do you think the calculated values are a slightly different than the measured values?

## Slide 7: Build Parallel Circuit and Measure Total Current from Power Source
+
-
220W
470W
5V
LOOP 1
LOOP 2
Compare with calculations:
5V
Ground
Connection Points (nodes)
5V
+
-
220Ω
470Ω

## Slide 8: Measure current passing through each resistor
+
-
220W
470W
5V
LOOP 1
LOOP 2
Current through470Ω resistor
Current through 220kΩ resistor
Current is divided between the loops of the circuit
Compare with calculations:
LOOP 1
LOOP 2
From KVL

## Slide 9: Kirchoff’s Current Law (KCL)
The current entering a junction point, or node, equals the sum of currents leaving a node
At A Node:
Series Circuits:
10kΩ
4.7kΩ
9V
No node where current can split; current is same through circuit
Parallel Circuits:
Current splits at node
More current passes through smaller resistor
+
-
4.7kW
10kW
9V
Node
I = 0.6mA
I1 = 2.8mA
I2 = 1.9mA
I3 = 0.9mA

## Slide 10: Class Problem
+
-
4.7kW
10kW
9V
Use Ohm’s Law and KVL/KCL to find the current in each branch of this circuit.

## Slide 11: More on Nodes
For the given circuit, identify the physical location of a node?
+-
220W
470W
5V
The connected rows on a breadboard allow for multiple components in a circuit to be joined together. They create junction points…nodes.
Identify the nodes for the given circuits:
5W
Vs
+
-
30W
20W
45W
20W
Vs
+
-
R1
R4
R2
R3

## Slide 12: Electrical Current Behaves like water in a River

## Slide 13: Implications of KCL
+
-
1000Ω
9V
1000Ω
500Ω
Node
I1
I2
I3
I
Node
What is current here?
More current travels in direction of lower resistance
Current remains the same through series resistors
Node
Current splits at a node when there are multiple paths it can take.
Current into a node equals current out of a node

## Slide 14: Implications of KCL
The algebraic sum of currents entering or leaving a node is zero
+
-
+
-
+
-
Sum up these currents
current entering node = positive &
current leaving node = negative
current in = current out
electrons are neither created nor destroyed

## Slide 15: What happens if the component(s) enters and leaves the circuit through the same node?
If the algebraic sum of currents entering or leaving a node is zero, then the current should be zero for that component(s).
+
-
4.7kW
10kW
9V
Identify nodes
If the component(s) enters and leaves through the same node, no current passes through it.
You can treat the problem, like that portion is not there.
Node 1
Node 2

## Slide 16: Assignment
Find total current leaving the power source by calculating Req and using Ohm’s Law.
Use KVL to determine the current through the resistors.
+
-
1000Ω
9V
1000Ω
500Ω
I1
I2
I3

## Slide 17: Assignment
Find total current leaving the power source by calculating Req and using Ohm’s Law.
Use KVL to determine the current through the resistors.
220Ω
+
-
680Ω
9V
1000Ω
470Ω
I1
I2
I3

## Slide 18
220Ω
+
-
470Ω
12V
1000Ω
520Ω