## Slide 1: Technical I Rotating Equipment Part II
Compressors
Development of a 21st Century Industrial Process Operations Program is supported by the National Science Foundation under Grant No. 1700558. Any opinions, findings, and conclusions or recommendations expressed on this site are those of the authors and do not necessarily reflect the views of the National Science Foundation.

## Slide 2: Industrial Compressors
Used to transfer gas at high to very high pressure
  Typical pressures ranges: 500 - 5000psi
  Special compressors can reach >10,000psi
Two types
  Centrifugal (Multistage)
  Reciprocating (recip)

## Slide 3: centrifugal Compressors
Centrifugal
  Works on the centrifugal force principle
  Uses multiple impellers in a single housing (barrel or case) to increase total developed pressure
  Outlet of stage 1 is fed into the inlet of stage 2, outlet of stage 2 is fed into the inlet of stage 3 ………
  Final outlet developed pressure is primarily a function of the number of stages and speed.
  Compressor flow is primarily a function of impeller size and speed.
  centrifugal compressor typical speed ~8800PRM

## Slide 4: centrifugal Compressors

## Slide 5: centrifugal Compressor construction
Diagram Key Code
1. Casing 10. Balancing Drum
2. Support Pier 11. Labyrinth Seal
3. Inlet 12. Seal Vent
4. Inlet Wall and Guide 13. Oil Seal
5. First Stage Impeller 14. Gas Seal
6. Diffuser 15. Bearing Housing
7. Return Channel 16. Journal Bearing
8. Return Bend 17. Thrust Collar
9. Discharge 18. Thrust Bearing

## Slide 6: centrifugal Compressors
Installation typically requires:
  Inlet separator (knockout drum)
  Inlet plenum
  Pressurized lubrication system
Generally utilizes product cooling
  Required to reduces the temperature of the gas do to “heat of compression”
  Increase efficiency and reliability

## Slide 7: centrifugal Compressors
https://www.youtube.com/watch?v=MgJlHW22KRY
https://www.youtube.com/watch?v=2z8dwFsdRLg

## Slide 8: centrifugal Compressor operator issues
Surge
Liquids induction
  Any type of liquid induction will damage the compressor
  Liquids separator vessel used to remove any residual liquids from inlet supply
  Commonly called “suction or inlet knockout”
Feed composition changes
Heat
Vibration
Lubrication issues

## Slide 9: centrifugal Compressor operation
Stonewalling
  Stonewall or choke point for a centrifugal compressor occurs when the resistance to flow in the compressor discharge line drops significantly below the normal levels.
  Can cause the compressor rotor to become unbalance and start “thrusting”
    Severe axial loading of the rotor

## Slide 10: centrifugal Compressor Surge
Centrifugal compressors must operate within their defined flow curve.
  All centrifugal compressors have a flow curve and a specific minimum flow requirement
    Commonly called the “surge line”

## Slide 11: Compressor surge Line

## Slide 12: centrifugal Compressor surge
Operating below the minimum flow results in “surge”
  Surge is the rapid fluctuation of the stage pressures which causes flow reversal which will damage the compressor.
    https://www.youtube.com/watch?v=W8DMun06NXg
  To maintain the compressor above the surge line an “anti-surge” system is required
    Also called “spill back or “snort” system
  https://www.youtube.com/watch?v=l1hjaXZE93w

## Slide 13: Compressor surge

## Slide 14: centrifugal Compressor Surge Control

## Slide 15: ISA centrifugal compressor symbol

## Slide 16: Reciprocating (recips) compressors
Work by positive displacement
Single or multiple cylinder arrangements (throws)
  Typical: 1.2.4.6 throws
Each cylinder Typically compresses in both directions
Cylinders arrangements can be;
  in parallel (higher flow/lower pressure)
  In series (higher pressure/ lower flow)
  Combination parallel & series

## Slide 17: Reciprocating (recips) compressors
Typical operating speed <1800RPM
  Large units 150-300RPM
Installation typically requires:
  Inlet separator (knockout drum)
  Inlet plenum
  Pressurized lubrication system
  Outlet pulsation dampener
Generally utilizes inter-stage cooling
  Required to minimize “heat of compression”
  Increase efficiency and reliability

## Slide 18: recip Compressors operator issues
Overpressure and deadhead protection
  Required to protect system from over pressurization and deadheading
    Over pressure protection to prevent catastrophic failure
    Deadheading rapidly increases compression heat and can damage the compressor
  Required both for the final pressure and the Interstage pressures
    Final pressure maybe a safety relief or spillback system or both
    Interstage are typically a spillback

## Slide 19: recip Compressors operator issues
Valve issues
  The inlet and outlet check valves are under constant and rapids operation and can be exposed to contaminates.
  They are subject to seat wear, spring breakage and sticking.
  Leaking creates excessive heat and reduced compressor efficiency
    Temp or vibration monitoring
    Compressor efficiency monitoring
  In extreme situations the check valve failure can cause catastrophic unit damage
    Dropping
    Lubrication loss on crankshaft bearing

## Slide 20: recip Compressors operator issues
Liquids induction
  Any type of liquid induction will damage the compressor
  Liquids separator vessel used to remove any residual liquids from inlet supply
  Commonly called “suction or inlet knockout”,
Rod drop
  Piston rider rings wear and piston scores the cylinder
Heat
Unbalance
Vibration
Lubrication issues

## Slide 21: What are reciprocating compressors?
Parts of the reciprocating compressor
Machine images
Notes: Gas transmission applications are typically powered by a reciprocating engine fueled by natural gas. These compressors may be located in the field at a remote station or at the inlet to a gas plant where raw, wet (containing droplets of water or hydrocarbon) and possibly sour (containing hydrogen sulfide, H2S) natural gas is compressed.
Why are hydrocarbon compressors horizontal?
Most practical way to meet mechanical balance and sealing requirements.
Crosshead is different that automobile engines because the need to control gas leakage.
Must have a robust frame, particularly in offshore applications where the platform itself is not particularly robust.
Driven by electric motor, gas turbine or diesel engine. A gearbox may be required to match the driver to the compressor speed.
Not normally variable speed since you can vary the output by reducing cylinder efficiency using clearance pockets, control on suction valve opening and offloading cylinders.
Safety is dominated by their piston rod sealing systems.
Modern compressors can range in speed from 500 to 1000 rev/min. Older recips are usually slower.
Compressors inherently increase the superheat in the gas being processed. Hence any free moisture in the gas will evaporate. Any tars or salts will be deposited on internal surfaces, particularly on valves. This will cause fouling. Similarly any solids e.g. dust or catalyst particles will potentially be deposited. These can cause loss of performance by restricting the valves or jamming piston rings, increase leakage by damaging piston rod seals, and in extreme cases cause mechanical damage by limiting piston travel thus overloading bearings.
Reciprocating compressors are in general intolerant of the ingestion of liquid. Slugs of liquid can cause major damage and a major gas release. If there is any risk at all of liquid, the inlet piping must be designed to avoid liquid ingestion. In all cases, the low points of inlet pipes require manual low point drains, for checks after overhaul / cleaning work. The drain valve should be of straight-through design e.g. plug or ball, permitting a wire or even an optical probe (borescope) to be used for a cleanliness check. The worst design is a long horizontal suction line, with a rising bend to the compressor. Liquid can collect in the line at low flow rates; this is swept up into a wave when flow is increased. A suction knockout pot as close as possible to the compressor, with drains, level detection, alarm and trip, is the normal solution. If liquid is rarely found, the drain valve may be blanked off. While some compressors can tolerate sucking in a mist of clean liquid with no ill effects (in some cases this is used for inter-stage evaporative cooling) accumulation of liquid must be avoided. Operating practices must ensure that all pipework is fully drained of liquid prior to restart the machines, and the machine itself does not contain liquid from process or internal leakage.
The potential for leakage of cooling water into the machine during normal operations is normally low, however during machine shut downs the risk significantly increases. Any liquid ingress into the machine may result in the machine becoming liquid locked with catastrophic results. Operator activity is required to prove the machine clear prior to any reestablishment, and it is good practice to isolate drain down cooling systems during any extended off line period.
A gas compressor can be driven backwards e.g. by incorrect electrical connections to the motor. The compressor will run and will compress gas, but the bearings and lubrication system are not intended for reverse running and will be damaged. The shaft driven oil pump, if fitted, may well not work if run backwards.

## Slide 22: Reciprocating Compressor Parts
Valves
`
= gas flow direction
`
Valve Parts
Notes: Piston
Piston rings act to decrease gas leakage
Piston bands are shaped to create an oil wedge to create a barrier.
Piston rod, with screw thread fasteners at both ends
Piston nut
Suction knock-out pots for liquid water or light hydorcarbons that condense out (installed immediately prior to the suction manifold with level detection and drainage)
- intercooler and aftercoolers to cool the discharge gas and drop out liquids and also require knock-out arrangements
- during start-up, discharge gas is often returned to the suction through a recycle valve. The recycle route should have a cooler.
Crankshaft
Crankcase bearing (main bearing)
Distance piece holds the Pressure packing whose purpose is to seal the long piston and rod system
Cylinder bore, is typically a sleeve that can be changed, alignment and leveling should be checked periodically
The space between the cylinder liner and cylinder wall is often used as a water cooling jacket. Which can pose a know risk of leaking cooling water into cylinder bore.
- cylinder and valve layout should promote liquid drainage.
Valves, seat, shutter, springs
Big end bearing (big end of connecting rod), little end bearing
Pressure packing seal
Oil wiper seal (wipes off oil from the crankcase and returns it to the sump, and also acts as a backup seal to the pressure packing)
Cross head shoe, oil lubricated
Crankcase atmosphere is air or nitrogen
May have up to 8 cylinders in pairs.
Loose or failure of the piston nut
Loose or failure of cross head nut
either can lead to piston being driven into the cylinder end or bending a piston rod
Bent or unsupported piston rod can wreck piston seals.
- Liquid may condense inside the compressor due to inter-coolers and water cooled cylinder jackets.
Failure of a valve cover or valve retainer could cause ejection of the valve complete with cover.
Liquid ingress, moisture carry over, liquid slugs, liquid ingestion: lubrication system should be inhibited while the machine is ofline to avoid a build up of oil. (oil is 3 – 5 bar). Oil can drip or spray when damaged when can pose risk of fire, toxicity, slip or eyes.
A change in the process gas composition, caused by a process upset or change in feedstock, can rapidly change the compressor discharge temperature or pressure. Reciprocating compressors are relatively tolerant to composition changes.
Failed crankshaft bearing can generate significant heat and can ignite oil. Nitrogen in the crank case can limit exposure to fire, but don’t open the crankcase while hot, or the inrush of air can immediately cause a fire or explosion.
Mechanical shaft coupling should be checked for misalignment and vibration. Misalignment waists energy. For turbine driven compressor, overspeed is a risk of a sheered coupling.
- Machine failures can be rapid with the loss of balance. It can quickly lead to loosening of connections and containment bolting.
- Failure or partial failure of the machine valves will result in gas recycling within the machine. This can cause high temperatures within the machine, the balance of forces within the machine to be disturbed sufficient to cause bearing overload, interstage pressures to be to high, thus lifting interstage relief valves, and the potential for larger back-flow through the machine once shutdown.
Reduction in the capacity of the machine can be achieved by offloading one or more cylinders. Though this can be designed as a normal operating mode, the faciltiy can be available for use during transient operations (start up / shut down). Such options in the machine operation can cause an imbalance of forces, in this case the configuration may only be suitable for short term activity and extending the activity can lead to machine failure.
If a standby compressor is already connected up and under automatic control, load may be shed to it without operator intervention. This is likely to pose negligible risk. If operators feel obliged to bring a spare machine into service quickly, they may take potentially hazardous shortcuts, for example omitting gas purging. If the status of a machine under overhaul is in doubt, and this machine is brought back into service in a hurry, serious risks are being taken.
Where the installation is subject to significant motion, for example when under tow or during a storm, the motion may exceed the capabilities of the compressor. The unit may have to be shut down as a precautionary measure; otherwise mechanical damage may be caused. The most sensitive system is likely to be the lubrication oil system; movement or roll angles may interfere with oil distribution & return, or cause spurious level trips.
Recips are not good for emergency duty as they require operator checks and attention during start, for example liquid in suction line.
- crankcase must be very stiff since it provides support for all of the working motion.
- if you have 4 cylinders, means for throws,
- passages in the crankshaft and connecting rods provide continuous pressure fed lubrication.
Often overlooked parameters:
flow control
Suction pressure
Discharge pressure
Speed
Suction and discharge throttle valve control
Rod reversal is required to ensure to ensure bearing lubrication
Power consumption
Lbrication pressure, flow and temperature

## Slide 23: Reciprocating Compressor Parts
Valves
`
`

## Slide 24: Reciprocating Compressor Parts
`
`
Big end bearing
Crankshaft
Inlet Plenum
Pressure pulsation vessel
The Bottles
Connecting rod
Main bearing
(crankshaft bearing)

## Slide 25: Reciprocating Compressor Parts
Piston
Rider band
Piston rod
Pressure packing
`
`
Oil wiper packing

## Slide 26: Reciprocating Compressor Parts
Crosshead
Crosshead
shoe
Crosshead pin
Crosshead
guide
`
`

## Slide 27: Reciprocating Compressor Parts
Main Frame
Distance piece
Or
Doghouse
cylinder
Cylinder liner
Main frame
Distance piece
Cylinder
`
`

## Slide 28: Reciprocating Compressor Parts

## Slide 29: Isa symbol
Not standardized
Most use a pictorial representation