## Slide 1: Heat TRANSFER CONCEPTS & Heat EXCHANGERS
Development of a 21st Century Industrial Process Operations Program is supported by the National Science Foundation under Grant No. 1700558. Any opinions, findings, and conclusions or recommendations expressed on this site are those of the authors and do not necessarily reflect the views of the National Science Foundation.

## Slide 2: Heat transfer
What is heat?
    It is a from of energy
    All “bodies” have some level of heat energy.
      In science/engineering there is no such thing as cold, it’s the lack of heat energy.
    It can be environmentally induced, externally generated or self-generated.
    Heat can be added to or removed from a “body”.
    Heat always moves from the Higher heat body to the Lower heat body.

## Slide 3: What factors affect heat transfer?
Discussion

## Slide 4: Measurement of Heat
Heat energy is measured in BTU’s
    It is the amount of energy needed to raise the temperature of one pound of water by one degree Fahrenheit (Physical analogue: one four-inch wooden kitchen match consumed completely generates approximately 1 BTU).
    In science, the joule, the SI unit of energy, has largely replaced the BTU. The British thermal unit (BTU or Btu) is a traditional unit of work equal to about 1055 joules.
    In US industry the BTU is still predominant
    From Wikipedia, the free encyclopedia

## Slide 5: Thermodynamics
Thermodynamics is a branch of physics concerned with heat and temperature and their relation to energy and work.
  For this class we are only going to concern ourselves with the amount of heat in a specific mass of a fluid(s) and the transfer of heat energy between fluids.
  From Wikipedia, the free encyclopedia

## Slide 6: enthalpy
n(General Physics) a thermodynamic property of a system equal to the sum of its internal energy and the product of its pressure and volume. Symbol: H Also called: heat content or total heat
Collins English Dictionary – Complete and Unabridged, 12th Edition 2014 © HarperCollins Publishers 1991, 1994, 1998, 2000, 2003, 2006, 2007, 2009, 2011, 2014

## Slide 7: Definitions:
  Saturated Liquid:
    the point (at any given pressure) that the liquid has “absorbed” the maximum amount of BTU’s and still remains 100% liquid.
  Saturated Vapor:
    the point (at any given pressure) that the liquid has been completely converted to a vapor (saturated or 100% quality steam) and no additional BTU’s have been absorbed.
      Best condition for heat transfer.
  Latent Heat (of vaporization)
    the quantity of additional heat energy (BTU’s) necessary to convert a saturated liquid to saturated vapor or visa-versa.
  Superheated Vapor:
    a vapor with excess heat energy over that required to maintain saturated vapor condition. Can be or intentional or unintentional.
      Best condition for mechanical work.

## Slide 8: Thermodynamic Example: Water & Steam
Ref: CVS Power Document

## Slide 9: Steam Tables
http://www.spiraxsarco.com/global/us/Resources/Pages/steam-tables.aspx
http://www.tlv.com/global/TI/calculator/steam-table-pressure.html

## Slide 10: Common Heat exchanger types
  Shell & Tube
  Fin-Fan
  Plate & Frame
  Kettle Reboiler
  Electric Heaters
  Gas Fired Heaters
  Jacketed Vessels
  Cooling Towers
  Furnaces
  Thermo-compressors
  Direct steam injection

## Slide 11: Shell & Tube

## Slide 12: Shell & Tube

## Slide 15: ISA symbology