## Slide 1: Process Operations Technical I
Gauges & Gauging
  Local indicators of a specific fluid property
    Pressure, Temperature, Level, Flow
Development of a 21st Century Industrial Process Operations Program is supported by the National Science Foundation under Grant No. 1700558. Any opinions, findings, and conclusions or recommendations expressed on this site are those of the authors and do not necessarily reflect the views of the National Science Foundation.

## Slide 2: Local Sight Level Indicators (Gauges)
Level gauges provide an indication or measurement of the level (how full) a vessel/tank is.
Typical measurements are:
  Percent
  Dimensional i.e.: inches, feet, meters etc.
Generally it does not tell you the amount (quantity) of product in the tank
  i.e. gallons, tons, barrels
  Occasionally special scales are utilized to indicate quantity.

## Slide 3: LEVEL

## Slide 4: Level Accessories
Gauge/Block Valves
Drain & Vent Valves
Armor
Insulators & Heaters

## Slide 5: Typical Common Level Gauges
Light Duty Tubular

## Slide 6: Typical Common Level Gauges
Industrial General Purpose

## Slide 7: Other Level Gauges
Special Purpose

## Slide 8: ISA Symbols for Local Level Indicator or Gauge
Side Mounted Top or Bottom Mounted

## Slide 9: Tank Gauging
The manual inspection and measurement of the level of product in a storage vessel using a “strapping” tape or stick

## Slide 10: Local Pressure Indicators (Gauges)
What is Pressure?
  Force per Unit of Area
  Common Imperial Units of Pressure Measure:
    Pounds per Square Inch Gauge (PSIG) (Commonly noted as just PSI)
    Pounds per Square Inch Absolute (PSIA)
    Others: inHg, in of H2O (“wc), Feet of water, Feet of Head
  Common Metric:
    Bar
    mmHg
    Kilograms per Centimeter Squared (Kg/cm2)
    Kilopascals

## Slide 11: Local Pressure Indicators (Gauges)
Other Pressure Measurements?
  Differential Pressure
    What is Differential Pressure
    A measurement of the difference in pressure between to two points
      Can be directly measured or calculated
      Common short hand: DP, ΔP
    Common Units: PSID, “wcd, BARD.
  Vacuum
    What is a Vacuum?
    It is a pressure that is less then the surrounding atmospheric pressure
    Common units are: PSIA, Torr, “HG, -PSI

## Slide 12: Typical Pressure Gauges
Standard Pressure Gauges

## Slide 13: Other Common Gauges
Compound Gauge Differential Gauge Vacuum Gauge

## Slide 14: Gauge Accessories
“Tic” Marks
“Tattletales”
Safety Indicator
Gauge Valves
Block & Bleed Valves
Siphons (Pigtails)
Diaphragm Isolators

## Slide 15: Pressure Gauges with Accessories

## Slide 16: Other Accessories
Gauge Valves (Needle Valves)
  Valve that isolates the gauge from the process
What issue might you have utilizing a simple gauge valve?

## Slide 17: Other Accessories
Block and Bleed Valve
Adds addition safety when removing the gauge by providing safer venting

## Slide 18: Other Accessories
Siphons
  Provide isolation between the gauge and hot vaporous process fluids (Steam)
Isolators
  Provides protection for the gauge from corrosive, toxic or high temperatures. Also provide method to measure pressure on slurry applications.

## Slide 19: Reading a Pressure Gauge
Requires Interpolation Skills
  What is Interpolation?
    A method of constructing new data points within the range of a set of known points.
  Highly dependent on gauge size, accuracy and scale resolution
    Typical interpolation with process gauges is to one half the scale resolution

## Slide 20: ISA Symbols for Local Pressure Indicator or Gauge

## Slide 21: Temperature Gauges
What is Temperature?
  An arbitrary scale used to indicate how “hot” (or cold) something is.
  It is NOT a measure of the heat energy in a specific body or fluid
  Most common temperature measurement scales are:
    US: Fahrenheit (F or °F)
    Rest of the world Celsius (C or °C)

## Slide 22: Typical Temperature Gauges

## Slide 23: Temperature Gauge Accessories
Thermowells
  Why?
  Fluid flowing over the body (temp element) produce bending force and vibration resulting in element failure.
  Thermowells provide mechanical protection and isolation from the process fluids

## Slide 24: Reading a Temperature Gauge
See “Reading a Pressure Gauge”

## Slide 25: ISA Symbols for Local Temperature Indicator or Gauge

## Slide 26: Local Flow Indicators (Gauges)
What is Flow?
  A Measurement of the Quantity of a Product “Passing a Specific Point, in a Specific Time Period, utilizing a Specific Unit of Measurement”.
  Common Imperial Units of Flow Measure:
    Gallons per Minute (GPM)
    Pounds per Hour (PPH)
      KPPH, MPPH, MMPPH
    Standard Cubic Feet per Hour (SFCH)
    Tons per Day (TPD)
  Common Metric:
    Cubic Meters per Hour (M3H)
    Liters per Minute (L/P)
    Kilograms per Hour (Kg/H)

## Slide 27: Typical Local Flow Indicators

## Slide 28: Reading a Flow Gauge
See “Reading a Pressure Gauge”

## Slide 29: ISA Symbols for Local Flow Indicator or Gauge