## Slide 1: Technical I Rotating Equipment Part III
Pumps
Development of a 21st Century Industrial Process Operations Program is supported by the National Science Foundation under Grant No. 1700558. Any opinions, findings, and conclusions or recommendations expressed on this site are those of the authors and do not necessarily reflect the views of the National Science Foundation.

## Slide 2: Industrial pumps
Used to transfer liquids at any pressure
  Typical pressures ranges: up to 3000psi
  Special pumps can reach >10,000psi+
Two types
  Centrifugal (single or Multistage)
  Reciprocating (recip)

## Slide 3: Industrial pumps
Most common is the centrifugal Pump
Relies on the principal of centrifugal force.
  It converts the energy provided by a prime mover (i.e. electric motor, steam turbine, or gasoline engine) to energy within the liquid being pumped

## Slide 4: Types of Centrifugal Pumps
Most common
Single stage
  Overhung
  Center-hung
Multi-stage
  Always Center hung
Split case/double suction pump
  Derivation of a center hung pump
Other types
Slurry pump
Submersible pump
Sump pump
Inline pump
Axial Flow Pump
Vertical Turbine pump

## Slide 5: Single stage Overhung pump

## Slide 6: Multistage center hung pump

## Slide 7: Split case double suction

## Slide 8: How a pump works: Simplified
Consists of rotating impeller inside a stationary casing (Volute)
Liquid enters the pump through the suction inlet of the impeller (eye)
The speed of the rotating impeller forces the liquid out through the discharge

## Slide 9: How it works: Overview
Liquid enters suction side and flows into the eye of the impeller
Centrifugal force is exerted on fluid by impeller, this moves the liquid from the eye, along the vanes, to the tip of the impeller.
It is forced against/along the walls of the casing and out through the discharge.
Due to the fluid particles being dislodged from the impeller eye, it reduces the pressure which draws in continuous flow

## Slide 10: How it works: Overview Cont.
Casing Shape: Wider at discharge then where impeller forces liquid against the case
When the liquid strikes the side of the case, the velocity increases. This accelerated energy is called “Kinetic Energy”
As the liquid travels through the volute, the area of the volute expands allowing the liquid’s velocity to slow down.
As the liquid slows down, the Kinetic Energy is changed into Potential (pressure) energy. The pressure forces the liquid out of the discharge.

## Slide 11
https://www.youtube.com/watch?v=BaEHVpKc-1Q
https://www.youtube.com/watch?v=Vhc-hEjh12I

## Slide 12: Basic pump construction

## Slide 13: Centrifugal Pump Advantages
Utilizes small floor space
Simple operation
Low first cost and maintenance
Can handle clean, dirty and slurry products
Impeller, shaft and bearings are the only moving parts
Fairly quiet operation
Can utilize a wide range of fluids and flows
Lower operating pressures result in a more compact unit

## Slide 14: Centrifugal Pump Disadvantages
Are usually not suitable for high pressure delivery at low volumes
Usually cannot handle high viscosity liquids
Single stage pumps are limited to lower pressure applications
Higher pressure applications require multistage pumps

## Slide 15: Positive displacement pumps
Work by positive displacement
Utilized for relatively low flows
capable of high pressures (10,000+PSI)
Multiple designs
  Metering pump
  Gear
  Reciprocating Piston
  Vane
  Lobe
  Diaphragm
  Peristaltic
  Screw
  Progressive cavity
Generally limited to fairly clean fluid

## Slide 16: Metering Pump
Used for product/chemical injection
Typically a single piston or diaphragm pump design
Generally quite small (a few GPM)
Can be high pressure
Will have a methods to:
  Adjust the displacement per stroke
  Adjust the number of strokes per minute

## Slide 17: Gear & Vane Pumps

## Slide 18: Piston/Recip Pumps

## Slide 19: Misc. PD Pumps

## Slide 20: Positive displacement pump operator issues
Pumps may need an inlet strainer
  Requires maintenance program/schedule
Must have a relief system
  If outlet deadheaded; Positive displacement pumps will continue build pressure until:
    Prime mover stalls
    Something ruptures
Generally self priming (to a point)
  Flooded suction is always better