## Slide 1: Rankine Cycle
Review of Components
Development of a 21st Century Industrial Process Operations Program is supported by the National Science Foundation under Grant No. 1700558. Any opinions, findings, and conclusions or recommendations expressed on this site are those of the authors and do not necessarily reflect the views of the National Science Foundation.

## Slide 2: Rankine Cycle Components

## Slide 3: Pumps
Name a couple different types of Pump?
What is the Rankine Cycle Pump Called in industry?
What does the Rankine cycle pump do?

## Slide 4: Boilers
Many types of Boilers out there?
Name 3 Types of Boilers ?

## Slide 5: Turbines
What are different uses for Turbines?
What types of Turbines are there?

## Slide 6: Condenser
What is the purpose of the Condenser?
Are there other uses for the condenser?

## Slide 7: Pump And The Rankine Cycle
Pump: The liquid condensate leaving the condenser at the state 1 is pumped to the operating pressure of the boiler. The pump operation is considered isentropic.

## Slide 8: Boiler and the Rankine
Boiler: The heat is supplied in the working fluid (feed water) in the boiler and thus vapor is generated. The vapor leaving the boiler is either at saturated at the state 3 or superheated at the state 3||, depending upon the amount of heat supplied by the boiler.

## Slide 9: Turbines and the Rankine Cycle
Turbine: The vapor leaving the boiler enters the turbine, where it expands isentropically to the condenser pressure at the state 4. The work produced by the turbine is rotary (shaft) work and is used to drive an electric generator or machine.

## Slide 10: Condenser and the Rankine Cycle
Condenser: The condenser is attached at the exit of the turbine. The vapor leaving the turbine is wet vapor and it is condensed completely in the condenser to the state 1, by giving its latest heat to some other cooling fluid like water.

## Slide 11: Basic Cycle
The Rankine cycle is the fundamental operating cycle of all power plants where an operating fluid is continuously evaporated and condensed. The selection of operating fluid depends mainly on the available temperature range. Figure 1 shows the idealized Rankine cycle.

## Slide 12: Basic Cycle
The pressure-enthalpy (p-h) and temperature-entropy (T-s) diagrams of this cycle are given in Figure 2. The Rankine cycle operates in the following steps:
1-2-3 Isobaric Heat Transfer. High pressure liquid enters the boiler from the feed pump (1) and is heated to the saturation temperature (2). Further addition of energy causes evaporation of the liquid until it is fully converted to saturated steam (3).

## Slide 13: Basic Cycle
3-4 Isentropic Expansion. The vapor is expanded in the turbine, thus producing work which may be converted to electricity. In practice, the expansion is limited by the temperature of the cooling medium and by the erosion of the turbine blades by liquid entrainment in the vapor stream as the process moves further into the two-phase region. Exit vapor qualities should be greater than 90%.
4-5 Isobaric Heat Rejection. The vapor-liquid mixture leaving the turbine (4) is condensed at low pressure, usually in a surface condenser using cooling water. In well designed and maintained condensers, the pressure of the vapor is well below atmospheric pressure, approaching the saturation pressure of the operating fluid at the cooling water temperature.

## Slide 14: Basic Cycle
5-1 Isentropic Compression. The pressure of the condensate is raised in the feed pump. Because of the low specific volume of liquids, the pump work is relatively small and often neglected in thermodynamic calculations.
?????
Home Work --- Describe the Rankine Cycle in your own words from the beginning of the Cycle to the End with a description on how this is a continuous cycle. Use Microsoft word and insert individual Pictures for each stage of the Rankine process. And research Rankine Cycle Efficiencies (Gains or Losses) for each step of the basic process.