## Slide 1: Video Capture Workshop
Technical Issues? Contact Zach Bladow
(218) 683-8851 | zach.bladow@northlandcollege.edu

## Slide 2
Presenters
Andrew Dahlen
Northland Community & Technical College
Matthew Gardner
MATE II
Dennis Courtney
Streamworks

## Slide 3: Purpose
Assemble an easy to use video production package
Designed for demonstrations, instruction, and livestreaming events
Save time in producing video content
Reduce or eliminate post-production time
Budget smart - under $3,000
Single person provides instruction and controls multiple cameras
Notes: We don’t intend to produce perfect, professional quality videos with these tools. Our goal for this project was to assemble an equipment package for faculty and other presenters to easily produce videos. With the package assembled here, one person can produce an instructional video in a single take. Accept that there will be errors in the video – it is ok. The videos will feel more natural as if in a classroom filled with students.

## Slide 5: Equipment
All equipment showcased available at B & H Audio
Wishlist: Basic Video Package
https://www.bnh.com/wish/22c74b35c9c6afb5ebff9ae49ace5b71/

## Slide 6: General Camera Setup
Camera in standby mode with HDMI output to video switch
SD Cards not needed in cameras
Clean HDMI: Free of onscreen data typically in a camera’s viewfinder/ screen
Long battery life or power from AC source
Turn off demo mode
Disable automatic power shutdown
Notes: I have tried other cameras – Cannon 5D, Panasonic camcorder. Many cameras don’t have Clean HDMI output.

## Slide 7
Sony a5100
Mirrorless camera for $450
Popular choice for livestream and vloggers
Clean HDMI output
Power save automatic shut down disabled when using AC adapter instead of battery

## Slide 8: Sony a5100 Setup
Manual Focus Setup:
Camera Settings
Navigate to Tab 3
Change Focus Mode to Manual
Clean HDMI setup:
Press Menu Button
Select Setup
Navigate to tab 2
HDMI Settings
HDMI Info Display
Turn Off
Notes: Auto Focus will change focus automatically. Intermittent change in focus. One second focus corrections. Manual focus will eliminate this problem.

## Slide 9: Cannon VIXIA HF R800
$249
CLEAN HDMI OUTPUT
57X zoom
Solid general-purpose camcorder

## Slide 10: Cannon VIXIA HF R800 Setup
Plug-in charger
Change these settings:
  Turn off - Output onscreen display
  Turn off - Demo mode
  Turn off - Auto power off

## Slide 11: Blackmagic Design ATEM Mini Pro HDMI Live Stream Switcher
Primary Component of Video Capture System
Faster way to produce videos
Easily switch between HDMI Inputs
USB Webcam output for livestream

## Slide 12: ATEM Mini Setup Notes
Connect presenter camera to HDMI 1 for picture-in-picture
Additional options available with ATEM Control Software:
  Still photos
  Green screen
  Audio mixer

## Slide 13: ATEM Mini Control Notes
DVE – Digital Video Effects
AFV – Audio Follows Video
Up and down arrows adjust volume
FTB – Fade To Black
Still – Displays a static image
KEY – Chromakey – Green Screen – Lower Third Graphics

## Slide 14: Mini ATEM – Audio Setup and Controls
Instructional videos use Yeti Mic
Consistent audio levels
  Place mic in fixed location relative to presenter
AFV = Audio Follows Video
Turn off audio from all cameras
Notes: Note – Some Cameras may have a small delay causing audio and video to be out of sync. Control Software can adjust for this.

## Slide 15: Video Assist HDMI/6G-SDI Recorder and 5" Monitor
Record video on SD Card
Monitor video output
Audio Metering:
  Red Zone - Clipped – avoid
  Yellow Zone - Speech should always stay in the yellow
  Green Zone - Everything else

## Slide 16: Blue Yeti Sound Patterns
Single Presenter - Set to CARDIOID MODE
https://www.bluedesigns.com/products/yeti/

## Slide 17: Yeti Blue Mic
Side addressable Microphone

## Slide 18: Lighting
GVM 560AS Bi-Color LED 3-Panel Kit
Watch videos on 3-point lighting:
https://www.youtube.com/watch?v=pBt8qdO03-k
https://www.youtube.com/watch?v=j_Sov3xmgwg

## Slide 19: Cables
2x HDMI A to HDMI Mini – 15 Foot - for Cannon Camcorders
1x HDMI A to HDMI Micro for Sony Camera
2x HDMI A-A – Video Assist and Laptop
1x USB TYPE A to USB TYPE C – ATEM Mini to Laptop
3.5 mm Audio Cable – Microphone

## Slide 20: Other Gear
Glide Gear OH50 Boom Pole
2x Magnus VT-4000 Tripod
Mini Table-Top Tripod for Video Assist
16 Outlet Power Strip
Cutting Mat (24 x 36", Black) – with grid
Zip ties for cable management and strain relief

## Slide 21: Post-Production Software
Camtasia
Movie Maker
Davinci Resolve – Included with Video Assist

## Slide 22: MATE | Background
MATE Professional Development Workshops: In-person instructor-led professional development
  Google slides
  Organized materials and disseminated via CANVAS
COVID: Move the entire experience to an online delivery
  Addition of audio files embedded into Google Slides
    Online Voice Recorder
  Addition of instructional and assessment videos linked into presentations
  CANVAS: Presentations, discussions, assignments

## Slide 23: Equipment – Pre-workshop
Video production: Creation of instructional and assessment videos for asynchronous delivery
  Lighting / Tripod
  iPad
  ATEM mini
  Assessment Video Link:
  The finished backplane board
How to attach propellers to your motors instructional video.

## Slide 24: Equipment – During the Workshop
Technology & equipment used for synchronous delivery
  Zoom
    Capability to switch camera views – webcam to document camera.
    Windows camera app with Zoom screen share allows annotation on the screen share.
  Zoom white board
  Jamboard (Google add-on)
  Two computers / two Zoom accounts

## Slide 25: MATE – Streamworks Site
Professional Development and Summer STEM Camps
Supported MATE professional development workshops with asynchronous content (video) creation and synchronous (Zoom) content delivery
Delivered content and instruction synchronously during online Summer STEM Camps
Captured videos during in-person Summer Underwater Robotics Camp
Notes: Piggybacking on Matt’s presentation, at STREAMWORKS we utilized the equipment to...

## Slide 26
Notes: Equipment added to existing assets to create a production studio

## Slide 27
Questions?