## Slide 1: Class Problem 3a-1
Given V = IR and P = IV. Find an expression for P, in terms of I and R.

## Slide 2: Power

## Slide 3: Power
Define power in terms of voltage and current.
Solve problems using the power equation and Ohm’s Law.
https://www.khanacademy.org/science/ap-physics-1/ap-circuits-topic/introduction-to-dc-circuits-ap/v/electric-power

## Slide 4: Power is work performed per unit time
  Unit of work (energy) is a Joule (J)
  Is there a relationship with units that will give us power?
Component | Unit | 
V | Volts | 
I | Amperes | 
R | Ohms | Ω
Component | Unit | 
V | Volts | 
I | Amperes | 
R | Ohms | Ω

## Slide 5: Class Problem
3a-2: A toaster consumes 150 Watts of electricity. How much voltage was applied if the current is 5A?

## Slide 6
Class Problems: If a D-Cell battery (1.5V) supplies 2W of power to a small bulb, find
  3a-3: The current through the bulb
  3a-4: The resistance of the bulb
  1.5V
  R=?
  I=?

## Slide 7
Class Problems: If a D-Cell battery (1.5V) supplies 2W of power to a small bulb, find
  3a-3: The current through the bulb
  3a-4: The resistance of the bulb
Solutions
  1.5V
  R=?
  I=?

## Slide 8: Alternate forms of the power equation
  Can you write the power equation to have R instead of V?
  Substitute Ohm’s Law in for in the Power equation.
  Likewise, we can eliminate from the power equation.

## Slide 9: Equation Summary
Ohm’s Law
Power
Tip: If you know any two of V, I, R, or P, then you can find the other two.
Component | Symbol | Unit | 
Voltage | V | Volts | 
Current | I | Amperes | 
Resistance | R | Ohms | Ω
Power | P | Watts | 
Component | Symbol | Unit | 
Voltage | V | Volts | 
Current | I | Amperes | 
Resistance | R | Ohms | Ω
Power | P | Watts | 

## Slide 10: Class Problems: Solving Circuits
  1.5V
  R=470Ω
3a-6. Find I and P
  V
  R
3a-7. Find V and R given that I = 3A and P = 18W.

## Slide 11: Solving for Voltage (E), Current(I), Resistance & Power

## Slide 12: Power Summary
Power is defined as work per unit time (Joules/second = Watts)
Power in a circuit element (e.g. a load) = Current x Voltage” P = IV
If you know any two of V, I, R, or P, you can find the other two using P = IV and V = IR.