## Slide 1: Computer Numerical Controls
CNC Machining with Fusion 360

## Slide 2: Topics CONVERTING CAD TO CAM 03 MILLING OR ROUTING 01 FEEDS AND SPEEDS AND TOOLING 02 CAM TO MACHINE 04 PROJECT EXAMPLES 05
Job setups & toolpaths.
Learning the Difference Between a Mill and a Router
Choosing the correct tool, feed and speed for the job.
Post-processors & controller software, workholding for the CNC, basic CNC safety
Mills and Routers

## Slide 3: ROUTERS & MILLS

## Slide 4: CNC
Computer Numerical Control is the automated control of machining tools (such as drills, lathes, mills and 3D printers) by means of a computer. A CNC machine processes a piece of material (metal, plastic, wood, ceramic, or composite) to meet specifications by following a coded programmed instruction and without a manual operator directly controlling the machining operation.

## Slide 5: Router
A computer numerical control (CNC) router is a computer-controlled cutting machine which typically mounts a hand-held router as a spindle which is used for cutting various materials, such as wood, composites, aluminium, steel, plastics, glass, and foams.

## Slide 6: Mill
Milling is the process of machining using rotary cutters to remove material by advancing a cutter into a workpiece.

## Slide 7: ROUTER VS MILL MILL ROUTER
Softer Materials: Wood, Non-Ferrous Metals, Composites, Plastics.
Larger Work Envelope (Wide, Flat, Sheets)
2D or 2.5D Geometry
High Speed, Low Torque
Less Rigidity
Lower Precision
Harder Materials: Steels, Titanium, and more.
Smaller work envelope
High torque, lower speeds
Stronger workholding
3D Geometry Possible
Horizontal & Vertical Orientations
High Rigidity
High Precision

## Slide 8: ANATOMY

## Slide 9: TOOLS, FEEDS, SPEEDS

## Slide 10: TOOLS END MILLS V-BITS BALL NOSE
Best choice for engraving signs.
Used for slots, pockets and contours.
Geometry is optimized for material and operation.
Used for 3D and 2.5D shapes

## Slide 11: ROUTER VS MILL HSS CARBIDE
Pros:
Harder
Higher SFM possible
Longer tool life
Cons:
Brittle
Expensive
Pros:
Cheap
Sharpenable
Bendable (more forgiving)
Cons:
Dulls Easier
Slower speeds

## Slide 12: TOOLING ANATOMY
https://www.destinytool.com/uploads/2/4/9/5/24954651/7102531_orig.png

## Slide 13: TOOLING ANATOMY
Stickout is the distance from the tip of the tool to where the tool shank goes into the tool holder.
More stickout can mean more clearance
More stickout means more deflection.
Deflection can break bits, lower tool life.
Deflection means imprecise parts.
ROT:
7-8x diameter on carbide
3-4x diameter with HSS tools

## Slide 14: TERMS Surface Feet Per Minute: Constant Based on Material FEEDRATE Inches Per Minute: Dependent on Finish, Tool Material, Tool Life Revolutions Per Minute: Dependent on SPM & Tool Diameter SPM RPM

## Slide 15: GWIZARD
Choose your material.
Choose your cutting tool geometry.
Choose your cut depth & width
Choose an aggressive or conservative cut, depending on needs.
Copy over RPM, FEED RATE & PLUNGE RATE.

## Slide 16: TOOLING ANATOMY
Never buy geometry you can’t confirm.

## Slide 17: CAD TO CAM

## Slide 18: CAD - Computer Aided Design
CAD - Software used to aid the creation, modification, analysis and optimization of an object’s design.
Can develop projects in 2D or 3D space, as needed.

## Slide 19: CAD - Computer Aided Design
Parametric Modeling - incorporates the relationship between geometries. Tries to capture the “design intent”.
Direct Modeling - Models without needing to modify the original sketch.

## Slide 20: Common CAD Software & Packages
Common programs:
OpenSCAD - Uses a programming language to develop objects
OnSHAPE (web based/free)
Fusion360 (free hobbyist version, limited CAM capacities)
SolidWorks

## Slide 21: CAD to CAM
Computer Aided Manufacturing - the use of software and machinery that aids in the manufacturing process.
Terms for the CNC Router:
Toolpaths - The line of travel for tool head
Water-tight - All polygons/geometries have no gaps in the loop

## Slide 22: CAD to CAM
Process:
Set Up the Job
Determine/Generate the Toolpaths
Check the Order of Operations

## Slide 23: Set Up
Stock - the large block of material the workpiece is carved out of
Workpiece - the actual part or object
Workholding - catch-all term for the variety of techniques used to secure the stock to the machine

## Slide 24: TOOLPATHS
Toolpath: Path of travel of the tool (end mill, chamfer bit, etc.)
Inside: Tool travels on the inside of the cut line (interior lines)
Outside: Tool travels on the outside of the cut line (exterior lines)
On the Line: Tool splits the line (inlays, engraving, etc)

## Slide 25: TOOLPATHS, CONT.
Facing: Operation to remove material from the end and/or shoulder of a workpiece. Often used to get square and dimensioned stock.
Roughing Pass: Toolpaths optimized to remove material quickly, leaving a “rough” finish in the work.
Finishing Pass: Toolpaths optimized to remove less material, usually more slowly, leaving a smoother surface on the work.

## Slide 26: CONVENTIONAL VS. CLIMB CONVENTIONAL CLIMB
Cutting motion of the tool is in the same direction as the feeding direction of the work.
Less wear
Less power needed
Better finish
Can be dangerous in certain conditions
Mostly used in CNC
Cutting motion rotates against the direction of the feed
More wear
More power necessary for similar cut
Poor finish
Less dangerous in manual milling operations

## Slide 27: TOOLPATHS, CONT.
Climb Milling
Conventional Milling

## Slide 28: Pocket Contour/Slot Engrave TOOLPATHS Adaptive (Fusion 360)
Toolpath will travel along a set line in workpiece geometry
Software generates a toolpath that clears material from a closed (water-tight) 2D geometry
Generates a toolpath that carves a profile (V or U shape example)
Toolpath that maximizes material clearing with the least amount of time, tool wear, etc.
Does not produce a final finish.

## Slide 29: CAM TO MACHINE

## Slide 30: PROCESS POST - PROCESSOR CAM CONTROL SOFTWARE
Software that turns CAM toolpaths into g-code for the control software
Text file ANY CNC software/controller combo can read.
The breakout board, contactors, motor drivers and sometimes even the variable frequency drive for the spindle.

## Slide 31: POST-PROCESSORS
A “driver” to match specific CAM software to a specific controller
Often installed as part of the set up for a CAM software
Generates the g-code that the CNC controller reads

## Slide 32: PROCESS CONTROL SOFTWARE G-CODE CONTROLLER
Software that sends g-code into control board.
Text file ANY CNC software/controller combo can read.
Generated by post-processor
The breakout board, contactors, motor drivers and sometimes even the variable frequency drive for the spindle.

## Slide 33: G-CODE
GO - Rapid Travel
G1 - Travel while Working
F - Feed
X; Y; Z - Coordinates in Space
M4/M5 - Tool On/Off
Units matter!

## Slide 34: CONTROL SOFTWARE PROPRIETARY OPEN-SOURCE
More expensive
Work out of the box
Customizable with support
Can sacrifice approachability for compatibility
Less expensive
Setup requires more expertise
Limited compatibility
Customizable with community support
Usually sacrifices approachability for compatibility

## Slide 35: CONTROLLER Breakout Board Drivers Variable Frequency Drive
Takes the signal from the computer and sends it to the drivers & VFD.
Use relays & contactors to run stepper motors & servos at a higher voltage than computer
Transforms signal & voltage from source to voltage & signal necessary to run spindle.

## Slide 36: BASIC CNC SAFETY
Wear Personal PPE
No gloves, loose clothing, loose hair, jewelry
Utilize E-Stop whenever changing bits without an automatic tool changer
Never leave the machine unattended
Double-triple check your toolpaths
Never enter the machine envelope while it is operating
Make sure bystanders are aware of machine when running
Notes: https://www.sjsu.edu/people/samuel.obi/Tech%20149%20CNC%20Lecture.pdf

## Slide 37: WORKHOLDNG
Spoilboard - Disposable work surface mounted onto the router’s permanent table. Often MDF, often needed to be “flattened” over time using a spoilboard cutter.
Screws - large plywood, wood, MDF, etc sheets can be screwed straight into the spoilboard. Can damage cutter/machine if not placed properly.
Plastic Nails - Faster than screws, fussier to secure, safer for cutter.
Double Sided Tape & Glue Fixturing - Useful for small objects only. Often used for sheet aluminum too.
Clamps & T-Slots/Track - Expensive to install but reusable. Can damage cutter/machine if not placed properly.

## Slide 38: BASIC CNC PROCESS
Turn on machine.
Home machine.
Install tooling.
Set Z height.
Move spindle away from work zone.
Secure workpiece on CNC bed
Set XY zero.
Load GCODE in controller software
Check output for obvious mistakes (tool moving outside working limits, Z height, wrong feed or speed, etc)
Start dust collection if necessary
Begin job.
Remain with job until project is complete.
Move spindle away from work zone.
Check work for any issues.
Remove workpiece from CNC.
Remove Tooling from CNC.
Shut down CNC.
Notes: https://www.sjsu.edu/people/samuel.obi/Tech%20149%20CNC%20Lecture.pdf