## Slide 1: Costing and Pricing for Transportation; Private Transportation & Fleet Management
LOG 102, Session 3
October 8, 2012

## Slide 2: What’s new in SCM?
Natural gas trucks coming
Biggest evil for SCM: Uncertainty
  Creates redundancies (excess capacity)
  Creates too much inventory
  Creates customer dissatisfaction
Key: 1) Visibility in the SC
Upstream -- Our firm -- Downstream

## Slide 3: What’s new (2)
2) Collaboration (mutual trust required)
3) Risk management
The concept of externalities

## Slide 4: Recap on Regulation (main take-aways):
Carrier abuses prompted federal govt. regulations, starting with the Interstate Commerce Act in 1887 (and the ICC)
All modes were eventually regulated, both economically and for safety
Mid 1970’s to mid 1990’s: Deregulation
Interstate Commerce Commission sunsetted at end of 1995, duties replaced by Surface Transportation Board and numerous DOT agencies.
Now mostly safety and environmental regs.
States can regulate, but not restrict interstate trade

## Slide 5: U.S. Dept. of Transportation (DOT):
Name of current Secretary: Ray LaHood
http://www.dot.gov/
http://www.fmc.gov/
“Commissions” are usually independent agencies (not under the DOT)

## Slide 6: The Green Team Case (2-2)
Recap:
  Implications:
    Procure produce locally
    Bake bread on site
    Reduce miles the inbound products are shipped
    Collaborate with suppliers to reduce packaging and transport miles
    Re-evaluate inventory strategies (“Never stock out”)

## Slide 7: The “Who Pays the Price” Case
Is security worth the price?
Public benefit vs. costs to the industry
The government’s role vs. self-governed private sector
Supply Chain Risk Management
C-TPAT
10+2

## Slide 8: Transportation Seventh Edition Coyle, Novack, Gibson & Bardi © 2011 Cengage Learning
Chapter 4
Costing and Pricing for Transportation

## Slide 9: Introduction
Chapter purpose
  Review of transport pricing principles, practice
Prior to economic deregulation
  The term “rate” represented the carrier’s charge
    Rates published in tariffs available to all shippers
    Rates were the lawful charge
      The published rate for a given commodity movement was available to any shipper meeting conditions of the tariff
    Changing a rate required regulatory approval
    Rates largely based on carrier costs
      Rates rarely influenced by short term market conditions

## Slide 10: How to set a freight rate
Cost of service
Market based (value of service)
  Customer willing or able to pay
  Competitive situation
  Local conditions

## Slide 11: Introduction
In post-deregulation period
  Transport prices largely determined and driven by market forces
    Carrier cost still a major force but as part of the dynamic between customer demand and carrier supply conditions
  Motor and rail carriers still offer tariff rates
    These rates no longer subject to regulatory control
  However, much traffic moves under confidential contracts negotiated by carrier and shipper
    Prices charged much more reflective of prevailing market conditions and each party’s market needs

## Slide 12: Introduction
Chapter organization
  Review of basic market structure models
    Perfect competition and monopoly
    Oligopoly and monopolistic competition
    Theory of contestable markets (competition)
  Pricing principles
    Cost-of-service pricing approach (COST PLUS)
    Value-of-service pricing approach (MARKET)
  Rate systems and pricing in practice
  Pricing in transport management

## Slide 13: Market Considerations Market Structure Models
Models evolve from conventional economic price theory
  Attempt to explain pricing behavior of collection of firms faced with particular market conditions
    Number of competitors
    Degree of product differentiation
    Barriers to entry, etc.
  Models do not do well in predicting pricing behavior of an individual firm

## Slide 14: Market Considerations Market Structure Models
Principal models (EXAMPLES?)
  Perfect competition
    Many sellers with same products, market sets price
    Each seller faces a perfectly elastic demand curve
  Monopoly
    One seller, no close product substitutes or competitors
    Too little output and excessively high profits
  Oligopoly: few large sellers, substitutable products
  Monopolistic competition
    Many small sellers, some product differentiation

## Slide 15: Market Considerations Market Structure Models
Few markets either perfectly competitive or totally monopolistic (usually in between)
All transport modes encounter some degree of oligopolistic competition
  Competitor’s products are substitutable
  (i.e. there is high cross-elasticity)
  In pricing and output decisions, sellers must consider potential reactions of competitors
  (i.e. mutual interdependence)

## Slide 16: Market Considerations Market Structure Models
Theory of contestable markets
  Instead of many sellers, “threat of entry” from new competitors puts downward pressure on price
  Necessary conditions:
    No barriers to entry
    No economies of scale
    Consumers able and willing to switch
    Carriers are not able to respond to new entrants’ prices
  In some time periods, theory applies well to airline industry, other times it does not

## Slide 17: Market Considerations Market Structure Models
Relevant market areas
  No single market structure model correctly describes competitive environment of transport or even an entire single mode in transport
  Instead, the classification of any given competitive environment should be (DISCUSS ALASKA)
    Mode-specific
    Route-specific
    Commodity-specific
    Shipment size-specific

## Slide 18: Cost-of-Service Pricing
An approach to setting prices on the basis of the cost of providing the service
Principal assumptions
  Transport service output is homogeneous
  One group of customers with similar service preferences and sensitivity to price
  Customers must cover all costs
  Seller has some degree of control in setting prices and sets prices to maximize profit

## Slide 19: The Break-even cost concept
B/E in units = Fixed costs / gross margin per unit
Gross margin per unit = Revenue per unit minus variable cost per unit
    (Gross margin often called “contribution margin”)

## Slide 20: Cost-of-Service Pricing
Two variations of cost-of-service pricing
  Average (fully allocated) cost approach
    Total cost (fixed and variable) divided by total output
    Must initially make assumption on total output level
    But, total output level is dependent on prices charged
    Thus, approach suffers from cost-price circular reasoning
      Initially assumed volume may not move at calculated prices
    Problem becomes more acute if fixed and/or common costs are relatively high (e.g. railroads and pipelines)
      Approach criticized: fixed and/or common costs arbitrarily allocated to output with little relation to cost of producing units
      Results in loss of some profitable traffic due to high prices

## Slide 21: Note typos in the textbook labels
AR
MR
MC

## Slide 22: Nature of costs
1. Fixed costs
2. Variable costs (= marginal costs)
$10,000 fixed per month
Var. costs $.50/mile
5,000 miles driven
Average cost = $10,000/5,000 + $.50 = $2.50
Marginal cost = v.c. = $.50
Contribution margin = Revenue – variable cost.

## Slide 23: Cost-of-Service Pricing
  Marginal cost approach (≈ variable costs)
    Price set at marginal or variable cost of producing each unit of output
    Some practical problems
      Marginal costs can be difficult to calculate for small quantities of output
      Marginal costs may fluctuate widely as volume changes
      Problem of decreasing cost industries
        If prices set at marginal cost, then firms in such industries will not make a profit
  To overcome problems, value-of-service approach is used in conjunction with costs

## Slide 24: Elementary accounting
Difference between marginal and average:
“Marginal” is cost or revenue of one additional unit (= variable cost or revenue)
Average costs include fixed costs that need to be spread over the units produced

## Slide 25: Value-of-Service Pricing
Alternative definitions and terminology
  All consider demand conditions (as well as costs)
    Pricing according to product value
    Third-degree price discrimination (if able to) =
      Differential pricing (segregating)
Pricing according to product value
  Charging higher prices on higher value products
    Some cost-based rationale for such pricing
  Value is indicator of ability to bear prices, but other demand factors may dictate price elasticity

## Slide 27: Value-of-Service Pricing
Third-degree price discrimination
  Seller sets separate prices for separate groups of buyers of essentially same service
  Three necessary conditions
    Must be able to segment buyers into sub-markets defined by differences in price elasticity (sensitivity)
    Seller must be able to prevent transfer of sales between sub-markets (“gray market” transactions)
    Seller must possess some degree of monopoly power (i.e. ability to set prices)

## Slide 28: Value-of-Service Pricing
Differential pricing
  Similar definition as third degree price discrimination
  Same three conditions apply
  Means of segmenting buyers
    By commodity
    By time
    By place
    By individual person
      Legal limitations

## Slide 30: Value-of-Service Pricing
Summary
  Variable (marginal) cost sets floor for prices
  Value-of-service sets ceiling on prices
  Useful if high % of costs are fixed or common
  Enables carrying of traffic that might be lost if average cost-based prices are charged
    Some prices < average costs can be profitable
  Keys to successful value-of-service pricing
    Knowing how costs behave
    Developing good estimates of price elasticity

## Slide 32: Rate Making in Practice General Rates
Some initial terminology
  Rates and tariffs
    Individual tariffs
  Rate bureaus and bureau tariffs
General rates
  Class, exception, and commodity rates
  Each designed to simplify the potential complexity of trillions of possible rates

## Slide 33: Rate Making in Practice General Rates
Class rate system
  Provides rate for any commodity between any two geographic locations
  Simplification procedure
    Geographic: locations in proximity are grouped and represented by a rate basis point. Each pair of points assigned a rate basis number
    Commodity: products with similar transport characteristics assigned a commodity classification number and class rating
    Rate structure: national scale of rates, cwt-based

## Slide 37: Rate Making in Practice General Rates
Commodity classification factors
18 classes (from 50 to 500)
Product characteristics impacting carrier costs:
    Product density
      Higher densities mean lower carrier costs per cwt
    Stowability
    Handling
    Liability
      Considers product value and susceptibility to damage
  Individual carriers may establish commodity exceptions

## Slide 39: National Motor Freight Classification (NMFC)
http://www.nmfta.org/Pages/welcome.aspx
Low-value and/or dense freight will get lower class ratings (50-100)
Expensive, light, fluffy freight will get higher class ratings (200-500)
Shipment weight counts as well

## Slide 40: Rate Making in Practice General Rates
Determining a class rate, step-by-step:
  Determine rate basis points for origin/destination
  Determine rate basis number (rate basis number tariff)
  Determine commodity classification rating (50-500)
  Determine rate from class rate tariff
  Multiply class rate by shipment weight in cwt

## Slide 43: Examples and useful resources:
BNSF’s website:
http://www.bnsf.com/customers/prices-and-tools/
Schneider’s website:
http://www.schneider.com/index.htm
ABF Freight System’s site:
http://www.abfs.com/resource/guide/

## Slide 44: Rate Making in Practice General Rates
Exception rates
  Individual carrier modifies national classification
  Used for particular transport conditions
    Examples: large volume movements, intense competition
Commodity rates: variety of basis for
  Most common: specific rate on a commodity between specified points via specific route and direction
    Typically offered for regular, large volume moves
  Not part of commodity classification system
  Takes precedence over class and exception rates

## Slide 46: Rate Making in Practice Rate Systems Under Deregulation
General rate structures were principal basis of rates published by rate bureaus pre-1980
Post-deregulation era
  Diminished role of rate bureaus in rate matters
  Increased number of individual carrier tariffs
  Expanded use of shipper-carrier negotiations
  Portions of general rate systems still used in LTL
    Commodity classification useful simplification
    Class rates serve as benchmark for new types of rates

## Slide 47: Rate Making in Practice Rate Systems Under Deregulation
Some new rate type examples
  Zip code based rates published as part of carrier specific class and commodity rate structures
    Many carriers offer web-based zip-code tariffs as variations of class rate system
  Mileage-based rates
    Variation of commodity tariff system
    Rates quoted per mile, regardless of weight

## Slide 48: Special Rates
Rate forms that evolved due to special cost features or to induce certain shipment patterns
Character-of-shipment rates
  LTL/TL rates
  Multiple-car rates
  Incentive rates
  Unit-train rates
  Per-car and per-truckload rates
  Any-quantity rates (“AQ”)
  Density rates

## Slide 49: Special Rates Area, Location, or Route Rates
Local rates (same carrier)
Joint rates (through rates)
Proportional rates (to compete w/direct)
Differential rates (ground vs. expedited, etc)
Per-mile rates
Terminal-to-terminal rates
Blanket or group rates (averaging regions)

## Slide 50: Special Rates Time/Service Rate Structures
Contract rates
  Contract services common in rail, trucking, water, and some air transport
  Rates, services negotiated by shipper, carrier
    Rates not governed by published tariffs
    Objectives of the negotiations
      Identify service and cost factors critical to each party
      Set rate inducements and penalties based on performance on those factors
  Contracts allow for tailoring services to particular needs of the shipper and carrier

## Slide 51: Special Rates Time/Service Rate Structures
  Examples of optional features
    Volume-based: reduced rates in exchange for volume commitment over specified period
    Equipment-based: variations in rate depending upon type of car supplied (car-supply charge)
    Transit-time based: variations in rates by transit-time
    Variety of services-based: menu of logistics services
Deferred delivery
  Lower rate for flexibility in delivery time
  Common in air transport
  Enables higher vehicle utilization

## Slide 52: Special Rates Other Rate Structures
For particular cost or service purpose
  Corporate volume rates, discounts
  Loading allowances
  Aggregate tender rates (lumped shipments)
  FAK rates
  Released rates (limited value per pound)
  Empty haul rates, two-way or three-way rates
  Spot-market rates
  Menu pricing (various added services)

## Slide 53: Pricing in Transportation Management Factors Affecting Pricing Decisions
Role of the market (customers)
  Relative power of customers vs. carrier
  Price elasticity (sensitivity)
  Availability of substitutes
Governmental controls
  Surface Transportation Board: economic regulation
  Justice Department: antitrust enforcement

## Slide 54: Pricing in Transportation Management Factors Affecting Pricing Decisions
Involvement of other channel members
  Carriers involved in interline movements
    Revenue split issues
    Price change interdependency
Influence of competitors’ pricing
  Price leader influences

## Slide 55: Pricing in Transport Management Major Pricing Decisions (strategic)
Setting prices on new service
  Often little info on price elasticity or actual costs
  Too high a price attracts competitors or not enough traffic
Modification of prices over time
  Response to market, service, or operating change
  Timing of change can be important
Initiating/responding to price leader changes

## Slide 56: Pricing in Transport Management Establishing the Pricing Objective
General considerations
  Should reflect corporate objectives
  May vary during product/service life-cycle
  May vary by market
Alternative objectives
  Survival-based pricing
    Increase cash flow through low prices that attract volume
  Profit maximization
    Attractive to carriers focused on returns on investment

## Slide 57: Pricing in Transport Management Establishing the Pricing Objective
Alternative objectives (cont.)
  Unit volume pricing
    Set prices to maximize utilization of existing capacity
      Examples: multiple pickup allowances (LTL), space available prices (air freight, multiple-car prices (rail))
  Skimming
    High price designed to attract traffic focused on service quality, uniqueness and insensitive to price
  Penetration pricing
      Often follows skimming

## Slide 58: Pricing in Transport Management Establishing the Pricing Objective
Alternative objectives (cont.)
  Sales-based pricing
    Lower price to attract mass market and higher sales
    Used in later stages of life cycle
  Market share pricing
    Lowering price to gain market share from competitors
    Attractive in stagnant or declining industries
  Social responsibility pricing (charitable)

## Slide 59: Pricing in Transport Management Estimating Demand and Costs
Estimating demand
  Important, but difficult, especially for new service
  For price changes, price elasticity estimates used to predict impact
    Similar market comparisons used (cautions)
  Role of surveys and market tests
Estimating costs
  Determination of what costs to include
  Cost variation at different levels of output

## Slide 60: Pricing in Transport Management Price Levels and Price Adjustments
Given demand and cost estimates, actual price can be set
Alternative methods of setting actual price
  Demand-based
  Cost-based
  Profit-based
  Competition-based

## Slide 61: Pricing in Transport Management Price Levels and Price Adjustments
Discounts and allowances (price adjustment)
  reduction from published price in exchange for buyer doing something beneficial to supplier
  Examples
    Lower prices for larger shipments (TL vs. LTL)
    Lower prices on low-demand seasons
    Cash discounts for quicker payment of bills
  Federal regulation of discounts
    Discount must result from carrier cost savings due to action of shipper
    Size of discount should not exceed cost savings

## Slide 62: Pricing in Transport Management Most Common Mistakes in Pricing
Over-reliance on cost-based pricing
Slow reaction to changes in market conditions
Ignoring marketing mix (The 4 “P”s)
Prices not tailored to services and markets
Failure to price consistently with strategic plan

## Slide 63: Spot Market Rates; Time Charter Rates; Bareboat Rates
Spot market: Today’s rate for available capacity or tonnage
Time charter: A daily rate for the entire vessel or vehicle
Bareboat: A leasing rate for the vessel or vehicle, without crew, fuel and operating costs

## Slide 64: Example: The Baltic Dry Index
http://www.cnbc.com/id/15840232?play=1&video=1544409005

## Slide 65: Hints for the Hardee Transportation case, due next wk.
Definitely study appendices 4A and 4B first
The equipment purchase price, incl. deprecation and interest, is a fixed cost
Calculate cost per haul (fuel, labor costs for drivers and dock workers, insurance, maintenance, billing, admin., dock facility), taking constraints (available hours, average speed)
Easiest to set it up using a spreadsheet
Answer the 4 questions at the bottom

## Slide 66: Transportation Seventh Edition Coyle, Novack, Gibson & Bardi © 2011 Cengage Learning
Chapter 13
Private Transportation and Fleet Management

## Slide 67: Introduction
Chapter focus
  Use of private transport in each mode
  Factors in decision to enter private transport
  Operation of a private truck fleet
Definition of private transport:
    “…. the movement of goods owned by a firm that also owns or leases and operates the transportation equipment for the furtherance of its primary business.”
Does not provide for-hire service to the general public except in rare circumstances

## Slide 68: Private Rail Transport
Takes the form of:
  Privately owned specialized rail cars moved by for-hire rail carrier
    RR grants an allowance (reduction) from normal rate
    Most prevalent among agri-businesses
      Ensures adequate supply of cars during peak seasons
  Privately owned rail sidings connecting shipper facilities with for-hire carrier’s track network
    Some large manufacturers also own small private RRs to move railcars exclusively within their manufacturing plants

## Slide 69: Private Air Transport
Used largely to transport people
  Helps save travel time for upper management
  Helps gain faster access to smaller, remote locations with minimum commercial service
  Significantly higher cost than commercial service flights
Occasionally used for emergency freight shipments
  Documents, emergency repair parts

## Slide 70: Private Water Transport
Used for movement of bulk, low-value products in large volumes on regular schedules
  Companies in mining, steel, petroleum and agriculture industries frequently have private fleets
    Shipments move between mines, grain silos, and ports to steel mills, electric power plants, refineries, and processing mills
  Large investment required to utilize private fleet
    Vessels and dock facilities
    Requires large volume, regular shipments to justify cost

## Slide 71: Examples: Dole, Boeing
http://www.doleoceancargo.com/

## Slide 72: Private Oil Pipeline Transport
Few, if any, oil pipelines operate as private transport carriers
Many pipelines owned by large oil companies
  Most of these lines required to operate as for-hire common carriers
    Must provide access at reasonable rates for other oil companies as well as the owning oil company
    As such, these lines do not operate as private pipelines
  Large capital investment requires regular, large volume shipments to justify start-up cost

## Slide 73: Private Trucking
Most pervasive form of transport in U.S.
  Generates over $300B in revenue, ½ of revenue generated by trucking in the U.S.
  50% of domestic tons shipped are moved by private trucking
  Contributes to 2.5% of gross domestic product
Estimated 4 million private truck fleets in U.S.

## Slide 74: Why Private Trucking?
Driving motivation: to enhance marketability and profitability of firm’s products
Private fleet can:
  Improve levels of service (e.g. lower transit times) that differentiate the firm’s products
  Lower costs that in turn maintain or lower prices and increase profits

## Slide 76: Why Private Trucking? Improved Service
Potential for improved service emanates from having greater control over operations
  Dispatching, routing, and delivery schedules can be customized/fine tuned to customer needs
  Drivers, as employees of seller, have a more direct vested interest in satisfying customer
    Private fleet drivers have much higher retention rates
Greater control used by sellers to:
  Lower delivery times, inventories and stockouts
  Provide more flexibility in meeting customer needs

## Slide 77: Why Private Trucking? Improved Service
Some disadvantages of private trucking
  Ties up capital, creating an opportunity cost
    Leasing is an option that reduces this problem
  Seller bears risk of in-transit loss and damage
    Cargo insurance can be purchased to reduce this risk
  Risk of public liability due to vehicle accidents
    Again, insurance can be used to manage this risk
  Administrative and maintenance responsibilities are higher compared with using for-hire carriers

## Slide 78: Private Trucking Cost Analysis Fixed Costs
Principal fixed costs are:
  Depreciation (lease payments)
  Interest on investments
  Management wages
  Office and maintenance garage
Fixed costs amount to about 27 cents per mile for long distance carriers
  But, as the fleet is utilized, the fixed costs per mile drop dramatically

## Slide 81: Why Private Trucking? Operating Costs
Estimated operating expense per mile: $1.73
Labor and fuel/oil are two largest categories
  Together account for approx. 70% of total operating expenses/mile
    Fuel expenses highly volatile in recent years
  Labor includes driver wages, benefits, bonuses
Other principal expense categories
  Maintenance, repair, and tire costs
  Insurance, licensing and vehicle registration

## Slide 82: Major Operating Decisions
Equipment-related decisions:
  Choosing the type of equipment to use
  Choosing to buy or lease equipment
Fleet operations and control:
  Organization
  Regulation
  Driver utilization
  Controlling empty backhauls
  Management control mechanisms

## Slide 83: Major Operating Decisions Equipment-Related Decisions
Equipment types vary in terms of:
  Carrying capacity (cube and weight)
  Fuel: gasoline vs. diesel powered vs. natural gas
  Engine and drive train
  Whether cargo unit separates from power unit
  Special needs, such as refrigeration
  Each of the above impacts
    Capital and operating costs for equipment
    Ability to meet transport requirements

## Slide 84: Major Operating Decisions Equipment-Related Decisions
Equipment selection factors
  Typical shipment size and product density
  Typical length of haul
    Influences what type of fuel is most economical
  Location of operations
    City vs. intercity: influences gasoline vs. diesel choice and straight truck vs. tractor-trailer combination choice
    Mountainous vs. flat terrain: Influences engine power and drive train choices
  Special needs – refrigeration, lift gates

## Slide 86: Major Operating Decisions Equipment-Related Decisions
Leasing vs. Buying Equipment
  Leasing reduces capital requirements
  Types of lease arrangements
    Full service lease
      Includes vehicle, variety of operating support services
      Support services may include some or all operating expense categories except driver labor expenses
      Fee includes fixed charge per month plus mileage fee
    Finance lease: includes vehicle only
      Lessee responsible for procuring/providing support services
      Fee covers equipment capital cost, lessor’s finance charge, profit

## Slide 87: Major Operating Decisions Equipment-Related Decisions
  Advantages of leasing
    Frees working capital for other business uses
    Full service lease reduces much of the risk and administrative responsibility of private fleet operation
      Fixed lease fee provides certainty on operating costs
      Full service is a cost-effective approach to use for a trial period
    Full service lease also offers potential benefit from lessor’s volume purchases of fuel, equipment, and parts
  Disadvantages of leasing
    Long run total cost may be higher than buying
  Net present value assessment should guide decision

## Slide 88: Major Operating Decisions Fleet and Operation Control
Managing intra-organization conflicts
  Multiple goals of increasing service levels and lowering transportation costs can create conflicts
    Marketing may push the service levels
    Operations may emphasize costs
  A typical approach to manage the conflict is to pursue a cost-constrained service goal
    A budget is set and the highest level of service is sought within the budget constraint

## Slide 89: Major Operating Decisions Fleet and Operation Control
Managing user perception that private fleet operation is “free”
  One approach: create private fleet as profit center
    Internal user’s budget charged a fee for use of fleet
    Fleet is operated as though it were a separate business
      Management responsible for profitability and asset utilization
      Should solicit other shippers’ business if necessary to increase utilization, provided it has necessary operating authority
    Internal user should have option to use for-hire carriers

## Slide 90: Major Operating Decisions Fleet and Operation Control
Organizational positioning of fleet management responsibilities.
Some options:
  As a profit center reporting to CEO
  As a cost center under control of marketing, production, finance, or traffic departments
    Tends to take on bias of controlling department
  Place under control of unit making greatest use
  Centralized vs. decentralized positioning

## Slide 91: Major Operating Decisions Fleet and Operation Control
Finding means to improve fuel mileage
  Small improvements have significant impact
    Assume one vehicle travels 140,000 miles/year. If vehicle averages 5 mpg, then 28,000 gallons consumed. At $4/gal. fuel cost = $112,000
    If vehicle averages 5.5 mpg, then 25,455 gallons consumed. Fuel cost = $101,818, a 9.1% savings
  Modifying vehicle equipment, such as adding air deflectors or improving vehicle routing and scheduling are means of improving fuel economy

## Slide 92: Major Operating Decisions Fleet and Operation Control
Control over cost and performance
  Data collection
    Should be done on disaggregated basis as much as practical
    Example: Fuel consumption should be monitored at the vehicle-level and then aggregated to the fleet level
    Fleet-wide averages alone can mask too many problems due to data aggregation
    Some useful data collection units include:
      By driver
      By vehicle
      By market, traffic lane, or facility

## Slide 93: Major Operating Decisions Fleet and Operation Control
  Useful data for creating performance measures
    Miles operated (loaded and empty), vehicle hours operated
    Number of trips, tonnage hauled, number of stops made
    Driver hours, fuel consumed, maintenance hours
  Typical performance control measures
    Cost per mile, per hour and per trip
    Miles/day, deliveries/day, hours/run (trip)
      These are measures of driver productivity

## Slide 94: Major Operating Decisions
Some well known, high performing private fleet operations
  Purdue Farms
    230 tractors, 235 drivers, 750 trailers
    22 million miles/year, 99% on-time delivery
  Walgreens: private fleet operations for 100 years
  Pepsi: fourth largest private fleet in U.S.
    5,937 tractors, 2,544 straight trucks, 8,800 trailers
    Operates 24/7 and ensures capacity availability

## Slide 95: Major Operating Decisions Regulations
To be exempt from federal economic regulation, truck operation must pass primary business test
  The trucking service must be incidental to and in furtherance of firm’s primary business
  Existence of production facilities, retail outlets, and product inventories indicate primary business is not transport

## Slide 96: Major Operating Decisions Regulations
Historically, private fleets were not permitted to conduct for-hire services
  Under current regulations, private carriers may now operate on a for-hire basis
    Fleets must obtain for-hire authority and publish rates
    Helps fleets to reduce empty backhauls and contribute more to firm profitability
  Other options for reducing empty backhauls:
    Trip leasing to another firm or another private carrier
    Transporting exempt commodities

## Slide 97: Major Operating Decisions Regulations
Private trucking subject to all federal safety regulations covering:
  Driver qualifications, hours of service, driving practices, and accident reporting
  Vehicle parts and accessories, vehicle inspection and maintenance, vehicle dimensions
  Hazardous materials transportation
  Federal safety regulations enforced by Bureau of Motor Carrier Safety in U.S. DOT

## Slide 98: Major Operating Decisions Regulations
Private trucking must also adhere to safety regulations of all states in which they operate
State safety regulations cover
  Vehicle speed
  Vehicle weight, length, height and width regulations not superseded by federal limits

## Slide 99: Major Operating Decisions Regulations
Issue of driver’s hours of service regulations
  Drivers in interstate commerce permitted to drive:
    Up to 10 hours following 8 hours off duty or up to 11 hours following 10 hours off duty.
    Up to 60 hours in a seven day period or up to 70 hours in an eight day period.
  Driver daily logs must be kept current showing time of last change of duty
  Electronic logs emerging to alert drivers and improve management control