## Slide 1
ACADs (08-006) Covered
Keywords
posting, label, tag, storage, loose, fixed, 10CFR20, lower limits, dose rate, removing/releasing materials,
Description
Supporting Material
Radiation Protection Postings
3.3.5.6.2 | 3.3.8.2 | 3.3.8.3 | 3.3.9.5
3.3.9.6 | 3.3.10.2 | 3.3.14.3 | 

## Slide 2: Postings
Radiological Safety and Response
RPT-243 -3
Notes: RPT-243-3
Postings
ACAD-08-006: 3.3.8.2; 3.3.8.3; 3.3.9.5; 3.3.9.6; 3.3.10.2; 3.3.14.3
DOE: 2.10.07; 2.10.09; 2.10.12; 2.10.13; 2.11.06
Duration: 1.25 hours
Material Resources Needed: none
Equipment/Supplies: Overhead display for PowerPoint
Assessment/Evaluation: The learning outcomes should be reviewed at the beginning of the class and should be reviewed periodically and at the conclusion. Examination number 1 will provide a formal assessment of these learning outcomes.
References Used in Development:
Basic Radiation Protection Technology, 5th edition, Gollnick; ISBN 0-916339-11-4
Nuclides and Isotopes/Chart of the Nuclides, 16th edition, Baum, Knox, Miller; ASIN: B000BUNFS8
Operational Health Physics Training, Moe; ANL-88-26 (1988)
DOE Health Physics Training, DOE-HDBK-1122-99 & DOE-HDBK-1122-2009
10CFR20 & 10CFR835 – current revisions
2/14/2013
2

## Slide 3: Learning Outcomes Upon completion of this lesson, the student will be able to:
Explain the differences between general area dose rate and contact dose rate and how each is used to control exposure.
Explain the difference between loose and fixed contamination.
State the purpose of radiological postings, signs, labels, and barricades; and the RPTs responsibilities for them
Define and state the posting requirements for the controlled area, radiologically restricted area, radiation area, high radiation area, locked high radiation area, very high radiation area, and hot spots.

## Slide 4
Describe the procedures for posting airborne radioactivity areas (10CFR20).
Describe the approval and posting requirements for radioactive material areas and radioactive material storage areas.
Discuss the reason for having lower limits for alpha contamination.
Describe good practices, support equipment to use, and common discrepancies in setting up radiological areas.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 5
List the requirements individuals should follow while working in RBAs.
State the requirements for removing or releasing materials from any radiological area.
Describe exposure control techniques that can be used to control worker and technician radiation exposures.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 6: Outline
Introduction
10CFR20 Basic Terms
10CFR20 Postings
10CFR835 Basic Terms
10 CFR 835 Postings
Summary
Questions

## Slide 7: Introduction

## Slide 8: Introduction
As discussed in the previous lecture, the nuclear industry is regulated through the use of either the 10CFR20 or 10CFR835 codes depending on whether it is NRC or DOE.
In this lecture, we will look at some base definitions and the posting requirements used in the industry established by these regulations.
Good practices and techniques for control of radioactive material will be examined.

## Slide 9: Introduction
Finally, we will further explore exposure control techniques.

## Slide 10: Posting, Labeling, Tagging
At their fundamental level, posting, labeling, and tagging are all communication devices.
They communicate the presence of a hazard to the workers and general population.
RPTs are the “guardians” of the communication tool. They:
  monitor for the presence of the hazard,
  determine the proper communication device(s)
  install the devices in such a way as to alert personnel prior to the hazard being encountered.

## Slide 11: Posting, Labeling, Tagging
RPTs also monitor the adequacy of the existing posting by comparing the radiological conditions in an area and verifying the posting is adequate.
As the experts in this area, the RPTs also are responsible for ensuring the posting, labeling, and tagging are installed in a way that ensures it fulfills its function without failure. For example:
  Boundary rope must not fall under normal use
  Signs, labels and tags are in good repair and legible
  Techniques will be addressed later

## Slide 12: 10CFR20 Basic Terms - Posting

## Slide 13: Basic Terms
Licensed material means source material, special nuclear material, or byproduct material received, possessed, used, transferred or disposed of under a general or specific license issued by the Commission.
Radiation (ionizing radiation) means alpha particles, beta particles, gamma rays, x-rays, neutrons, high-speed electrons, high-speed protons, and other particles capable of producing ions. Radiation, as used in this part, does not include non-ionizing radiation, such as radio- or microwaves, or visible, infrared, or ultraviolet light.

## Slide 14: Basic Terms
Restricted area means an area, access to which is limited by the licensee for the purpose of protecting individuals against undue risks from exposure to radiation and radioactive materials. Restricted area does not include areas used as residential quarters, but separate rooms in a residential building may be set apart as a restricted area.
Unrestricted area means an area, access to which is neither limited nor controlled by the license

## Slide 15: Basic Terms
Entrance or access point means any location through which an individual could gain access to radiation areas or to radioactive materials. This includes entry or exit portals of sufficient size to permit human entry, irrespective of their intended use.
Radiation area means an area, accessible to individuals, in which radiation levels could result in an individual receiving a dose equivalent in excess of 0.005 rem (0.05 mSv) in 1 hour at 30 centimeters from the radiation source or from any surface that the radiation penetrates

## Slide 16: Basic Terms
High radiation area means an area, accessible to individuals, in which radiation levels from radiation sources external to the body could result in an individual receiving a dose equivalent in excess of 0.1 rem (1 mSv) in 1 hour at 30 centimeters from the radiation source or 30 centimeters from any surface that the radiation penetrates.

## Slide 17: Basic Terms
Very high radiation area means an area, accessible to individuals, in which radiation levels from radiation sources external to the body could result in an individual receiving an absorbed dose in excess of 500 rads (5 grays) in 1 hour at 1 meter from a radiation source or 1 meter from any surface that the radiation penetrates.
(Note: At very high doses received at high dose rates, units of absorbed dose (e.g., rads and grays) are appropriate, rather than units of dose equivalent (e.g., rems and sieverts)).

## Slide 18: Basic Terms
Contact dose rates – dose rates taken with a portable radiation survey instrument with the probe centered (where feasible) and in contact with the article containing the radioactive material causing the reading.
General area dose rates – generally speaking, dose rates taken at waist level in an area. If the source of radiation is know to be above the head then the dose rate would be taken at head level. If the source is from an identified contact reading, then the general area dose rate is at 30 cm from the surface.

## Slide 19: Basic Terms
Airborne radioactivity area means a room, enclosure, or area in which airborne radioactive materials, composed wholly or partly of licensed material, exist in concentrations –
  In excess of the derived air concentrations (DACs) specified in appendix B, to §§ 20.1001-20.2401, or
  To such a degree that an individual present in the area without respiratory protective equipment could exceed, during the hours an individual is present in a week, an intake of 0.6 percent of the annual limit on intake (ALI) or 12 DAC-hours.

## Slide 20: Subpart J—Precautionary Procedures

## Slide 21: 10CR20.1901 Caution Signs
Standard radiation symbol. Unless otherwise authorized by the Commission, the symbol prescribed by this part shall use the colors magenta, or purple, or black on yellow background. The symbol prescribed by this part is the three-bladed design:

## Slide 22: 10CR20.1901 Caution Signs
Exception to color requirements for standard radiation symbol. licensees are authorized to label sources, source holders, or device components containing sources of licensed materials that are subjected to high temperatures, with conspicuously etched or stamped radiation caution symbols and without a color requirement.

## Slide 23: 10CFR20.1902 Posting Requirements
The licensee shall post each radiation area with a conspicuous sign or signs bearing the radiation symbol and the words
CAUTION
RADIATION AREA

## Slide 24: 10CFR20.1902 Posting Requirements
The licensee shall post each high radiation area with a conspicuous sign or signs bearing the radiation symbol and the words
CAUTION or DANGER
HIGH RADIATION AREA

## Slide 25: 10CFR20.1902 Posting Requirements
The licensee shall post each very high radiation area with a conspicuous sign or signs bearing the radiation symbol and words
GRAVE DANGER
VERY HIGH RADIATION AREA

## Slide 26: 10CFR20.1902 Posting Requirements
The licensee shall post each airborne radioactivity area with a conspicuous sign or signs bearing the radiation symbol and the words
CAUTION or DANGER
AIRBORNE RADIOACTIVITY AREA

## Slide 27: 10CFR20.1902 Posting Requirements
The licensee shall post each area or room in which there is used or stored an amount of licensed material exceeding 10 times the quantity of such material specified in appendix C to part 20 with a conspicuous sign or signs bearing the radiation symbol and the words
CAUTION or DANGER
RADIOACTIVE MATERIAL(S)

## Slide 28: RAM Area Approval
The establishment of radioactive material (RAM) areas must be approved by station radiation protection management (specified in facility procedures).
This is necessary to ensure that radioactive materials are properly controlled and that the hazard is clearly communicated in keeping with the requirements of the regulations.
Typically, the radiation protection organization will maintain a list of approved RAM areas.

## Slide 29: 10CFR20.1903 Exceptions to Posting Requirements
A licensee is not required to post caution signs in areas or rooms containing radioactive materials for periods of less than 8 hours, if each of the following conditions is met:
  The materials are constantly attended during these periods by an individual who takes the precautions necessary to prevent the exposure of individuals to radiation or radioactive materials in excess of the limits established in this part; and
  The area or room is subject to the licensee's control.

## Slide 30: 10CFR20.1903 Exceptions to Posting Requirements
Rooms or other areas in hospitals that are occupied by patients are not required to be posted with caution signs pursuant to § 20.1902 provided that the patient could be released from licensee control pursuant to § 35.75 of this chapter.
A room or area is not required to be posted with a caution sign because of the presence of a sealed source provided the radiation level at 30 centimeters from the surface of the source container or housing does not exceed 0.005 rem (0.05 mSv) per hour.

## Slide 31: 10CFR20.1903 Exceptions to Posting Requirements
Rooms in hospitals or clinics that are used for teletherapy are exempt from the requirement to post caution signs under § 20.1902 if—
  Access to the room is controlled pursuant to 10 CFR 35.615; and
  Personnel in attendance take necessary precautions to prevent the inadvertent exposure of workers, other patients, and members of the public to radiation in excess of the limits established in this part.

## Slide 32: 10CFR20.1904 Labeling Containers
The licensee shall ensure that each container of licensed material bears a durable, clearly visible label bearing the radiation symbol and the words:
CAUTION or DANGER
RADIOACTIVE MATERIAL(S)

## Slide 33: 10CFR20.1904 Labeling Containers
The label must also provide sufficient information such as:
  the radionuclide(s) present,
  an estimate of the quantity of radioactivity,
  the date for which the activity is estimated, radiation levels,
  kinds of materials, and
  mass enrichment
to permit individuals handling or using the containers, or working in the vicinity of the containers, to take precautions to avoid or minimize exposures.

## Slide 34: 10CFR20.1904 Labeling Containers
Each licensee shall, prior to removal or disposal of empty uncontaminated containers to unrestricted areas, remove or deface the radioactive material label or otherwise clearly indicate that the container no longer contains radioactive materials.

## Slide 35: 10CFR20.1905 Exemptions to Labeling Requirements
A licensee is not required to label containers –
  holding licensed material in quantities less than the quantities listed in appendix C to part 20; or
  holding licensed material in concentrations less than those specified in table 3 of appendix B to part 20; or
  attended by an individual who takes the precautions necessary to prevent the exposure of individuals in excess of the limits established by this part; or

## Slide 36: 10CFR20.1905 Exemptions to Labeling Requirements
A licensee is not required to label containers –
  when they are in transport and packaged and labeled in accordance with the regulations of the Department of Transportation, or
  that are accessible only to individuals authorized to handle or use them, or to work in the vicinity of the containers, if the contents are identified to these individuals by a readily available written record. The record must be retained as long as the containers are in use for the purpose indicated on the record; or
Notes: (examples of containers of this type are containers in locations such as water-filled canals, storage vaults, or hot cells).

## Slide 37: 10CFR20.1905 Exemptions to Labeling Requirements
A licensee is not required to label containers –
  installed manufacturing or process equipment, such as reactor components, piping, and tanks; or
  holding licensed material (other than sealed sources that are either specifically or generally licensed) at a facility licensed under Parts 50 or 52 of this chapter, not including non-power reactors, that are within an area posted under the requirements in § 20.1902 if the containers are:
Notes: (examples of containers of this type are containers in locations such as water-filled canals, storage vaults, or hot cells).

## Slide 38: 10CFR20.1905 Exemptions to Labeling Requirements
      Conspicuously marked (such as by providing a system of color coding of containers) commensurate with the radiological hazard; and
      Accessible only to individuals who have sufficient instruction to minimize radiation exposure while handling or working in the vicinity of the containers; and
      Subject to plant procedures to ensure they are appropriately labeled, as specified at § 20.1904 before being removed from the posted area.
Notes: (examples of containers of this type are containers in locations such as water-filled canals, storage vaults, or hot cells).

## Slide 39: 10CFR835 Basic Terms - Posting
Subpart G – Posting and Labeling
Notes: http://ecfr.gpoaccess.gov/cgi/t/text/text-idx?c=ecfr&tpl=/ecfrbrowse/Title10/10cfr835_main_02.tpl

## Slide 40: Basic Terms
Radiological area means any area within a controlled area defined in this section as a “radiation area,” “high radiation area,” “very high radiation area,” “contamination area,” “high contamination area,” or “airborne radioactivity area.”
Radiation means ionizing radiation: alpha particles, beta particles, gamma rays, X-rays, neutrons, high-speed electrons, high-speed protons, and other particles capable of producing ions. Radiation, as used in this part, does not include non-ionizing radiation, such as radio waves or microwaves, or visible, infrared, or ultraviolet light.

## Slide 41: Basic Terms
Controlled area means any area to which access is managed by or for DOE to protect individuals from exposure to radiation and/or radioactive material.

## Slide 42: Basic Terms
Entrance or access point means any location through which an individual could gain access to areas controlled for the purpose of radiation protection. This includes entry or exit portals of sufficient size to permit human entry, irrespective of their intended use.
Radiation area means any area, accessible to individuals, in which radiation levels could result in an individual receiving an equivalent dose to the whole body in excess of 0.005 rem (0.05 mSv) in 1 hour at 30 centimeters from the source or from any surface that the radiation penetrates.

## Slide 43: Basic Terms
High radiation area means any area, accessible to individuals, in which radiation levels could result in an individual receiving an equivalent dose to the whole body in excess of 0.1 rems (0.001 Sv) in 1 hour at 30 centimeters from the radiation source or from any surface that the radiation penetrates.

## Slide 44: Basic Terms
Very high radiation area means any area, accessible to individuals, in which radiation levels could result in an individual receiving an absorbed dose in excess of 500 rads (5 grays) in one hour at 1 meter from a radiation source or from any surface that the radiation penetrates.

## Slide 45: Basic Terms
Airborne radioactivity area means any area, accessible to individuals, where:
  The concentration of airborne radioactivity, above natural background, exceeds or is likely to exceed the derived air concentration (DAC) values listed in appendix A or appendix C of this part; or
  An individual present in the area without respiratory protection could receive an intake exceeding 12 DAC-hours in a week.

## Slide 46: Basic Terms
Contamination area means any area, accessible to individuals, where removable surface contamination levels exceed or are likely to exceed the removable surface contamination values specified in appendix D of this part, but do not exceed 100 times those values.
High contamination area means any area, accessible to individuals, where removable surface contamination levels exceed or are likely to exceed 100 times the removable surface contamination values specified in appendix D of this part.

## Slide 47: Basic Terms
Loose surface contamination – radioactive material existing on a surface that is easily transferred from the surface to items coming in contact with the surface under moderate pressure.
Fixed surface contamination - radioactive material existing on a surface not easily removed requiring, excessive pressure, abrasive actions (material removal), or chemical treatment to be removed from the surface.

## Slide 48: Appendix D Surface Contamination Values dpm/100 cm2
Radionuclide | Removable | Total (Fixed + Removable)
U-nat, U-235, U-238, and associated decay products | 1,000 | 5,000
Transuranics, Ra-226, Ra-228, Th-230, Th-228, Pa-231, Ac-227, I-125, I-129 | 20 | 500
Th-nat, Th-232, Sr-90, Ra-223, Ra-224, U-232, I-126, I-131, I-133 | 200 | 1,000
Beta-gamma emitters (nuclides with decay modes other than alpha emission or spontaneous fission) except Sr-90 and others noted above5 | 1,000 | 5,000
Tritium and STCs6 | 10,000 | See Footnote 6

## Slide 49: Basic Terms
Alpha versus Beta/Gamma – notice on the table the difference in the values permitted for alpha contamination versus the beta/gamma values.
Why do you suppose that is?
Due to the different ionization characteristics of alpha.
Once airborne and ingested, alpha causes significant long-term physical damage.
Highly ionizing, it is necessary to more tightly control the amount of alpha emitting isotopes permitted to accumulate prior to cleaning it up.

## Slide 50: Basic Terms
Radioactive material area means any area within a controlled area, accessible to individuals, in which items or containers of radioactive material exist and the total activity of radioactive material exceeds the applicable values provided in appendix E of this part.

## Slide 51: 10CFR-835.601 General Requirements
Except as otherwise provided in this subpart, postings and labels required by this subpart shall include the standard radiation warning trefoil in black or magenta imposed upon a yellow background.
Signs required by this subpart shall be clearly and conspicuously posted and may include radiological protection instructions.
.

## Slide 52: 10CFR-835.601 General Requirements
The posting and labeling requirements in this subpart may be modified to reflect the special considerations of DOE activities conducted at private residences or businesses.
Such modifications shall provide the same level of protection to individuals as the existing provisions in this subpart.

## Slide 53: 10CFR-835.602 Controlled Areas
Each access point to a controlled area (as defined at §835.2) shall be posted whenever radiological areas or radioactive material areas exist in the area.
Individuals who enter only controlled areas without entering radiological areas or radioactive material areas are not expected to receive a total effective dose of more than 0.1 rem (0.001 sievert) in a year.
Signs used for this purpose may be selected by the contractor to avoid conflict with local security requirements.

## Slide 54: 10CFR-835.602 Controlled Areas
Each access point to a controlled shall be posted whenever radiological areas or radioactive material areas exist in the area.
Individuals who enter only controlled areas without entering radiological areas or radioactive material areas are not expected to receive a total effective dose of more than 0.1 rem (0.001 sievert) in a year.
Signs used for this purpose may be selected by the contractor to avoid conflict with local security requirements.

## Slide 55: 10CFR835.603 Radiological Areas and Radioactive Materials Area
Each access point to radiological areas and radioactive material areas (as defined at §835.2) shall be posted with conspicuous signs bearing the wording provided in this section.

## Slide 56: 10CFR835.603 Radiological Areas and Radioactive Materials Area
The words “Caution, Radiation Area” shall be posted at each radiation area.
CAUTION
RADIATION AREA

## Slide 57: 10CFR835.603 Radiological Areas and Radioactive Materials Area
The words “Caution, High Radiation Area” or “Danger, High Radiation Area” shall be posted at each high radiation area.
CAUTION or DANGER
HIGH RADIATION AREA

## Slide 58: 10CFR835.603 Radiological Areas and Radioactive Materials Area
The words “Grave Danger, Very High Radiation Area” shall be posted at each very high radiation area.
GRAVE DANGER
VERY HIGH RADIATION AREA

## Slide 59: 10CFR835.603 Radiological Areas and Radioactive Materials Area
The words “Caution, Airborne Radioactivity Area” or “Danger, Airborne Radioactivity Area” shall be posted at each airborne radioactivity area.
CAUTION or DANGER
AIRBORNE RADIOACTIVITY AREA

## Slide 60: 10CFR835.603 Radiological Areas and Radioactive Materials Area
The words “Caution, Contamination Area” shall be posted at each contamination area.
CAUTION
CONTAMINATION AREA

## Slide 61: 10CFR835.603 Radiological Areas and Radioactive Materials Area
The words “Caution, High Contamination Area” shall be posted at each high contamination area.
CAUTION
HIGH CONTAMINATION AREA

## Slide 62: 10CFR835.603 Radiological Areas and Radioactive Materials Area
The words “Caution, Radioactive Material(s)” shall be posted at each radioactive material area.
CAUTION or DANGER
RADIOACTIVE MATERIAL(S)

## Slide 63: 10CFR835.604 Exceptions to Posting Requirements
Areas may be excepted from the posting requirements of §835.603 for periods of less than 8 continuous hours when placed under continuous observation and control of an individual knowledgeable of, and empowered to implement, required access and exposure control measures.

## Slide 64: 10CFR835.604 Exceptions to Posting Requirements
Areas may be excepted from the radioactive material area posting requirements when:
  Posted as another type of radiologically controlled area (10CFR20 doesn’t have this)
  Each item or container of radioactive material is labeled in accordance with this subpart such that individuals entering the area are made aware of the hazard; or
  The radioactive material of concern consists solely of structures or installed components which have been activated

## Slide 65: 10CFR835.604 Exceptions to Posting Requirements
Areas containing only packages received from radioactive material transportation labeled and in non-degraded condition need not be posted in accordance with §835.603 until the packages are monitored in accordance with §835.405 (receipt of RAM packages).

## Slide 66: 10CFR835.605 Labeling Items and Containers
Except as provided at §835.606, each item or container of radioactive material shall bear a durable, clearly visible label bearing the standard radiation warning trefoil and the words “Caution, Radioactive Material” or “Danger, Radioactive Material.”
The label shall also provide sufficient information to permit individuals handling, using, or working in the vicinity of the items or containers to take precautions to avoid or control exposures.

## Slide 67: 10CFR835.606 Exceptions to Labeling Requirements
Items and containers may be excepted from the radioactive material labeling requirements of §835.605 when:
  Used, handled, or stored in areas posted and controlled in accordance with this subpart and sufficient information is provided to permit individuals to take precautions to avoid or control exposures; or
  The quantity of radioactive material is less than one tenth of the values specified in appendix E of this part and less than 0.1 Ci; or

## Slide 68: 10CFR835.606 Exceptions to Labeling Requirements
Items and containers may be excepted from the radioactive material labeling requirements of §835.605 when: (cont’d)
  Packaged, labeled, and marked in accordance with the regulations of the Department of Transportation or DOE Orders governing radioactive material transportation; or
  Inaccessible, or accessible only to individuals authorized to handle or use them, or to work in the vicinity; or

## Slide 69: 10CFR835.606 Exceptions to Labeling Requirements
Items and containers may be excepted from the radioactive material labeling requirements of §835.605 when: (cont’d)
  Installed in manufacturing, process, or other equipment, such as reactor components, piping, and tanks; or
  The radioactive material consists solely of nuclear weapons or their components.
Radioactive material labels applied to sealed radioactive sources may be excepted from the color specifications of §835.601(a).

## Slide 70: Good Practices Support Equipment Common Problems

## Slide 71: In General…
Each facility and organization will establish specific techniques to be used in ensuring posting is properly installed.
The rope used is often stiff and made of nylon for durability.
However, that makes it difficult to tie secure in a manner that keeps it functional. The PE will demonstrate methods often used to address the proper securing of the rope ends.
The signs must also be secured to ensure they stay intact.

## Slide 72: In General…
Although radiological buffer areas (RBA) are not specifically address in the regulations, they are used in some applications to provide a buffer zone between controlled areas and general access areas.
Stop gap measure to ensure the public doesn’t come in contact with radioactive material.
Typically entry into the RBA will be signed in on an RWP and have proper dosimetry.

## Slide 73: In General…
Free release of equipment and material and personnel from an RBA will be the same as that for removal from a radiologically controlled area:
  No detectable loose surface or fixed contamination
  No measurable radiation beta-gamma or alpha.
If it has inaccessible areas that can not be surveyed, then it can not be released.

## Slide 74
Summary
  Dose limits and posting requirements of 10 CFR 20 and 10 CFR 835 are very similar.
  10CFR20 does not specify contamination area postings
  You should now be able to apply dose limits and post an area based on the likely or actual radiological conditions.

## Slide 75: What Are Your Questions?

## Slide 76: Ready for RPT-243-PE-4