## Slide 1
ACADs (08-006) Covered
Keywords
Procedures, permits, instructions, stay times, RWP, job coverage, low dose waiting area, dosimeter, protective clothing, face shield, glasses, contamination, decontamination, exposure reduction, 10CFR20, controlled areas, administrative controls and limits.
Description
Supporting Material
Radiological Controls
1.1.8.4 | 3.3.8.4 | 3.3.8.9 | 3.3.8.14 | 3.3.8.17 | 3.3.8.18 | 3.3.8.19 | 3.3.8.21
3.3.8.23 | 3.3.9.8 | 3.3.9.21 | 3.3.9.26 | 3.3.10.9 | 3.3.10.10 | 3.3.11.7 | 3.3.11.9
3.3.11.12 | 3.3.11.13 | 3.3.11.15 | 3.3.11.16 | 3.3.11.18 | 3.3.11.19 | 3.3.11.20 | 3.3.11.23
3.3.11.29 | 3.3.11.30 | 3.3.11.31 | 3.3.11.33 | 3.3.11.34 | 3.3.11.36 | 3.3.11.38 | 3.3.11.40
3.3.11.41 | 3.3.12.4 | 3.3.13.7 |  |  |  |  | 

## Slide 2
Describe the concept of “total risk” as applied to the prescription of radiological work controls.
Describe exposure control techniques that can be used to control worker and technician radiation exposures.
Review Related Learning Outcomes Upon completion of this lesson, the student will be able to:
Notes: These learning outcomes should have been addressed at least one other time. Repetition here is to help ensure the student sees relationships and has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 3
Describe special precautions to be used when practical to control or reduce exposures during certain radiological conditions, such as:
  assignment of stay times and timekeepers,
  continuous radiological protection technician coverage,
  use of alarming dosimeters or dose rate meters,
  use of temporary shielding,
  availability of low dose rate waiting areas, and
  removal of high dose rate sources.
Review Related Learning Outcomes Upon completion of this lesson, the student will be able to:
Notes: These learning outcomes should have been addressed at least one other time. Repetition here is to help ensure the student sees relationships and has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 4
Describe work time reduction techniques that can be used to reduce worker radiation exposure, such as the following:
  pre-job planning and preparation
  pre-job mockup training for worker familiarity
  review of procedures for workability and efficiency
  use of special tools to improve worker efficiency
  improvement of worker comfort by controlling the environment (temperature, lighting, humidity, space)
  prefabrication of equipment in low-dose or no-dose areas
  decontamination to reduce protective clothing requirements .
Review Related Learning Outcomes Upon completion of this lesson, the student will be able to:
Notes: These learning outcomes should have been addressed at least one other time. Repetition here is to help ensure the student sees relationships and has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 5
Describe techniques by which increased distance can be used to reduce worker radiation exposure, such as:
  positioning workers away from hot spots or high dose areas,
  using remote operators or special tools to increase worker distance from a source, and
  removing equipment to low dose areas for maintenance.
Review Related Learning Outcomes Upon completion of this lesson, the student will be able to:
Notes: These learning outcomes should have been addressed at least one other time. Repetition here is to help ensure the student sees relationships and has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 6
Discuss factors that determine the ultimate effectiveness of installing temporary shielding, such as:
  the cost of installation (dollars and person-rem) versus benefit,
  physical space limitations,
  10CFR50.59 review constraints,
  floor loading constraints, and
  pipe and pipe hanger load constraints.
Describe the consequences of removing permanent or temporary shielding without proper review and authorization.
Review Related Learning Outcomes Upon completion of this lesson, the student will be able to:
Notes: These learning outcomes should have been addressed at least one other time. Repetition here is to help ensure the student sees relationships and has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 7
Based on the results of the prejob surveys and the scope of work, identify or evaluate the need for the following:
  a formal ALARA review
  pre-job briefings with workers
  the type and location of whole-body dosimeters,
  multiple whole-body dosimeters, and extremity dosimeters
  protective clothing requirements
  respiratory protection requirements
  special precautions or conditions to minimize the spread of contamination, reduce exposure, or minimize airborne contamination
Review Related Learning Outcomes Upon completion of this lesson, the student will be able to:
Notes: These learning outcomes should have been addressed at least one other time. Repetition here is to help ensure the student sees relationships and has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 8
Based on the results of the prejob surveys and the scope of work, identify or evaluate the need for the following (cont’d) :
  the degree of radiological protection technicians’ on-the-job coverage
  in-progress radiological surveys to be performed
  radiological hold points
Review Related Learning Outcomes Upon completion of this lesson, the student will be able to:
Notes: These learning outcomes should have been addressed at least one other time. Repetition here is to help ensure the student sees relationships and has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 9
Discuss generic plant procedures for conducting pre-job briefings for radiological work, including:
  when briefings are required,
  the frequency of briefings for continuing jobs,
  personnel required to attend briefings,
  items to be discussed in briefings, and
  the importance of resolving all questions in briefings.
Describe the in-progress radiological surveys that should be performed, at your site, under various radiological conditions.
Review Related Learning Outcomes Upon completion of this lesson, the student will be able to:
Notes: These learning outcomes should have been addressed at least one other time. Repetition here is to help ensure the student sees relationships and has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 10
Identify generic locations to be included for in- progress radiation surveys, such as:
  component being worked on,
  nearby piping and components,
  location where workers are positioned,
  path to and from the work site,
  low dose areas,
  hot spots, and
  potentially transient dose rate areas (resin lines, drain lines, movement of sources).
Review Related Learning Outcomes Upon completion of this lesson, the student will be able to:
Notes: These learning outcomes should have been addressed at least one other time. Repetition here is to help ensure the student sees relationships and has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 11
Demonstrate actions that should be taken if radiological conditions at the job site are significantly different from those shown on the RWP.
Explain actions to be taken if surveys show radiological conditions significantly different than expected, such as:
  high contact dose rates,
  high general area dose rates,
  unexpected low dose rates,
  high beta dose rates,
  very high contamination levels,
  very high airborne radioactivity, and
  unexpected lack of airborne radioactivity.
Review Related Learning Outcomes Upon completion of this lesson, the student will be able to:
Notes: These learning outcomes should have been addressed at least one other time. Repetition here is to help ensure the student sees relationships and has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 12
Discuss proper job coverage and radiological protection measures for high-exposure jobs and potential high-exposure jobs, such as the following: • steam generator maintenance (PWR) • reactor coolant pump seal replacement (PWR) • reactor water cleanup pump maintenance (BWR) • recirculation pump seal replacement (BWR) • reactor internal pump maintenance (ABWR) • control rod drive maintenance (BWR and ABWR) • diving operations
Review Related Learning Outcomes Upon completion of this lesson, the student will be able to:
Notes: These learning outcomes should have been addressed at least one other time. Repetition here is to help ensure the student sees relationships and has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 13
Discuss proper job coverage and radiological protection measures for high-exposure jobs and potential high-exposure jobs, such as the following (cont’d): • spent resin transfer operations • spent fuel movements • in-core detector maintenance • work in or around the spent fuel pool
Review Related Learning Outcomes Upon completion of this lesson, the student will be able to:
Notes: These learning outcomes should have been addressed at least one other time. Repetition here is to help ensure the student sees relationships and has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 14: New Learning Outcomes

## Slide 15: Learning Outcomes Upon completion of this lesson, the student will be able to:
Describe the methods that can be used to invoke radiological protection requirements, such as:
  steps in written procedures,
  radiation work permits,
  verbal instructions from the supervisor, and
  verbal instructions from radiological protection personnel.

## Slide 16: Exposure Control

## Slide 17: Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:
Describe techniques for controlling individual exposures during radiological work such as:
  assignment of stay times,
  use of radiation work permits (RWP),
  radiological protection technician job coverage (local or video monitor),
  use of low dose waiting areas, and
  use of remote electronic dosimeters.

## Slide 18: Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:
Identify techniques for controlling worker exposure to beta radiation, such as:
  the wearing of protective clothing,
  face shields, and
  glasses.

## Slide 19: Learning Outcomes Upon completion of this lesson, the student will be able to:
Explain exposure control, including the following: • contamination • decontamination • exposure reduction methods • protective clothing and respirators • provisions of 10CFR20 • radiologically controlled areas • site administrative controls and limits (margin from regulatory limits)

## Slide 20
Describe source reduction techniques that can be used to reduce worker radiation exposures, including the following: • decontamination of major system components • flushing of hot spots • sequencing of work so high dose rate items are removed from the work area early on • reduction of cobalt in system components • enhanced filtration of reactor coolant • early boration (PWR) • use of hydrogen peroxide (PWR) • lithium control (PWR) • soft shutdown (BWR)
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 21: Learning Outcomes Upon completion of this lesson, the student will be able to:
Describe how to estimate beta and gamma dose rates from the following:
  contamination on floor
  airborne radioactivity (particulate, iodine, noble gases, and tritium)
  pipes or tanks that contain radioactive liquids

## Slide 22: Contamination Controls

## Slide 23
Describe techniques for controlling the spread of contamination to personnel and equipment, including the following: • use of protective clothing • packaging of contaminated materials • use of containment devices • control of leaks from radioactive systems • decontamination
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 24
Describe precautions to be used, when practical, to control the spread of radioactive contamination during radiological work, such as:
  the use of containment devices,
  special protective clothing requirements, and
  the use of disposable coverings during job-site preparation.
Describe contamination control techniques that can be used to limit or prevent personnel and area contamination and/or reduce radioactive waste generation.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 25
Describe techniques to minimize the spread of contamination, including:
  protective clothing requirements and
  precautions during use,
  removal of contaminated equipment, and
  post-job removal or decontamination of the containment device.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 26
Discuss the generic plant requirements for entering and working in areas with contamination above plant limits, such as:
  radiation work permits,
  protective clothing,
  use of tools for a hot tool room,
  Step-off pads, and
  notification of the Radiological Protection Department.
Explain the importance of tracking and trending personnel contaminations.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 27: Airborne Radioactivity

## Slide 28
Identify work situations and work practices that could produce airborne radioactivity, such as:
  opening a contaminated system;
  working in highly contaminated areas;
  grinding, cutting, or welding radioactive of contaminated materials; and
  leaks from contaminated systems.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 29
Describe job coverage techniques that can be used to prevent or limit the spread of airborne radioactive material.
Describe precautions to be used, when practical, to control airborne radioactivity, such as:
  special ventilation,
  containment devices, and
  work area decontamination, as well as
  performing work under water or
  dampening the work area.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 30
Describe controls that can be used to reduce exposure to airborne radioactivity, such as:
  the use of filtered ventilation,
  decontamination of areas or equipment to eliminate the source of airborne radioactivity,
  use of containment devices (such as tents, glove bags),
  repair of leaks in contaminated systems,
  the performance of work under water or keeping contaminated materials wet, and
  use of a respirator (last resort).
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 31: RWPs, Work Documents, Job Coverage

## Slide 32
Explain the purpose of using radiation work permits (RWPs).
Explain the difference between “standing” and job-specific radiation work permits and when each is used.
State the purpose of and information found on a Radiological Work Permit (RWP) including the different classifications at your site.
State responsibilities in using or initiating a RWP.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 33
Identify the information to be included on radiation work permits (RWPs), such as the following: • scope of work covered by the RWP • radiation, contamination, and airborne radioactivity levels • internal and external dose action levels • location of hot spots • personnel authorized to use the RWP • dosimetry requirements • respiratory protection requirements • protective clothing requirements
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 34
Identify the information to be included on radiation work permits (RWPs), such as the following (cont’d):
  the period during which the RWP is valid
  radiological protection coverage and notification requirements
  special precautions, restrictions, and limitations
Explain the purpose of having each worker read and sign the RWP.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 35
Explain actions to be taken if the work scope or work location changes from that listed on the RWP.
Explain why technicians have stop-work authority, and identify types of situations in which this authority is to be implemented.
Identify the prejob radiological survey requirements for the work operation to be performed.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 36
Discuss the conditions under which each of the following is to be invoked during radiological work:
  continuous radiological protection (RP) technician coverage
  intermittent RP technician coverage
  RP technician present at start of job
  no RP technician coverage
  advanced radiation worker coverage
Explain the differences between continuous and intermittent job coverage.
Given example conditions, identify those that should require job coverage.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 37
Describe the in-progress radiological surveys to be performed under various radiological conditions, including radiation surveys, contamination surveys, and airborne radioactivity surveys.
Identify items that should be considered in planning job coverage.
Identify examples of information that should be discussed with workers during pre-job briefings.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 38
Describe actions required when personnel leave a work site upon completion of radiological work, such as:
  packaging, marking, and transferring contaminated tools, equipment, and trash;
  removing protective clothing;
  monitoring for contamination;
  returning special dosimetry;
  signing out of the RWP; and
  notifying radiological protection personnel of job completion.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 39
List the requirements individuals should follow while working in RBAs.
State the requirements for removing or releasing materials from any radiological area.
List four purposes of job coverage.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 40
Describe overall job control techniques in maintaining control of radiological work.
State the reasons to stop radiological work activities in accordance with the DOE RCS.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 41: Outline
General Control
Exposure Control
Contamination Control
Airborne Radioactivity Control
RWPs, Work Documents, and Job Coverage
Access Control
Questions

## Slide 42: General
Many different ways to specify and require radiological controls:
  The primary methods are through the radiation (radiological ) work permit (RWP) and posting
  Often times process, operational, and maintenance procedures will contain specific radiological controls
  The work group supervisor may specify radiological controls for the task
  Radiological Protection personnel might also stipulate specific radiological controls

## Slide 43: Exposure Control
The general means for controlling personnel exposure have been addressed on several occassions – TDS
Specific job coverage techniques for controlling personnel exposures during radiological work include:
  Stay time assignment and control
  Varying levels of RP Technician “job coverage”
  Use of low dose waiting areas
  Use of technology such as alarming dosimeters, video monitoring, and audio communnication

## Slide 44: Stay Times
Typically used in job coverage sitautions where the measured or anticpated dose rate is high enough that an exposure limit could be exceeded.
The actually contraints and guidelines used in deriving a stay time to assign is very specific to the faility and organization .
Typically – take the remaining margin of available dose (mr) for the individual and divide it by the dose rate (mr/hr) to identify the time allowed .
Often a “fudge factor” to be used to inject a level of conservatism into the stay time actually used.

## Slide 45: Stay Times
The individual’s electronic alarming dosimeter can be programmed to alarm at the end of the stay time
A dedicated time keeper should be used (often it is the RP Tech)

## Slide 46: Low Dose Waiting Areas
Job coverage and RWPs will be covered later in this lesson
Often in radiological work environments, it is advantageous to identify deignated “low dose waiting areas”
  Whenever not actively involved in work, workers will go to the low dose waiting area
  Although still in a dose rate area, the dose to be received will be less

## Slide 47: Other More Subtle Means
Other means of exposure reduction that are a bit more subtle include:
  Decontamination of contaminated areas – long term - reduces the amount of time a person spends in a dose rate area
  Control of airborne – again reduces the time spent in an area due to increased efficiency
  Establishing posted radiologically controlled areas imposes controls which will control the dose received
  Site administrative limits – conservate approach

## Slide 48: Beta Dose
So far we’ve been focused on gamma whole body dose
On some occasions beta dose will be a concern
Methods for reducing beta dose include:
  The use of protective clothing – possibly plastics for high energy beta dose to control skin dose
  Face shield or safety glasses will shield the lens of the eyes from beta dose
  Shielding the source of the beta dose with plastic or aluminum will also work

## Slide 49: Source Term Reduction
On a larger strategic level, plants work to reduce the overall amount of radioactive material causing the dose rates – referred to as source-tern reduction.
A number of techniques exist:
  System decontamination – use of chemical soultions to remove the oxide layer containing the corrosion and activation products
  Flushing the system to remove hot spots
  Reducing the inventory of cobalt in plant materials (less cobaly…less Co-60)

## Slide 50: Source Term Reduction
A number of techniques exist (cont’d):
  Micro filtration – the use of sub-micron filters in the purification system filters
  Chemistry control –
    Early boration (PWR) injects high levels of borated water early in the shutdown to cause a controlled crud burst such that the crud is removed via purification flow
    Hydrogen Peroxide injection – same principle as early boration but used at lower temperatures

## Slide 51: Source Term Reduction
A number of techniques exist (cont’d):
  Chemistry control –
    Lithium control (PWR) – used to maintain the pH at a base level to control the formation of corrosion products while minimizing stress cracking corrosion
    Soft Shutdown (BWR) minimizes the release of corrosion products into the coolant inventory; therfore, reducing the out of core dose rates after shutdown.

## Slide 52: Source Term Reduction
A number of techniques exist (cont’d):
  Remove components or sequence work such that dose contributors are removed from an area during high work activity periods

## Slide 53: Other Sources of Dose
Surface contamination, airborne radioactivity, and radioactive liquids in tanks and piping all can cause dose.

## Slide 54: Contamination Controls
Notes: Contaminaition Controls are introduced here and will be addressed in detail at a later time.

## Slide 55: Techniques and Precautions
Remember, contamination is the presence of radioactive material in an undesirable location.
The most effective form of contamination control is the prevent contamination in the first place.
This is most commonly accomplished through the use of contamination containment devices.
They range in style and size but all work off of the key word – containment.
  Glove bag, glove box, catch containment, containment hut, etc.

## Slide 56: Techniques and Precautions
Containment means – contain the contamination
  The choice of what to use is dependant upon :
    Size of component
    Configuration of system or component
    Location
    Quantity of fluids expected
    Vapors involved
    Isotopes involved

## Slide 57: Techniques and Precautions
If a containment installation is not appropriate or otherwise not permissable, other precautions should be considered such as:
  Job site preparations including the placement of washable or disposable coverings on adjacent structures, components, and floor spaces.
  Removal of the contaminated equipment from the area to a different controlled area.
  Closure of contaminated system or component openings with plastic or other contamination barrier

## Slide 58: Techniques and Precautions
If a containment installation is not apporpriate or otherwise permissable, other precautions should be considered such as (cont’d):
  Redirection of supply ventilation or any source of air flow away from contaminated surfaces
  Installation of exhaust ventilation from low to high contamination levels
At times where containment is not possible or the containment of contamination has been unsuccessful, then personnel are proteced from contamination through the use of protective clothing.

## Slide 59: Techniques and Precautions
Referred to by several names:
  PPE (personnel protective equipment)
  ANTI-C Clothing (anti-contamination)
  PCs (Protective Clothing)
The amount and type of PCs required will be dictated by several factors:
  The level and type of contamination present
  The level of physical activity anticipated
  Whether the work environment is dry or wet or extremely hot

## Slide 60: Techniques and Precautions
The requirements for working in contaminated areas within facilities will vary from facility to facility. In general they are:
  The work must be performed under the control of an active RWP
  The area will be appropriately posted with the exit designated by a step-of-pad with receptacles for removed clothing and trash
  Typically, tooling already contaminated with fixed contaminstion will be required for use in a contaminated area (hot tool room)

## Slide 61: Techniques and Precautions
When personnel become contaminated, it is necessary to document, track, and trend the contaminations.
The reasons this is necessary are:
  To document the location and amount in order to perform skin dose calculations
  To identify substandard work practices
  To identify substandard job packages
  To identify and correct deficient posting and contamination control measures

## Slide 62: Airborne Radioactivity

## Slide 63: Airborne Radioactivity Production
Several situations and work practices can produce airborne radioactivity:
  Any time a radioactive system is opened either in the course of operation (venting or draining operations) of for maitnenance (breaking open a flanged joint or threaded connection) radioactive gases or radioactive water (or both) can be released
  Any work activity within an area with pre-existing high levels of contamination can cause it to become suspended in air

## Slide 64: Airborne Radioactivity Production
Several situations and work practices can produce airborne radioactivity (cont’d):
  Vigorous activites such as grinding, cutting or welding on contaminated surfaces can cause it to become suspended in air
  Use of air operated tools or equipment in an area with loose surface contamination
  High velocity ventilation in a highly contaminated area can cause the suspension of the contamination in the air stream

## Slide 65: Airborne Radioactivity Prevention and Control
Some of the techniques and precautions used in contamination control are also effective in preventing or controlling airborne radioactivity:
  Containment enclosures
  Ventilation control over the surface
  Restricting the use of air in contaminated areas
  Decontamination of the work area
  Misting or dampening the work area
  Performing the work underwater

## Slide 66: Airborne Radioactivity Prevention and Control
Other precautions that are effective in controlling or preventing airborne radioactivity:
  Use of high efficiency absolute (HEPA) ventilation on the containment device or on the area
  Repairing leaks from radioactive systems
  Use of HEPA vacuum with griinding or welding
As a last resort, respiratory protection is worn where definitive measures at elliminating airborne are not possible or effective.

## Slide 67: Airborne Radioactivity Prevention and Control
In any case , the RP providing the job coverage must obtain work area air samples to facilitate the calculation of internal dose in the event airborne does occur

## Slide 68: RWPs, Work Documents, Job Coverage
Notes: RWP was covered previously as part of the LARA Process – it is presented here once more and can be done as a review or re-instruction

## Slide 69: RWP
Radiological Work Permit (sometimes called a Radiation Work Permit) both are RWPs.
RWPs are used to control work performed in a radiologically controlled area or activities associated with the use of radioactive material.
This is achieved by specifying:
  protective clothing requirements for a job,
  contamination control requirements,
  respiratory protection requirements,
  dosimetry requirements,

## Slide 70: RWP
This is achieved by specifying (cont’d):
  type of RPT coverage required,
  work restrictions,
  Time keeping for stay times
  Continuous RP coverage – either locally or remotely
  Stipulation of low dose waiting areas
  Use of temporary shielding
  Removal of source term from work area
Each worker is required to read and acknowledge understanding the requirements of the RWP to ensure they are held accountable for their protection

## Slide 71: RWP
General RWPs (sometimes called Standing RWPs) are for routine tasks with low radiological impact with entry into areas where radiological conditions are usually considered to be static.
  Usually don’t allow entry into High Radiation Areas, Contamination Areas, or Airborne Areas.
  Although the total estimated dose is high (long durations), the effective dose rate will be very low.
  These are usually written for long periods of time, quarterly or annually in some cases.

## Slide 72: RWP
Specific RWPs are for specific work tasks:
  in areas not permitted by a General RWP
  requiring the breech of a radioactive system
  that may change the radiological conditions of the area including the generation of airborne
Involve detailed job planning through the ALARA planning process

## Slide 73: RWP
The degree of detailed ALARA planning is normally determined by calculating the total person-rem estimated (dose assessment) for the job. Typical values might be:
  < 1 person-rem - normal planning process
  > 1person-rem but < 10 person-rem – ALARA Planning Group planning process
  > 10 person-rem – ALARA Group Planning plus review and approval by ALARA Committee

## Slide 75: Procedure or Work Package
The RWP is the controlling document for radiological protection requirements.
The procedure or work package specifically controls the technical aspects of the job (re: how to repack 2SI-46A) by providing written instructions.
May include prerequisites or safety or ALARA items such as:
  flush lines before beginning work,
  verify lockout is in place, or
  special training or qualification required to perform certain tasks.
Notes: 2/8/2013
75

## Slide 76: Procedure or Work Package
Detail and complexity depends on task to be performed and risk/consequence from a step being performed incorrectly or out of sequence.
Notes: 2/8/2013
76

## Slide 77: Sample

## Slide 78: Job Coverage
The term “job coverage” refers to the level of attention given by a fully qualified radiation protection technician to the work activity and the radiological controls being imposed on that activity.
Job coverage has four basic purposes:
  Ensure workers’ exposures are maintained ALARA and within limits and guidelines
  To minimize contamination and its spread
  To minimize airborne radioactivity and its spread
  To minimize the creation of radioactive waste

## Slide 79: Job Coverage
The following conditions or job types will dictate the need for some level of job coverage:
  Dose levels exist such that limits may be exceeded
  Dose rates are expected to increase significantly during the work
  Potential exists for spread of contamination or airborne radioactivity or significantly increasing levels
  Dosimetry in use may not be adequate for the types of radiation to be encountered
  Entry is made into high radiation areas

## Slide 80: Job Coverage - Types
The “type” of job coverage can take several forms:
  No coverage or coverage by an advanced radiation worker – for relatively benign activites that are not expected to have a significant impact on the radiological conditions of the area. Normally requires no additional surveys other than the survey used for planning the job and a verification survey at the beginning of the job.

## Slide 81: Job Coverage - Types
The “type” of job coverage can take several forms (cont’d):
  Initial and Intermittent – the RPT must be present with the task initially to determine the current radiological conditions to confirm they are as expected and will then periodically check the work to ensure no unforseen changes have occurred. Normally documents the initial radiation and contamination survey and air sample

## Slide 82: Job Coverage - Types
The “type” of job coverage can take several forms (cont’d):
  Continuous Coverage – the RP Technican must be an integral part of the team working on the job. The job does not work without the RP Tech being present. The Technician will conduct an initial survey – does rates, contamination, and air sample as appropriate and will perform other surveys as needed to monitor the radiological conditions as the job progresses.

## Slide 83: Job Coverage - Surveys
Surveys associated with radiological job coverage can be classified as follows:
  Prejob survey – taken in preparation for planning the job. Typically will be:
    a detailed radiation survey with contact, 12” and general area reading in the specific work site. A baseline to perform the needed dose estimates for the work.
    a detailed contamination survey of the work site to determine the controls that will be need in doing the job.
    evaluation of the expected airborne activity

## Slide 84: Job Coverage - Surveys
Surveys associated with job coverage can be classified as follows (cont’d):
  Prejob survey – may also be taken just prior to the start of the task to confirm the conditions have not changed such that the controls are no longer adequate.
  In-Progress (In-Process) Surveys – dose rate, contamination, and airborne surveys done at key points in the task where radiological conditions might be expected to change (i.e. opening a flanged joint, removing installed shielding, etc.)

## Slide 85: Job Coverage - Surveys
Surveys associated with job coverage can be classified as follows (cont’d):
  Restoration Surveys – dose rate, contamination, and airborne surveys done at key points in the restoration of the area. After the system is closed, after decontamination attempts, prior to removing posting installed in support of the job.

## Slide 86: Job Coverage – Stop Work
When performing any of the surveys discussed or in the course of providing job coverage, if radiological conditions are different than those which are expected, the technician must make a decision as to whether in their opinion it is safe to continue the work or not.
If they consider it is not, then they have the responsibility and the authority to “stop work”.
If that authority is exercised, then they must immediately, upon exiting the area, notify their supervision.

## Slide 87: Job Coverage – Stop Work
The supervisor will make the required notifications and a recovery plan will be constructed.
Examples of cases where a technician might stop the job:
  The dose rates were not expected to increase with this task; however, shortly after starting the work dose rates went from 2 mr/hr to 120 mr/hr.
  With another task, after about an hour of working on removing a valve from the system, a large volume of liquid is released into the area unexpectedly overflowing the catch basin under the valve.
Notes: Industry OE might be gathered that illustrate situations where an RPT stopped the work.

## Slide 88: Job Coverage – Stop Work
Examples of cases where a technician might stop the job (cont’d):
  In lifting the highly irradiated core barrel on a PWR during refueling, the water level in the refueling pool suddenly drops unexpectedly exposing a portion of the barrel causing the workers’ alarming dosimeters to go into alarm on the dose rate alarm.
  While covering work in the general area, a local continuous air monitor (CAM) goes into alarm. No one in the area has respiratory protection.
Notes: Industry OE might be gathered that illustrate situations where an RPT stopped the work.

## Slide 89: Job Coverage – Stop Work
Examples of cases where a technician might stop the job (cont’d):
  A worker’s protective clothing is ripped exposing bare skin.
  A worker repeatedly refuses to adhere to sound radiological work practices
Notes: Industry OE might be gathered that illustrate situations where an RPT stopped the work.

## Slide 90: Completion of the Job
Ideally, upon completion of the work, the work site is returned to a condition at least as good if not better than it started.
Some things that typically must be addressed:
  Packaging and disposal of radioactive trash
  Packaging of radioactive material such as tools an parts or components and to be decontaminated and or stored.
  Comprehensive restoration survey and removal of radiological control equipment and material put in place to support the work including special dosimetry

## Slide 91: Completion of the Job
Some things that typically must be addressed (cont’d):
  signing off of the RWP
  closing out the ALARA package for the work
In order to remove material from acontaminated area, a survey must be performed to identify the preence of loose surface and fixed contamination.
If levels are above the levels requiring posting, then the equipment must be wrapped, bagged, or otherwise contained with a radioactive materials tag attached.

## Slide 92: Completion of the Job
The items must be controlled by a qualified radiation worker knowledgeable of its contents or it must be stored in an approved radioactive materials area.
In order to be free-released, the item must be free of the presence of radioactive material including internally.
This is confirmed through the performance of release surveys and inspection of the item.

## Slide 93: Access Control

## Slide 94: How
There are numerous components that go into ensuring that entry into, work in, and exit from a radiologically controlled area is done safely:
  Posting
  RWP
  Job Coverage
  Personnel and Equipment Monitoring

## Slide 95: How
Posting was addressed in the previous lesson.
RWPs have been discussed; however, some means must be in place to ensure workers read and acknowledge the requirements of the RWP.
  This is often done with some form of access control software.
  The worker scans their ID badge, receives and “registers” an alarming dosimeter, enters in the RWP number, acknowledges reading and understanding, and is then “registered” onto the RWP

## Slide 96: How
This is normally accomplished at electronic sign-in stations (Control Points)
  Designated and authorized point of entry at radiologically controlled areas
  System may verify qualifications of workers signing in on RWPs (rad worker training, respirator quals, current bioassay, below dose control levels)
  Reads dosimetry and provides a searchable database for entry and dose records

## Slide 97: How – High, Locked, and Very High Radiation Areas
  High radiation, Locked High Radiation and Very High Radiation Areas have special access control requirements.
  For power plants, the requirements are specificed in licensing documents (technical Specifications). These may vary slightly facility to facility.
  In general, the posting for these areas are uniquely identifiable by either the shape and or the color of the posting.
Notes: DOE and Power Plant High Radiation, very Hogh Radiation Area access control requirements are almost identical.
2/8/2013
97

## Slide 98: How – High, Locked, and Very High Radiation Areas
  To enter a High Radiation Area, individuals shall have one or more of the following:
    A radiation monitoring device which continuously indicates the radiation dose rate in the area.
    A radiation monitoring device which continuously integrates the radiation dose rate in the area and alarms when a preset integrated dose is received.
      Entry into such areas with this monitoring device may be made after the dose rate level in the area has been established and personnel have been made knowledgeable of them.
Notes: 2/8/2013
98

## Slide 99: How – High, Locked, and Very High Radiation Areas
  To enter a High Radiation Area, individuals shall have one or more of the following (cont’d):
    A Health Physics qualified individual (i.e., qualified in radiation protection procedures) with a radiation dose rate monitoring device, and who is responsible for providing positive control over the activities within the area, and shall perform periodic radiation surveillance at the frequency specified by the RWP.
Notes: 2/8/2013
99

## Slide 100: How – High, Locked, and Very High Radiation Areas
  Previously, in the posting lecture, the focus was on what the regulations required.
  High Radiation and Very High Radiation Areas were discussed for both 10CR20 and 10CFR835.
  The defintions and requirements for posting are consistent for these areas.
  Power plants typically have another classification for posting that exists between High Radiation and Very High Radiation Areas – called Locked High Radiation Areas.
Notes: 2/8/2013
100

## Slide 101: How – High, Locked, and Very High Radiation Areas
  Locked High Radiation Areas – any area accessible to individuals with radiation levels greater than 1000 mrem/hr at 30 centimeters from the radiation source or from any surface penetrated by the radiation.
    Specific posting requirements
    Must be maintained locked until access is required. Key is maintained under administrative control of upper management
Notes: Make note that 10CFR835 and DOE do not designate 1R/hr at 30 cm from the surface penetrated by the radiation as a differntly posted HRA; however, access control requirements closely match LHRA access control requirements.
2/8/2013
101

## Slide 102: How – High, Locked, and Very High Radiation Areas
  Locked High Radiation Areas
    Specific access control requirements vary but typically will require (cont’d);
      Designated RP Technician coverage with a survey meter or remote monitoring
      Specific RWP with a specific PJB for entry
      Use of alarming dosimeter and in some case a flashing beacon at the boundary of the LHRA
      Controls in place to prevent the access point from being locked while personnel are in the area
Notes: Make note that 10CFR835 and DOE do not designate 1R/hr at 30 cm from the surface penetrated by the radiation as a differntly posted HRA; however, access control requirements closely match LHRA access control requirements.
2/8/2013
102

## Slide 103: How – High, Locked, and Very High Radiation Areas
  Very High Radiation Areas
    Specific access control requirements vary but typically will require the same type of controls noted for LHRAs.
    However ,because of the large dose rates involved and the infrequency of these types of entries, it would receive a considerably higher level of management oversight and documentation than a HRA or LHRA entry.
Notes: Make note that 10CFR835 and DOE do not designate 1R/hr at 30 cm from the surface penetrated by the radiation as a differntly posted HRA; however, access control requirements closely match LHRA access control requirements.
2/8/2013
103

## Slide 104: What Are Your Questions?

## Slide 105: Ready for RPT-243-PE-5