## Slide 1
ACADs (08-006) Covered
Keywords
ALARA, beta exposure, protective clothing, face shield, total risk, work-time reduction, pre-job, special tools, prefab, distance, temporary shielding, reduce exposure, source reduction.
Description
Supporting Material
Contamination Control, Decontamination and Respiratory Protection
1.1.8.4 |  |  |  |  | 
3.3.8.9 | 3.3.8.11 | 3.3.8.14 | 3.3.8.17 | 3.3.8.18 | 3.3.8.19
3.3.8.21 | 3.3.8.23 | 3.3.9.5 | 3.3.9.6 | 3.3.9.7 | 3.3.9.8
3.3.9.16 | 3.3.9.17 | 3.3.9.18 | 3.3.9.19 | 3.3.9.20 | 3.3.9.21
3.3.9.22 | 3.3.9.23 | 3.3.9.24 | 3.3.9.25 | 3.3.9.26 | 3.3.10.9
3.3.10.10 | 3.3.10.12 | 3.3.10.13 | 3.3.10.14 | 3.3.10.15 | 3.3.11.7
3.3.11.9 | 3.3.11.19 | 3.3.11.20 | 3.3.11.23 | 3.3.11.29 | 3.3.11.30
3.3.11.31 | 3.3.11.33 | 3.3.11.34 | 3.3.11.36 | 3.3.11.38 | 3.3.11.40
3.3.11.41 | 3.3.12.4 | 3.3.13.1 | 3.3.13.3 | 3.3.13.7 | 3.3.13.8
3.3.13.9 | 3.3.13.15 | 3.3.13.19 | 3.3.13.21 | 4.15 | 4.16
Notes: RPT-243-5
Contamination Control and Airborne Radioactivity
ACAD-08-006: 3.3.8.9; 3.3.8.11; 3.3.8.14; 3.3.8.17; 3.3.8.18; 3.3.8.19; 3.3.8.21; 3.3.8.23; 3.3.9.5; 3.3.9.6; 3.3.9.7; 3.3.9.8; 3.3.9.16; 3.3.9.17; 3.3.9.18; 3.3.9.19; 3.3.9.20; 3.3.9.21; 3.3.9.22; 3.3.9.23; 3.3.9.24; 3.3.9.25; 3.3.9.26; 3.3.10.9; 3.3.10.10; 3.3.10.12; 3.3.10.13; 3.3.10.14; 3.3.10.15; 3.3.11.7; 3.3.11.9; 3.3.11.19; 3.3.11.20; 3.3.11.23; 3.3.11.29; 3.3.11.30; 3.3.11.31; 3.3.11.33; 3.3.11.34; 3.3.11.36; 3.3.11.38; 3.3.11.40; 3.3.11.41; 3.3.12.4; 3.3.13.1; 3.3.13.3 ;3.3.13.7; 3.3.13.8; 3.3.13.9; 3.3.13.15; 3.3.13.19; 3.3.13.21
DOE: 2.05.01; 2.05.02; 2.05.04; 2.05.05; 2.05.06; 2.05.07; 2.07.01; 2.07.02; 2.07.03; 2.07.04 a-e; 2.07.05; 2.07.06; 2.07.07; 2.07.08; 2.07.09; 2.07.11; 2.10.10; 2.10.11; 2.10.13; 2.11.01; 2.11.02; 2.11.03; 2.11.04; 2.11.05; 2.11.06; 2.11.07; 2.11.10; 2.11.11; 2.11.12; 2.11.13
Duration: 3 hours
Material Resources Needed: none
Equipment/Supplies: Overhead display for PowerPoint
Assessment/Evaluation: The learning outcomes should be reviewed at the beginning of the class and should be reviewed periodically and at the conclusion. Examination number 2 will provide a formal assessment of these learning outcomes.
References Used in Development:
Basic Radiation Protection Technology, 5th edition, Gollnick; ISBN 0-916339-11-4
Nuclides and Isotopes/Chart of the Nuclides, 16th edition, Baum, Knox, Miller; ASIN: B000BUNFS8
Operational Health Physics Training, Moe; ANL-88-26 (1988)
DOE Health Physics Training, DOE-HDBK-1122-99 & DOE-HDBK-1122-2009
10CFR20 & 10CFR835 – current revisions

## Slide 2: Review Learning Outcomes Upon completion of this lesson, the student will be able to:
Identify techniques for controlling worker exposure to beta radiation, such as the wearing of protective clothing, face shields, and glasses.
Explain the ALARA concept and how it is applied to radiological work at the plant (for example, time, distance, shielding, engineering controls, and source reduction).
Describe the concept of “total risk” as applied to the prescription of radiological work controls.

## Slide 3
Describe work time reduction techniques that can be used to reduce worker radiation exposure, such as the following: • prejob planning and preparation • prejob mockup training for worker familiarity • review of procedures for workability and efficiency • use of special tools to improve worker efficiency • improvement of worker comfort by controlling the environment (temperature, lighting, humidity, space) • prefabrication of equipment in low-dose or no-dose areas • decontamination to reduce protective clothing requirements .
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 4
Describe techniques by which increased distance can be used to reduce worker radiation exposure, such as positioning workers away from hot spots or high dose areas, using remote operators or special tools to increase worker distance from a source, and removing equipment to low dose areas for maintenance.
Describe the consequences of removing permanent or temporary shielding without proper review and authorization.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 5
Describe special precautions to be used when practical to control or reduce exposures during certain radiological conditions, such as:
  assignment of stay times and timekeepers,
  continuous radiological protection technician coverage,
  use of alarming dosimeters or dose rate meters,
  use of temporary shielding,
  availability of low dose rate waiting areas, and
  removal of high dose rate sources.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 6
Discuss factors that determine the ultimate effectiveness of installing temporary shielding, such as the cost of installation (dollars and person-rem) versus benefit, physical space limitations, 10CFR50.59 review constraints, floor loading constraints, and pipe and pipe hanger load constraints.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 7
Describe source reduction techniques that can be used to reduce worker radiation exposures, including the following: • decontamination of major system components • flushing of hot spots • sequencing of work so high dose rate items are removed from the work area early on • reduction of cobalt in system components • enhanced filtration of reactor coolant • early boration (PWR) • use of hydrogen peroxide (PWR) • lithium control (PWR) • soft shutdown (BWR)
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 8: Contamination

## Slide 9
Discuss the generic plant requirements for entering and working in areas with contamination above plant limits, such as:
  radiation work permits,
  protective clothing,
  use of tools for a hot tool room,
  stepoff pads, and
  notification of the Radiological Protection Department..
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 10
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:
Explain the difference between loose and fixed contamination.
Identify potential sources of radioactive contamination, including work operations that can generate contamination.
Describe techniques to minimize the spread of contamination, including protective clothing requirements and precautions during use, removal of contaminated equipment, and post-job removal or decontamination of the containment device.
Notes: These learning outcomes have been addressed at least one other time. They are here to help ensure the student has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 11
Describe techniques for controlling the spread of contamination to personnel and equipment, including the following: • use of protective clothing • packaging of contaminated materials • use of containment devices • control of leaks from radioactive systems • decontamination
Describe contamination control techniques that can be used to limit or prevent personnel and area contamination and/or reduce radioactive waste generation.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 12
Describe precautions to be used, when practical, to control the spread of radioactive contamination during radiological work, such as:
  the use of containment devices,
  special protective clothing requirements, and
  the use of disposable coverings during job-site preparation.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 13
Describe how to estimate beta and gamma dose rates from the following:
  contamination on floor
  airborne radioactivity (particulate, iodines, noble gases, and tritium)
  pipes or tanks that contain radioactive liquids
Explain the differences between fixed and removable contamination and the resulting differences in techniques used for decontamination.
Explain the importance of tracking and trending personnel contaminations.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 14
State the components of a radiological monitoring program for contamination control and common methods used to accomplish them.
State the basic principles of contamination control and list examples of implementation methods.
List and describe the possible engineering control methods used for contamination control.
State the purpose of using protective clothing in contamination areas.
List the basic factors which determine protective clothing requirements for personnel protection.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 15: Airborne Radioactivity

## Slide 16
Describe controls that can be used to reduce exposure to airborne radioactivity, such as:
  the use of filtered ventilation,
  decontamination of areas or equipment to eliminate the source of airborne radioactivity,
  use of containment devices (such as tents, glove bags), and
  repair of leaks in contaminated systems,
  the performance of work under water or
  keeping contaminated materials wet, and
  use of a respirator (last resort).
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 17
Describe precautions to be used, when practical, to control airborne radioactivity, such as:
  special ventilation,
  containment devices, and
  work area decontamination, as well as
  performing work under water or
  dampening the work area.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 18: Job Coverage, RWPs, and Surveys

## Slide 19
Describe the methods that can be used to invoke radiological protection requirements, such as:
  steps in written procedures,
  radiation work permits,
  verbal instructions from the supervisor, and
  verbal instructions from radiological protection personnel.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 20
Explain the purpose of using radiation work permits (RWPs).
Explain why technicians have stop-work authority, and identify types of situations in which this authority is to be implemented.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 21
Based on the results of the prejob surveys and the scope of work, identify or evaluate the need for the following:
  a formal ALARA review
  prejob briefings with workers
  the type and location of whole-body dosimeters, multiple whole-body dosimeters, and extremity dosimeters
  protective clothing requirements
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 22
Based on the results of the prejob surveys and the scope of work, identify or evaluate the need for the following (cont’d):
  respiratory protection requirements
  special precautions or conditions to minimize the spread of contamination, reduce exposure, or minimize airborne contamination
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 23
Discuss generic plant procedures for conducting prejob briefings for radiological work, including:
  when briefings are required,
  the frequency of briefings for continuing jobs,
  personnel required to attend briefings,
  items to be discussed in briefings, and
  the importance of resolving all questions in briefings.
Identify the prejob radiological survey requirements for the work operation to be performed.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 24
Discuss the conditions under which each of the following is to be invoked during radiological work: • continuous radiological protection (RP) technician coverage • intermittent RP technician coverage • RP technician present at start of job • no RP technician coverage • advanced radiation worker coverage
Describe the in-progress radiological surveys to be performed under various radiological conditions, including radiation surveys, contamination surveys, and airborne radioactivity surveys.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 25
Identify generic locations to be included in progress radiation surveys, such as:
  component being worked on,
  nearby piping and components,
  location where workers are positioned,
  path to and from the work site,
  low dose areas,
  hot spots, and
  potentially transient dose rate areas (resin lines, drain lines, movement of sources).
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 26
Explain actions to be taken if surveys show radiological conditions significantly different than expected, such as:
  high contact dose rates,
  high general area dose rates,
  unexpected low dose rates,
  high beta dose rates,
  very high contamination levels,
  very high airborne radioactivity, and
  unexpected lack of airborne radioactivity.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 27
Describe actions required when personnel leave a work site upon completion of radiological work, such as:
  packaging, marking, and transferring contaminated tools, equipment, and trash;
  removing protective clothing; monitoring for contamination;
  returning special dosimetry; signing out of the RWP; and
  notifying radiological protection personnel of job completion.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 28
Discuss proper job coverage and radiological protection measures for high-exposure jobs and potential high-exposure jobs, such as the following: • steam generator maintenance (PWR) • reactor coolant pump seal replacement (PWR) • reactor water cleanup pump maintenance (BWR) • recirculation pump seal replacement (BWR) • reactor internal pump maintenance (ABWR) • control rod drive maintenance (BWR and ABWR) • diving operations
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 29
Discuss proper job coverage and radiological protection measures for high-exposure jobs and potential high-exposure jobs, such as the following (cont’d): • spent resin transfer operations • spent fuel movements • in-core detector maintenance • work in or around the spent fuel pool
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 30
Given example conditions, identify those that should require job coverage.
Identify items that should be considered in planning job coverage.
Identify examples of information that should be discussed with workers during pre-job briefings.
Describe exposure control techniques that can be used to control worker and technician radiation exposures.
List four purposes of job coverage.
Explain the differences between continuous and intermittent job coverage.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 31
Describe the in-progress radiological surveys that should be performed, at your site, under various radiological conditions.
Describe job coverage techniques that can be used to prevent or limit the spread of airborne radioactive material.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 32
Describe overall job control techniques in maintaining control of radiological work.
State the reasons to stop radiological work activities in accordance with the DOE RCS.
Review Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 33: New Learning Outcomes

## Slide 34: Contamination

## Slide 35
Define cross-contamination, and describe how it can result in the uncontrolled spread of contamination.
Describe other types of protective clothing available, including conditions under which each is used, procedures for donning and removing protective clothing, and inspections of clothing prior to use.
Describe methods used to protect against facial contamination, such as face shield, “ski-mask,” and specially designed hoods.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 36
Describe the devices used for containment of contamination during radiological work, such as:
  drapes,
  glove bags,
  tents,
  drain bottles,
  berms,
  absorbents to contain liquid, and
  catch containments.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 37
Identify the conditions in which the use of each type of containment device is to be considered.
Explain the inspections that are to be performed prior to the use of containment devices.
List discrepancies frequently observed in containment devices.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 38
Identify methods by which a work site can be prepared for the performance of highly contaminated work, such as:
  using disposable plastic;
  covering the work area with launderable, reusable sheeting;
  covering the work area with strippable paint; and
  painting concrete surfaces for ease in decontamination.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 39
State the requirements for removing or releasing materials from any radiological area.
Describe techniques to prevent the spread of contamination when contaminated materials are brought out of posted areas.
Describe the purpose and use of a stepoff pad in controlling the spread of contamination.
Discuss the reason for having lower limits for alpha contamination.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 40: Decontamination

## Slide 41
Explain why area decontamination should begin at areas of lowest contamination levels and progress toward areas of high levels.
Describe methods used for decontamination of areas within the plant, such as:
  mopping,
  using oil-impregnated wipes (masslin),
  wiping with damp rags,
  vacuuming, and
  scrubbing with brushes.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 42
Identify techniques available for the decontamination of tools and equipment, including the advantages, disadvantages, and limitations of each:
  carbon-dioxide-pellet blasting
  chemical decontamination
  electropolishing
  grit blasting
  high-pressure water blasting
  ice-pellet blasting
  low-pressure water blasting
  mechanical removal (grinding, machining, filing)
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 43
Select the appropriate personnel decontamination techniques for various levels of contamination and the degree to which contamination is fixed.
  removing particles with tape
  scrubbing gently with soft brush
  shaving contaminated hair
  sweating and chemical decontamination
  washing with lukewarm water and mild detergent
Explain why hot water, cold water, and abrasive cleaners are not used for personnel decontamination.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 44: Respiratory Protection

## Slide 45
Identify work situations and work practices that could produce airborne radioactivity, such as:
  opening a contaminated system;
  working in highly contaminated areas;
  grinding, cutting, or welding radioactive or contaminated materials; and
  leaks from contaminated systems.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 46
Identify the standards which regulate respiratory protection.
Identify plant requirements that must be met before an individual is issued a respirator, such as:
  training the individual in the proper use of equipment,
  medical evaluation, and
  quantitative fit test.
State the difference between a qualitative and quantitative fit test.
State the recommended physical functions the subject must perform during a respirator fit test.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 47
Define protection factor (10CFR20).
Identify the protection factors, advantages, and disadvantages of each type of respirator used in radiological applications at the station. • full-face negative pressure respirator • full-face positive pressure respirator • full-face air line respirator • air line (bubble) hood respirator • self-contained breathing apparatus
State how the term protection factor (PF) is applied to the selection of respiratory protection equipment.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 48
Describe the conditions under which each type of respiratory protection equipment must be used.
Explain the purpose of respiratory protection standards and regulations. Identify the OSHA, ANSI, and DOE respiratory protection program requirements.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 49
Identify the quality specification breathing air must meet.
Describe good practices in setting up portable ventilation systems and count rate meters.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 50: Outline
Additional Contamination Control and Containments
Decontamination – Personnel, Equipment, Area
Airborne Radioactivity & Respiratory Protection
Questions

## Slide 51: Additional Contamination Control

## Slide 52: Contamination Control
Contamination control is arguably the most challenging aspect of radiation protection.
In previous lectures, the basic components of contamination control were addressed:
  Protection
  Containment
  Access control measures and processes
This lecture will take a closer look at some of these basic components and some additional techniques to be used in contamination control.

## Slide 53: Contamination Control
Anything that transfers loose surface contamination from one surface to another in an uncontrolled fashion can be defined as cross-contamination.
Contamination control techniques and devices act to minimize that cross-contamination.
Improper undressing or misuse of contamination control devices can lead to cross contamination.
This in turn can result in the uncontrolled spread of radioactive contamination.
The actual control and threshold values vary facility-to-facility – a “typical” set is presented here.

## Slide 54: Contamination Control Protective Clothing
Cotton liners and modesty garments are NOT considered to be protective clothing
Partial PCs –a combination of gloves, and protective foot wear. At times may include lab coats.
Full PCs – booties, coveralls, gloves, hood, rubber over shoes
Double PCs – a full set with double gloves, double booties, double coveralls. The outer set might be disposable, or plastic. In some cases another hood may be specified as well as specialty items

## Slide 55: Contamination Control Protective Clothing
Some level of protective clothing is required in areas with loose surface contamination in excess of the station’s limits.
Typically this is >1000 dpm/100 cm2 beta-gamma or > 100 dpm/100 cm2 alpha contamination.
Alpha has a lower limit due to the increased risk of inhalation and ingestion at higher levels (an internal hazard)
> 1000 – 10,000 dpm/100 cm2 beta-gamma partial to full PCs will normally be used
> 10,000 – 100,000 dpm/100 cm2 beta-gamma full PC must be worn.

## Slide 56: Contamination Control Protective Clothing
> 100,000 dpm/100 cm2 beta-gamma will often require double PCs be worn. It some cases, the outer set must be plastic (regardless of wet or dry environment).
Plastic is also specified for wet work environments.
The industry is mixed regarding the material their protective clothing is made of.
  Some of it is a launderable synthetic material (pro-tech plus)
  Some of it is disposable breathable material – such as Ortex
  Some of it is made of tyvek disposable material

## Slide 57: Contamination Control Protective Clothing
Hot particle zones will usually require the use of disposable material that is segregated from other material.
Alpha zones will usually require that the used protective clothing be segregated from other material.
Even with double PCs – normally the worker’s face is still exposed.
In days past, respiratory protection was often stipulated because of high contamination levels to prevent facial contamination leading to internal deposition.

## Slide 58: Contamination Control Protective Clothing
Now, specific facial protection is used. This can be in the form of:
  Face shields (similar to a grinding shield or surgical shields)
  A mask type facial piece that covers a large portion of the skin of the face (think ninja).
  A special hood designed to cover a portion of the face as well as the head and neck.

## Slide 59: Contamination Control Containment Methods and Devices
Notes: http://www.lancsindustries.com/Lancs_Brochure.pdf accessed September 7, 2011

## Slide 60: Contamination Control Containment Methods and Devices
As noted previously, containment and control of the radioactive material is the preferred method for contamination control; however, total containment is not always possible.
Various types of containment devices or methods are available:
  Drapes – used where larger areas of the plant may be exposed to contamination and total containment is not appropriate. Involves draping the area and equipment with disposable or launderable material.

## Slide 61: Contamination Control Containment Methods and Devices
Various types of containment devices or methods are available (cont’d):
  Catch Containments – a drip bag that is positioned under a leaking device or a mechanical joint that is being breached. May have absorbents placed in the bottom to catch liquids or may have a drain line routed to a radioactive floor drain or drain bottle
Notes: http://www.lancsindustries.com/Lancs_Brochure.pdf accessed September 7, 2011

## Slide 62: Contamination Control Containment Methods and Devices
Various types of containment devices or methods are available (cont’d):
  Glove Bag – a total enclosure that is designed to contain all fluids and vapors released when a radioactive system is breached or a hazardous container is opened.
  May have absorbents placed in the bottom to catch liquids or may have a drain line routed to a radioactive floor drain or drain bottle.
  Should be vented via a HEPA filter.
Notes: http://www.lancsindustries.com/Lancs_Brochure.pdf accessed September 7, 2011

## Slide 63: Contamination Control Containment Methods and Devices
  Tents (Huts) – a fabricated “room(s)” erected around a rigid frame.
  May have multiple rooms.
  Usually vented via a HEPA fan unit.
  Used for extremely contaminated work or hazardous breeches of large components
Notes: http://www.lancsindustries.com/Lancs_Brochure.pdf accessed September 7, 2011

## Slide 64: Contamination Control Containment Methods and Devices
Inspections – are performed on an installed containment device commensurate to the hazard it is protecting against.
In general – any containment designed to contain liquid should have all joints and seams tested with clean liquid before use.
Penetrations for filters and drain rigs should also be tested after the installation process
The integrity of the device should be tested by inflating slightly with air and checking for leaks
Typically required to have visual inspections done periodically during use.
Notes: http://www.lancsindustries.com/Lancs_Brochure.pdf accessed September 7, 2011

## Slide 65: Contamination Control Containment Methods and Devices
Common discrepancies observed include:
  Holes, rips, leaks in the device
  Positive pressure on the device
  Ventilation inadequately routed to filtered exhaust
  Excessive material accumulated inside of device
  Sharp objects in unprotected area of device
  Body of device not properly supported
  Transfer assembly not properly installed or not properly used
  HEPA filter clogged or not properly installed
  Service access not available or not installed correctly
Notes: http://www.lancsindustries.com/Lancs_Brochure.pdf accessed September 7, 2011

## Slide 66: Contamination Control Containment Methods and Devices
Common discrepancies observed include (cont’d):
  Drain hose not adequate to handle the volume released
  Drain lines not free of obstructions or kinked
  Catch funnel used where glove bag is required
  Bottle not secured from tipping over
  Lighting in hut not adequate
  Airlock too small to accommodate undressing
  Failure to decontaminate the interior of device prior to removal

## Slide 67: Contamination Control Work Site Preparation
In addition to installation of catch basins or containment devices, the following items or techniques can also be used in preparing a work site for work on a contaminated system or material
  Barricades – temporary walls established to minimize air flow from contaminated to non-contaminated area and therefore the spread of contamination
  Application of a fixative coating that captures and locks loose srface contamination in place
  Painting or sealing exposed concrete to facilitate decontamination later

## Slide 68: Contamination Control Control of Material
Controlled removal of personnel and material from a contaminated area is necessary to control the spread of contamination.
Material Control
  Bagged at the step-off pad
  Carefully vent air out of bag
  Seal using a “j-seal” and duct tape
  Use of the transfer sleeve system in a containment set-up
  Survey outside of transfer bag and wipe clean as appropriate

## Slide 69: Contamination Control Control of Personnel
Personnel Control
  Apply principle of clean-to-clean and dirty-to-dirty when wearing and for removing PCs when leaving a contaminated area
  Follow recommended donning and doffing sequences – usually posted at a dress out area and at step-off pads
  Establishing step-off pad as designated exit location for contaminated areas
  Usually maintained as clean (non-contaminated)

## Slide 70: Decontamination

## Slide 71: Equipment and Area Decontamination
When equipment and areas do become contaminated – if it is economically and ALARA to decontaminate – there are certain techniques that are applied to ensure the contamination is cleaned up and not spread:
  Start at the lowest level of contamination and work toward the highest
    Ensures that the contamination is removed and not spread around
    Starting at the highest and moving to the lowest would tend to spread the contamination

## Slide 72: Equipment and Area Decontamination
Use the least needed – that is don’t use a wet mop if a masslin or dry wipe will work just as effectively – the idea is to minimize the radwaste generated during the decontamination process
Other methods that are effective:
  Use of a vaccum (HEPA filtered)
  Simple wiping with a damp rag or a rag and a spray cleaner (foam or liquid)
  Scrubbing with a cleaning brush and cleaning solution

## Slide 73: Equipment and Area Decontamination
Other methods that are effective (cont’d):
  CO2 blasting
  Use of strippable paint or other fixative coating

## Slide 74: Tools and Equipment Decontamination
CO2 blasting –basically uses frozen CO2 pellets under pressure to dislodge contamination which is then vacuumed up and collected. Little waste is generated, euipment is expensive to do initial set-up, CO2 pellets have to be
produced and could cause
oxygen displacement
Notes: http://www.google.com/imgres?q=co2+blaster&hl=en&client=firefox-a&hs=Kbb&sa=X&rls=org.mozilla:en-US:official&biw=1440&bih=707&tbm=isch&prmd=imvns&tbnid=_J51PzU6F9uqQM:&imgrefurl=http://news.thomasnet.com/fullstory/Dry-Ice-Blaster-provides-in-place-cleaning-500869&docid=UUwGkwatiqfa1M&w=350&h=351&ei=7pVuToeDA8yDtgejsJ3iBQ&zoom=1&iact=rc&dur=770&page=9&tbnh=153&tbnw=153&start=162&ndsp=19&ved=1t:429,r:18,s:162&tx=105&ty=100 accessed September 12, 2011

## Slide 75: Tools and Equipment Decontamination
Chemical decontamination – used to chemically remove a portion of the material – likely the oxide layer on metal objects. In doing so removal of the contamination occurs. Generates a mixed waste situation often difficult to dispose of. Very effective at decontamination.
Blasting – uses water, ice, or grit under pressure. All generate some waste but very effective at decontamination. Initial set-up can be expensive. The grit braks down over time and must be replaced.

## Slide 76: Tools and Equipment Decontamination
Electropolishing – a metal finishing process that involves immersion of the material in an electrolytic solution and the application of electrical current. In addition to the hazrd from using an electrolyte and electrically charged equipment, chemical mixed radioactive waste can be generated.
Mechanical grinding and machining – removes the portion of the equipment where the contamination has affixed itself. Generates waste products that may cause the spread or possibly airboren if not properly controlled.

## Slide 77: Personnel Decontamination
The role of the RPT is critical in responding to personnel contamination events.
Remember that many people are apprehensive about working around radioactive material
To have it on or in their body may be the cause of a great deal of stress
How you respond to the event can set the stage for the tone of the process and the ultimate conclusion to the event.
If you are calm and professional in your approach the individual will likely respond favorably.

## Slide 78: Personnel Decontamination
In response to personnel contamination events, the RPT has three basic steps that are followed in every case:
  First – evaluate the physical condiditon of the individual – if serious injury exists that requires medical attention, the need for that attention takes priority over contamination control
  Second – evaluate the location and quantity of the contamination – the type, clothing verus skin, internal verus external
  Third – remove and control contaminated clothing then evaluate and decontaminate skin contamination.

## Slide 79: Personnel Decontamination
In the event medical treatment is required, the RPT assists the medical personnel in exercising control measures which can be taken without jeopardizing the treatment.
In evaluating the event consider the following:
  Is the contamination localized on the general skin surface?
  Is the contamination located at body orifice or is a body orifice in close proximity?
  Is the contamination located in or around a break in the skin structure of the individual?

## Slide 80: Personnel Decontamination
In evaluating the event consider the following (cont’d):
  Is there any type of skin condition present in the vicinity of the contamination?
  Is the contamination on the clothing of the individual?

## Slide 81: Personnel Decontamination
Perform or direct the individual in doing a whole body survey for contamination for both alpha and beta-gamma contamination.
Start at the head and proceeding to the feet, pay particular attention to the following areas:
  contaminated area (if known)
  nose and mouth
  hands
  skin folds
  buttocks
  knees
  feet

## Slide 82: Personnel Decontamination
Hold the probe less than 1/2 inch from the surface being surveyed for beta and gamma contamination, approximately 1/4 inch for alpha contamination.
Do not touch the area being surveyed with the probe to preclude contaminating the probe.
Move the probe slowly (approximately 2 inches per second) over the surface.
If the count rate increases during the survey, pause for 5 to 10 seconds over the area to provide adequate time for instrument response.

## Slide 83: Personnel Decontamination
The whole body survey should take several minutes.
Do not hurry the survey and survey all areas that could be contaminated.
If the individual must be movd to another location, take measures to contain the contamination.
If clothing is contaminated, carefully remove and contain the contaminated items
Survey skin previously covered by the clothing.

## Slide 84: Personnel Decontamination
Decontaminate skin observing the following general precautions and techniques:
  Use tepid water – skin temperature. Cold water will cause the skin pores to contract and hold the contamination while hot water will open the pores allowing the contamination to go deeper into the pores.
  Use mild non-abrasive soap
  Work from low to high levels to prevent spread
  Use gentle scrubbing brushes
  Do not allow skin to become damaged
  Typically three attempts with soap and water

## Slide 85: Personnel Decontamination
Decontaminate skin observing the following general precautions and techniques:
  If hot particles are suspected, use tape presses applied gently to capture the particle
  If reductions are ineffective, consult supervisoin and consider the use of sweating or mild chemical solutions.
Collect samples of contamination for dose evaluation if needed.
Document initial and final levels and locations as well as all decontamination efforts.

## Slide 86: Personnel Decontamination
If contamination was wide-spread or found near wounds, on the person’s face or in any location where internal contamination may be suspected, the person should be directed to have a whole body count performed.
Supervisory and medical personnel also need to be involved.

## Slide 87: Respiratory Protection

## Slide 88: Respiratory Protection Regulatory Requirements
Previously the causes for airborne radioactivity and the measures taken to mitigate airborne radioactivity were discussed.
When needed to protect the individual and it is ALARA to wear, respiratory protection is specified.
Several entities govern the use of respiratory protection.
Local regulations such as DOE Order 440.1may require that your facility follow OSHA 29CFR1910.134.
Some Technical Specifications may require that ANSI Z88.2-1992 be adhered to as well.

## Slide 89: Respiratory Protection Regulatory Requirements
10CFR20 Subpart H – “Respiratory Protection and Controls to Restrict Internal Exposure in Restricted Areas” provides requirements that must be adhered to by NRC Licensees.

## Slide 90: Regulatory Requirements
NRC – 10 CFR 20
DOE – 10 CFR 835 (ANSI Z88.2)
States – 29 CFR 1910.134 OSHA

## Slide 91: Other Requirements
NIOSH Testing and Certification
  National Personal Protective Technology Laboratory
  Testing and research

## Slide 92: 10CFR20 Subpart H Respiratory Protection and Controls to Restrict Internal Exposure in Restricted Areas
Satisfies the requirements of OSHA 29CFR1910.134
20.1701 – to the extent practical – use engineering controls to control airborne.
20.1702 – when not practical – maintain dose ALARA by:
  Control of access
  Limit exposure times
  Use respiratory protection equipment

## Slide 93: 20.1703 Use of Respiratory Protection Equipment
NIOSH approved only – unless certified otherwise by permission
Implement and maintain a respiratory protection program that contains the following elements:

## Slide 94: 10 CFR 20.1703 Program Requirements
Air sampling
  Identify hazard
  Permit proper respirator selection
  Estimate doses
http://tbn1.google.com/images?q=tbn:im9pafP_PAot8M:http://www.staplex.com/airsamplers/TFIA/TFIA.jpg

## Slide 95
Surveys and bioassays as needed to evaluate intakes
10 CFR 20.1703 Program Requirements (cont’d)
http://www.wastestream.com/index_files/image016.jpg

## Slide 96
Operability test immediately before use
  User seal check for face-fitting type
  Functional check for others
10 CFR 20.1703 Program Requirements (cont’d)
http://www.cdc.gov/niosh/images/99-143l.jpg

## Slide 97
Written procedures for:
  Monitoring (air sampling and bioassay)
  Supervision and training of users
  Fit Testing
  Respirator selection
  Breathing air quality
  Inventory control
10 CFR 20.1703 Program Requirements (cont’d)
www.cdc.gov

## Slide 98
Written procedures
  Storage, issuance, maintenance, repair, testing, QA
  Record keeping
  Limitations on duration of use; periods of relief
10 CFR 20.1703 Program Requirements (cont’d)

## Slide 99
Medical clearance
  Before initial fitting for face-sealing type
  Before first field use for non face-sealing
  Annually or at frequency set by physician
10 CFR 20.1703 Program Requirements (cont’d)

## Slide 100: 10 CFR 20.1703 Program Requirements (cont’d)
Respirator fit testing –
  Prior to first use
  At least annually
  Negative pressure devices - for protection factor (PF) > 10 times the Assigned PF (APF)
  For other types - > 500 times the APF

## Slide 101
Relief From Respirator Use:
  Equipment malfunction
  Physical distress or psychological distress
  Procedure failure
  Communication failure
  Deterioration of operating conditions
  Any other conditions…
20.1703 Use of Respiratory Protection Equipment (cont’d)

## Slide 102
Limitations
  Vision correction
  Communication
  Low temperatures
20.1703 Use of Respiratory Protection Equipment (cont’d)
http://tbn3.google.com/images?q=tbn:Vm6f6edWdUJakM:http://www.avon-rubber.com/getimage.aspx.ID-126958.gif

## Slide 103
Standby person:
  Required for air supplied suits
  Must have combination of respirator and safety gear
  Maintain continuous communication
  Must be immediately available to assist worker who could not extract himself
20.1703 Use of Respiratory Protection Equipment (cont’d)
http://tbn0.google.com/images?q=tbn:qoyAjXnZPPNuKM:http://www.stoprescue.com/assets/images/autogen/a_tripod-tank.gif
- TGE Safety Services

## Slide 104
Supplied with respirable air of Grade D quality or better (OSHA 1910.134)
  Oxygen content 19.5 – 23.5 %
  Limits on hydrocarbons, CO, CO2
  Lack of noticeable odor
20.1703 Use of Respiratory Protection Equipment (cont’d)
http://www.trustcrm.com/ectny/respiratory_advisor/documentimages/figure2-49.gif

## Slide 105
No objects such as facial hair
  Beards, mustaches, sideburns, bangs,
  Must not interfere with seal between respirator and skin
20.1703 Use of Respiratory Protection Equipment (cont’d)
http://www.remnantresource.com/pictures/facial.hair.jpg

## Slide 106: Respirators
Two general categories
  Air purifying
  Atmosphere supplying
http://tradetechmarketing.com/marketing/efrfc.jpg
http://imghost.indiamart.com/data/Y/V/MY-7849/respiratory-20protection-20equipment_10556463_250x250.jpg

## Slide 107: Air Purifying Respirators
Negative pressure – worker’s lungs provide motive force- inhalation draws air through filters
Powered air purifying (PAPR) – drawn through filters by pump.
http://www.americanairworks.com/images/papr1.jpg
http://tbn1.google.com/images?q=tbn:d4LR_X3PrTN3gM:http://www.dartmouth.edu/~toxmetal/images/respirator.jpg

## Slide 108: Limitations of Air Purifying Respirators
Do not protect against oxygen deficiency
Low concentration of contaminant
Requires right cartridge for contaminant
Face fit is critical

## Slide 109: Air Supplied
Receive air from cylinders or compressors
  Continuous flow
  Pressure demand
http://tbn2.google.com/images?q=tbn:SE-q7NCf9aTGmM:http://www.airsystems.cc/images/High%2520Res/CBF.jpg
http://tbn2.google.com/images?q=tbn:QSdq9xLNwW35cM:http://www.geneseo.edu/~ehs/Respirator%2520Web%2520page/scba.gif

## Slide 110: Continuous flow
Half, full face piece; helmet; hood; suit
Can accommodate workers with facial hair
Can provide heating or cooling
http://tbn2.google.com/images?q=tbn:Kv3C4DfDaCO2_M:http://www.sea.com.au/html/products/pospress/pp_images/compair_sr63_alone.jpg

## Slide 111: Limitations of Air Supplied Respirators
Need secure air supply
Increased maintenance
Cost
Drag hose around

## Slide 112: Fit Testing
Two methods
  Qualitative fit test (QLFT)
  Quantitative fit test (QNFT) (measures effectiveness numerically)
http://www.trainingprofessionals.com/components/com_virtuemart/shop_image/product/ee2ebd72059392157c20b9a11b124aae.jpg
http://www.evereadyincomefund.com/UserFiles/Respitory%20mask%20fit%20testing%20a(1).jpg

## Slide 113: Fit Testing 29 CFR 1910.134, App A (OSHA)
Not conducted if hair prevents good seal
Respirator selection
Donning review

## Slide 114
Assessment of comfort - worker
  Position of mask on nose
  Room for eye protection
  Room to talk
  Position of mask on face and cheeks
Fit Testing 29 CFR 1910.134, App A (OSHA) – (cont’d)
http://tbn0.google.com/images?q=tbn:opPs0oIug2hOBM:http://www.midwestsalesinc.com/full%2520respirator.jpg

## Slide 115
Adequacy of fit - assessor
  Chin properly placed
  Adequate strap tension
  Fit across nose bridge
  Proper size to span nose to chin
  Tendency of mask to slip
Fit Testing 29 CFR 1910.134, App A (OSHA) – (cont’d)
www.cdc.gov

## Slide 116
User seal check
  Positive pressure check
  Negative pressure check
Fit Testing 29 CFR 1910.134, App A (OSHA) – (cont’d)
http://www.cdc.gov/niosh/images/99-143l.jpg

## Slide 117
During test
  Terminate if worker has breathing difficulty
  Use safety equipment
Fit Testing 29 CFR 1910.134, App A (OSHA) – (cont’d)
http://www.behltd.co.uk/fittest.jpg

## Slide 118
Test exercises – one minute each
  Normal breathing
  Deep breathing
  Turn head side to side
  Move head up and down
Fit Testing 29 CFR 1910.134, App A (OSHA) – (cont’d)
http://img.directindustry.com/images_di/photo-g/respirator-fit-tester-370727.jpg

## Slide 119
Test exercises
  Talking
  Grimace (15 sec)
  Bending over
  Normal breathing
Fit Testing 29 CFR 1910.134, App A (OSHA) – (cont’d)
http://img.directindustry.com/images_di/photo-g/respirator-fit-tester-370727.jpg

## Slide 120: Medical Evaluation
Must be completed before
  Fit testing
  Required to use respirator in work place
Must be performed by PLHCP (Physician or other Licensed Health Care Professional)
  Examination
  Review of questionnaire

## Slide 121: Medical Evaluation
Tobacco use
Claustrophobia
Pulmonary/lung problems
Coughing/shortness of breath
Heart problems
Hearing problems
Back/musculoskeletal problems
Previous exposure hazardous materials

## Slide 122: Assigned Protection Factors 10 CFR 20 App A (examples)
Type | APF
Full facepiece, negative pressure | 100 (DOE – 50)
Full facepiece, PAPR | 1000
Hood, PAPR | 1000
Full facepiece, supplied air, continuous flow | 1000
Full facepiece, supplied air, pressure demand | 100
Hood, air supplied, continuous flow | 1000
SCBA, full facepiece, pressure demand | 10000

## Slide 123: Questions