## Slide 1
ACADs (08-006) Covered
Keywords
Historical, shipping, low specific activity, interrelationship, limited quantity, regulatory limits, loose, fixed, contamination, sources, controlling contamination spread, hot particles, protective clothing, containment device, cross contamination, trending, radiation survey, incident response, step off.
Description
Supporting Material
Radiological Safety & Response
3.1.4 | 3.3.5.6.7 | 3.3.9.8.4 | 3.3.9.8.5 | 3.3.9.7 | 3.3.9.17 | 3.3.9.25 | 3.3.10.9
3.3.10.10 | 3.3.11.13.8 | 3.3.11.20.4 | 3.3.11.27 | 3.3.11.40 | 3.3.12.1 | 3.3.12.3 | 3.3.12.4.1
3.3.12.4.2 | 3.3.12.4.3 | 3.3.12.5 | 3.3.12.6 | 3.3.12.8 | 3.3.12.9 | 3.3.12.10 | 3.3.12.11
3.3.12.12 | 3.3.12.13 | 3.3.12.13 | 3.3.12.14 | 3.3.12.16 | 3.3.12.18 | 3.3.12.19 | 3.3.12.22
3.3.14.8 | 3.3.14.9 | 3.3.14.16 | 3.3.14.20.4 | 4.14.1 | 4.14.2 | 4.14.3 | 4.14.4
4.14.5 | 4.14.5.1 | 4.14.6.1 | 4.14.6.2 | 4.14.6.3 | 4.14.6.4 | 4.14.6.5 | 4.14.6.6
4.14.6.7 | 4.14.6.8 | 4.14.7.7 | 4.16.1 | 4.16.2 | 4.16.7 |  | 

## Slide 2: Radiological Safety & Response
RPT 211

## Slide 3: Shipping Radioactive Material
Identify regulations and procedures for shipping and receiving radioactive materials
49 CFR 172
49 CFR 173

## Slide 4: Shipping Radioactive Material
Define the following terms related to shipping radioactive material:
Type A and Type B
  “Type A package” means a packaging that, together with its radioactive contents limited to A1or A2as appropriate, meets the requirements of §§173.410 and 173.412 and is designed to retain the integrity of containment and shielding required by this part under normal conditions of transport as demonstrated by the tests set forth in §173.465 or §173.466, as appropriate. A Type A package does not require Competent Authority approval.

## Slide 5
“Type B package” means a packaging designed to transport greater than an A1or A2quantity of radioactive material that, together with its radioactive contents, is designed to retain the integrity of containment and shielding required by this part when subjected to the normal conditions of transport and hypothetical accident test conditions set forth in 10 CFR part 71.

## Slide 6
Low Specific Activity
  Low Specific Activity (LSA) material means Class 7 (radioactive) material with limited specific activity which satisfies the descriptions and limits set forth below. Shielding material surrounding the LSA material may not be considered in determining the estimated average specific activity of the package contents. LSA material must be in one of three groups:
  (1) LSA-I:
    (i) Uranium and thorium ores, concentrates of uranium and thorium ores, and other ores containing naturally occurring radionuclides which are intended to be processed for the use of these radionuclides; or
    (ii) Solid unirradiated natural uranium or depleted uranium or natural thorium or their solid or liquid compounds or mixtures; or
    (iii) Radioactive material other than fissile material, for which the A2value is unlimited; or
    (iv) Other radioactive material, excluding fissile material in quantities not excepted under §173.453, in which the activity is distributed throughout and the estimated average specific activity does not exceed 30 times the values for activity concentration specified in §173.436, or 30 times the default values listed in Table 8 of §173.433.
  (2) LSA-II:
    (i) Water with tritium concentration up to 0.8 TBq/L (20.0 Ci/L); or
    (ii) Other radioactive material in which the activity is distributed throughout and the average specific activity does not exceed 10−4A2/g for solids and gases, and 10−5A2/g for liquids.
  (3) LSA-III. Solids ( e.g., consolidated wastes, activated materials), excluding powders, that meet the requirements of §173.468 and in which:
    (i) The radioactive material is distributed throughout a solid or a collection of solid objects, or is essentially uniformly distributed in a solid compact binding agent (such as concrete, bitumen, ceramic, etc.);
    (ii) The radioactive material is relatively insoluble, or it is intrinsically contained in a relatively insoluble material, so that, even under loss of packaging, the loss of Class 7 (radioactive) material per package by leaching when placed in water for seven days would not exceed 0.1 A2; and
    (iii) The estimated average specific activity of the solid, excluding any shielding material, does not exceed 2 × 10−3A2/g.

## Slide 7
Limited Quantity
  Limited quantity of Class 7 (radioactive) material means a quantity of Class 7 (radioactive) material not exceeding the material's package limits specified in §173.425 and conforming with requirements specified in §173.421.
Exempt Quantity
  Radioactive material not meeting the lower limits of §173.436 (ACEM and ALEC)

## Slide 8: Shipping Radioactive Material
Discuss regulatory limits for radiation levels and contamination levels for packages and vehicles while in transit.

## Slide 9: State the limits for radioactive contamination for release of materials, equipment, and areas for unrestricted use.
<1000 dpm/100cm2 beta-gamma
<20 dpm/100cm2 alpha

## Slide 10: State the limit for radioactive contamination on personnel.
None detectable

## Slide 11: Define and state the posting requirements for contaminated areas.
Established by the plants. Standard is “Caution, Contamination Area.”

## Slide 12: Explain the difference between loose and fixed contamination.
Loose (removable) contamination can be removed by casual contact and non-destructive means. Fixed contamination requires destructive means for removal.

## Slide 13: Discuss the reason for having lower limits for alpha contamination.
Alpha is an internal hazard with a Quality Factor (weighting factor) of 20. It is 20 times more hazardous than beta-gamma emitters when internally deposited.

## Slide 14: Identify potential sources of radioactive contamination, including work operations that can generate contamination.
Reactor coolant systems
Systems connected to reactor coolant systems
Previously unexposed surfaces.
Work that will expose new surfaces
Work that will result in breaching systems

## Slide 15: Describe techniques for controlling the spread of, including:
Use of protective clothing
  Proper donning and doffing of PCs minimizes contact of skin with contamination
Packaging of contaminated materials
  Packaging materials keep the contamination at the source.
  Packaging materials prevent contact with material surface

## Slide 16
Use of containment devices
  Same concepts as for packaging, but applies to equipment being serviced “in place.”
Control of leaks from radioactive systems
  If the contamination stays in, it doesn’t spread. Pretty simple concept
Decontamination
  Removes the contamination

## Slide 17: Describe plant procedures for performing special contamination surveys, including
  Radioactive particles on personnel or equipment
  Radioactive particles in areas
  Small volumes of liquid leaving the radiologically controlled area
  Loose materials, such as sand, leaving the radiologically controlled area.

## Slide 18: Discuss the normal uses (plant specific locations), advantages, disadvantages, and relative sensibility of the following contamination detection devices:
Bag counters

## Slide 19
Conveyor-type contamination monitors

## Slide 20
Portable frisker
Portal monitors

## Slide 21
Tool monitors

## Slide 22
Whole-body contamination monitor

## Slide 23: Describe procedures for controlling hot particles.
  Large area wipes for surveys
  All primary system breaches “hot particle areas” until proven otherwise
  Increased survey frequency and special survey techniques

## Slide 24: Define a full set of protective clothing under normal circumstances
  Coveralls
  Hood
  Gloves
  Booties
  Shoecovers

## Slide 25: Describe other types of protective clothing available, including conditions under which each is used, procedures for donning and removing protective clothing, and inspections of clothing prior to use.

## Slide 26: Describe the devices used for containment of contamination during radiological work, such as drapes, glove bags, tents, drain bottles, absorbents to contain liquid, and catch containments.

## Slide 27: Glovebag

## Slide 28: Drape

## Slide 29: Tent

## Slide 30: Catch Containment

## Slide 31: Identify the conditions in which the use of each type of containment device is to be considered.

## Slide 32: Explain the inspections that are to be performed prior to the use of containment devices.

## Slide 33: Describe methods used to protect against facial contamination, such as face shields, “ski-mask,” and specially designed hoods.

## Slide 34: Describe techniques to minimize the spread of contamination: Protective clothing requirements and precautions during use Removal of contaminated equipment Removal or decontamination of the containment device.

## Slide 35: Identify methods to prepare a work site for highly contaminated work:
Disposable plastic
Covering the work area with launderable, reusable sheeting
Covering the work area with strippable paint
Painting concrete surfaces for ease in decontamination.

## Slide 36: Define cross-contamination, and describe how it can result in the uncontrolled spread of contamination.

## Slide 37: Describe techniques to prevent the spread of contamination when contaminated materials are brought out of posted areas.

## Slide 38: Describe the purpose and use of a stepoff pad in controlling the spread of contamination.
  Provides a place to conduct surveys prior to stepping into clean areas
  Provides a first indication of contamination spread
  Easily isolated

## Slide 39: Discuss the generic requirements for entering and working in areas with contamination above plant limits
  Radiation work permits
  Protective clothing,
  Use of hot tool room
  Stepoff pads
  Notification of the Radiological Protection Department.

## Slide 40: Describe, in general terms, the expected response to radiological incidents, including
  Precedence given to treating injuries
  Mitigation and minimization of exposure to plant personnel and the public
  Mitigation and minimization of damage to equipment
  Notification of appropriate personnel.

## Slide 41: Identify the radiological consequences that my result from various incidents
  Sudden increase in dose rate
  Uncontrolled spread of contamination
  A leak or spill of contaminated liquid
  An injury to and individual performing radiological work
  A fire in the radiologically restricted area
  Loss of a high-activity radiation source
  A degraded core
  Uncontrolled or unsecure high radiation areas.

## Slide 42: Describe how to estimate beta and gamma dose rates from the following:
Contamination on floor
Airborne radioactivity (particulate, iodines, noble gases, and tritium)
Pipes or tanks that contain radioactive liquids

## Slide 43: Describe how to estimate skin dose resulting from skin contamination including hot particles

## Slide 44: Describe isotopes expected to be present in the event of a radiological incident.

## Slide 45: Describe how to estimate dose due to ingestion or inhalation of radioactive materials.

## Slide 46: Estimate the activity released during an incident using the following:
Airborne activity levels in a plume
Contamination levels and extent of area contaminated
Gaseous/particulate-specific activity and volume released
Liquid-specific activity and volume released
Prerelease and post release radiation surveys (for example, pipe, valves, tanks)

## Slide 47: Identify work practices, instrument responses, and alarms that indicate the potential for radiological incident.

## Slide 48: Identify the immediate actions to be taken to control and minimize the extent of radiological incidents such as the following:
Alarm on electronic dosimeter
Area radiation monitor alarm
Contaminated injured personnel
Contaminated personnel
Continuous air monitor alarm
Fire in the radiologically controlled area
Off-scale pocket dosimeter
Contaminated liquid or resin spill
Dry contaminated material spill
Unmonitored release of radioactivity to the environment

## Slide 49: Evaluate radiological incidents to identify the scope and cause.

## Slide 50: Identify follow-up actions to correct the causes of the incidents.

## Slide 51: Identify radiological surveys to be taken as a result of an incident and the purpose of each.

## Slide 52: Describe how to locate and track a radioactive plume.

## Slide 53: Explain the importance of using trending to identify the causes of individual incidents and the common causes of multiple incidents.

## Slide 54: Trending
Precursors
Probabilities
Precautions
Procedures
Planning

## Slide 55: Discuss how reports of incidents at one plant can be useful in preventing similar incidents at another plant.
Discussion topic

## Slide 56: Describe recent significant radiological incidents at this plant or at another nuclear power plants.
Discussion

## Slide 57: Discuss emergency dose limits for life-saving and the control of plant safety.
10 Rem for saving valuable property
25 Rem for saving life

## Slide 58: Discuss the historical development of radiological protection standards.

## Slide 59: Explain the purpose of radiological protection standards and guidelines.
Discussion

## Slide 60: Identify the regulatory and advisory organizations that have cognizance in this area, and describe the function of each.
International Commission on Radiation Protection
  Provides recommendations and guidance on all aspects of protection against ionising radiation.
National Council on Radiation Protection and Measurements
  NCRP's mission is to help disseminate information and research data about radiation exposure and protection guidelines in the public interest.
International Commission on Radiation Units and Measurements
  More of the same
International Atomic Energy Agency
  United Nations organization to promote the peaceful use of nuclear energy
American National Standards Institute
  Establishes standards in many areas
Nuclear Regulatory Commission
  U.S. Regulator and licensing agency for nuclear materials
Department of Transportation
  Regulates the shipment of hazardous material
Agreement state
  States that develop their own regulations for nuclear materials.

## Slide 61
Discuss the philosophy of radiation protection limits, including the prevention of nonstochastic effects, minimization of stochastic effects, concept of “acceptable risk” or “comparable risk,” concepts of “cost versus benefit,” and ALARA.

## Slide 62: Define and discuss the interrelationship among the following:
Regulation
Regulatory guide
NUREG
Recommendation (health physics position papers)
License condition
Technical specification

## Slide 63: Explain the principles and use of the following standards:
10CFR19, Notices, Instructions, and Reports to Workers
10CFR20, Standards for Protection Against Radiation
10CFR21,Reporting of Defects and Noncompliance
10CFR34, Licenses for Radiography and Radiation Safety Requirements for Radiographic Operations
10 CFR50, Domestic Licensing of Production and Utilization Facilities
10 CFR61, Licensing Requirements for Land Disposal of Radwaste
10 CFR71, Packaging and Transportation of Radioactive Materials
regulatory guides applicable to power reactor radiological protection (such as RG 8.38, RG 8.18, and RG 8.15)