## Slide 1
ACADs (08-006) Covered
Keywords
Roentgen, gray, exposure rates, absorbed dose, dose equivalent, quality factors, linear energy transfer, relative biological effectiveness.
Supporting Material
Dose Equivalent
1.1.8.3.1 | 1.1.8.3.2 | 1.1.8.3.3 | 3.3.1.8 | 3.3.1.9.5 | 3.3.3.4 | 4.9.8 | 

## Slide 2: Dose Equivalent
Rad Pro III
NUCP 2331

## Slide 3: Several units
There are several units that we use to express how radiation interacts with matter
They may seem to be measuring the same thing but they are very specific
The specific type of interaction you are talking about has a specific unit
People will usually know what you are talking about but it should be paid attention to which unit is used

## Slide 4: Exposure
Roentgen - equivalent to 2.58 x E-4 C/kg in air,
  measures the amount of ionization in air
Applies only to X and gamma Radiation
Useful for measuring external radiation exposure from X and gamma rays
How many ions pairs does it take to create one R in air?
Notes: The Roentgen was named after W Roentgen, who discovered X-rays. It is used to to measure the amount of ionization that occurs in air by the passage of X or gamma radiation only.

## Slide 5: Exposure
1 R= 2.58 E –4 C/kg (as defined)
Charge on electron 1.6 E-19 C
Determine # of electrons needed to create amount of charge, to read 1 R in 1 kg of air
1.6 E 15 electrons(ion pairs) to read 1 R
1 ion pair = 33.7 eV in air
Can calculate amount of energy needed to be deposited in air to create one R
Notes: Relate charge on electrons to charge of R

## Slide 6: Absorbed Dose
Classic- RAD (radiation absorbed dose)
100 ergs/g (0.1 J/Kg)
  energy absorbed per mass of material
SI unit Gray (Gy) = 100 Rad = 1 J/Kg
1 R= .87 Rad in air (assume 33.7 eV/ion pair)
1 R= .98 Rad in tissue (assume 33.7 eV/ion pair)
Convention 1 R= 1 Rad
Notes: The RAD measures the amount of energy that is absorbed in any medium by radiation imparted in that medium

## Slide 7: Dose Equivalent
Classic-REM (Roentgen equivalent man)
Rad X Quality Factor (QF) = REM
SI unit Sievert (Sv) = 100 REM
QF ranges from 1-25 for different radiations
Measures biological effect of all types of radiation
  relates damage from all radiation at the cellular level.
Notes: A unit was needed to related the biological damage of different types of radiation. This unit made it possible to compare the biological effect of the several types of radiation.

## Slide 8: Quality Factors
Quality factor allows the assessment of biological response based upon the parameters of absorbed dose adjusted for the effectiveness of the radiation in producing damage.

## Slide 9: Quality Factors
X and gamma Rays = 1
Beta particles = 1
Alpha Particles = 25
Neutrons slow = 5
Neutrons fast= 20
Neutrons relativistic = 7
Protons= 8.5
Notes: Quality factors relate the amount of biological damage that can be done by absorbed energy from different radiation. The quality factor is closely related to the Relative biological effect(RBE) on relates the a mount of damage done by the same about of energy and the other relates the amount of energy to produce the same amount of effect.

## Slide 10: DOSE

## Slide 11: Radiation Interactions
Specific Ionization:
  Number of ion pairs produced by charged particle radiations per unit path length
  Energy loss can be by collision or coulomb interaction

## Slide 12
SPECIFIC IONIZATION
Specific ionization for a 4.8 MeV beta particle in air is 37 ion pairs/cm


## Slide 13
SPECIFIC IONIZATION

Specific ionization for a 4.8 MeV alpha particle in air is 40,000 ion pairs /cm

## Slide 14: Radiation Interactions
Specific Ionization
  Applicable to charged particles
  Measures charge produced
Linear Energy Transfer (LET)
  Average kinetic energy loss
Relative Biological Effectiveness (RBE)

## Slide 15: Radiation Interactions
Linear Energy Transfer (LET)
  Identifies the average energy loss per unit path length traveled due to all processes in that segment of the path
LET of particle increases as the particle slows down
  Low LET at high speeds
  High LET at low speeds

## Slide 16: RBE
Relative Biological Effectiveness
  Relates the amount of radiation it takes to produce the same effect (for each effect and each radiation)
  Res will change with end point
QF relates the amount of damage is done by same amount of radiation (general for reach type of radiation)
  QF do not change they are associated with a specific kind/energy radiation.

## Slide 17
CHANGE IN LET WITH INCREASING PATH LENGTH
Distance of Penetration
Relative
LET
For Heavy Charged Particles
Bragg Peak

## Slide 18: QUESTIONS?