## Slide 1
ACADs (08-006) Covered
Keywords
analytical balance, conductivity bridge with flow cell, inductively coupled plasma analyzer, in-line sodium monitor, ion selective electrode, microwave digestion
Description
Describe the operation and purpose of chemistry analytical equipment
Supporting Material
Chemistry Analytical Equipment
4.6.5.2 | 4.6.5.3 | 4.6.5.9 | 4.6.5.11 | 4.6.5.12 | 4.6.5.18 |  | 

## Slide 2: analytical balance
Purpose:
Measure weights
Notes: http://www.files.chem.vt.edu/chem-ed/gravimetry/balance.html
Analytical balances are accurate and precise instruments to measure weights. They require a draft-free location on a solid bench that is free of vibrations. Modern balances have built-in calibration weights to maintain accuracy. Older balances should be calibrated periodically with a standard weight. A few weighing tips follow:
Do not bump or place objects on the bench after zeroing the balance.
Weigh powders on weighing paper or in weighing dishes. Handle objects with tongs, gloves, or weighing paper to prevent fingerprints.
Let hot objects cool before weighing.
Weigh hygroscopic materials rapidly since they will absorb water during weighing.
When making repetitive weighings always use the same procedure.

## Slide 3: analytical balance
Operation:
Require a draft-free location on a solid bench that is free of vibrations.
Do not bump or place objects on the bench after zeroing the balance.
Weigh powders on weighing paper or in weighing dishes.
Handle objects with tongs, gloves, or weighing paper to prevent fingerprints.
Let hot objects cool before weighing.
Weigh hygroscopic materials rapidly since they will absorb water during weighing.
Notes: http://www.files.chem.vt.edu/chem-ed/gravimetry/balance.html
Analytical balances are accurate and precise instruments to measure weights. They require a draft-free location on a solid bench that is free of vibrations. Modern balances have built-in calibration weights to maintain accuracy. Older balances should be calibrated periodically with a standard weight. A few weighing tips follow:
Do not bump or place objects on the bench after zeroing the balance.
Weigh powders on weighing paper or in weighing dishes. Handle objects with tongs, gloves, or weighing paper to prevent fingerprints.
Let hot objects cool before weighing.
Weigh hygroscopic materials rapidly since they will absorb water during weighing.
When making repetitive weighings always use the same procedure.

## Slide 4: conductivity bridge with flow cell
Purpose:
Measurement of both electrical resistance and conductance of solutions.
If a measurement is to be performed in pure water, it is necessary to use a flow cell.
Notes: YSI Model 31A Conductance Bridge Instructions
http://www.ysi.com/media/pdfs/31A-Conductance-Bridge.pdf
Standard Operating Procedure for Conductivity Bridge (PDF)
http://www.epa.gov/greatlakes/lmmb/methods/conducti.pdf
Conductivity Theory and Practice
http://www.analytical-chemistry.uoc.gr/files/items/6/618/agwgimometria_2.pdf

## Slide 5: conductivity bridge with flow cell
Operation:
Rinse the apparatus with sample by filling the receptacle and putting it in place on the apparatus.
Discard this rinse and then fill the receptacle with sample and place it on the apparatus so no air bubbles are inside the conductivity cell.
Adjust the temperature to 25.0EC, and record the reading from the conductivity meter.
Notes: YSI Model 31A Conductance Bridge Instructions
http://www.ysi.com/media/pdfs/31A-Conductance-Bridge.pdf
Standard Operating Procedure for Conductivity Bridge (PDF)
http://www.epa.gov/greatlakes/lmmb/methods/conducti.pdf
Conductivity Theory and Practice
http://www.analytical-chemistry.uoc.gr/files/items/6/618/agwgimometria_2.pdf

## Slide 6: inductively coupled plasma analyzer
Purpose:
Measure the isotopic ratios of elements used in geochronologic/ thermochronologic, radiogenic isotopic, and stable isotopic studies
Notes: http://blog.labplanet.com/2011/12/19/inductively-coupled-plasma/
http://en.wikipedia.org/wiki/Inductively_coupled_plasma
http://serc.carleton.edu/research_education/geochemsheets/techniques/MCICPMS.html
http://www.gso.uri.edu/icpms/how_does.htm

## Slide 7: inductively coupled plasma analyzer
Operation:
ICP-AES, a type of atomic emission spectroscopy
ICP-MS, a type of mass spectrometry
ICP-RIE, a type of reactive-ion etching
Notes: http://blog.labplanet.com/2011/12/19/inductively-coupled-plasma/
http://en.wikipedia.org/wiki/Inductively_coupled_plasma
http://serc.carleton.edu/research_education/geochemsheets/techniques/MCICPMS.html
http://www.gso.uri.edu/icpms/how_does.htm

## Slide 8: in-line sodium monitor
Purpose:
Continuous monitoring of sodium in the process water
To detect sodium breakthrough and to ensure the process water is pure.
Notes: Sodium Monitoring in Water Treatment Processes
http://www05.abb.com/global/scot/scot203.nsf/veritydisplay/afbd10f3a046b78d80256e2e0036d793/$file/ag_ai-024_4.pdf
Why use Sodium
Monitoring in Water
Treatment Processes?
The customer needs:
To detect sodium breakthrough and to ensure the process water is pure.
To ensure the plant operates at the maximum efficiency.
To allow the plant to be maintained to specified standards.
Basic Measurement/ Analysis Theory
All on-line sodium monitors are based on the use of a sodium ion selective
electrode and a reference electrode. The measurement is very similar to that of pH,
with the electrode pair also responding to hydrogen ions and changes in sample
temperature.
The hydrogen ion interference is controlled by raising the pH of the sample
(reducing the hydrogen ion concentration). This is achieved by adding an alkali
– usually ammonia gas or a volatile amine. Temperature effects are reduced by
monitoring temperature and carrying out automatic temperature compensation.
The monitor is calibrated by use of solutions of known sodium ion concentration,
with the electrode pair producing a millivolt output proportional to the sodium
ion concentration.

## Slide 9: in-line sodium monitor
Operation:
The hydrogen ion interference is controlled by raising the pH of the sample (reducing the hydrogen ion concentration).
  This is achieved by adding an alkali – usually ammonia gas or a volatile amine.
Temperature effects are reduced by monitoring temperature and carrying out automatic temperature compensation.
The monitor is calibrated by use of solutions of known sodium ion concentration, with the electrode pair producing a millivolt output proportional to the sodium ion concentration.
Notes: Sodium Monitoring in Water Treatment Processes
http://www05.abb.com/global/scot/scot203.nsf/veritydisplay/afbd10f3a046b78d80256e2e0036d793/$file/ag_ai-024_4.pdf
Why use Sodium
Monitoring in Water
Treatment Processes?
The customer needs:
To detect sodium breakthrough and to ensure the process water is pure.
To ensure the plant operates at the maximum efficiency.
To allow the plant to be maintained to specified standards.
Basic Measurement/ Analysis Theory
All on-line sodium monitors are based on the use of a sodium ion selective
electrode and a reference electrode. The measurement is very similar to that of pH,
with the electrode pair also responding to hydrogen ions and changes in sample
temperature.
The hydrogen ion interference is controlled by raising the pH of the sample
(reducing the hydrogen ion concentration). This is achieved by adding an alkali
– usually ammonia gas or a volatile amine. Temperature effects are reduced by
monitoring temperature and carrying out automatic temperature compensation.
The monitor is calibrated by use of solutions of known sodium ion concentration,
with the electrode pair producing a millivolt output proportional to the sodium
ion concentration.

## Slide 10: ion selective electrode
Purpose:
Converts the activity of a specific ion dissolved in a solution into an electrical potential, which can be measured by a voltmeter or pH meter.
Notes: http://web.nmsu.edu/~kburke/Instrumentation/IS_Electrod.html
http://en.wikipedia.org/wiki/Ion_selective_electrode

## Slide 11: ion selective electrode
Operation:
ISE measures the potential of a specific ion in solution.
This potential is measured against a stable reference electrode of constant potential.
The potential difference between the two electrodes will depend upon the activity of the specific ion in solution.
This activity is related to the concentration of that specific ion, therefore allowing the end-user to make an analytical measurement of that specific ion.
Notes: http://web.nmsu.edu/~kburke/Instrumentation/IS_Electrod.html
http://en.wikipedia.org/wiki/Ion_selective_electrode

## Slide 12: microwave digestion
Purpose: Sample decomposition
Dissolve heavy metals in the presence of organic molecules prior to analysis by inductively coupled plasma, atomic absorption, or atomic emission measurement
Notes: Microwave Digestion (PDF)
Sample Dissolution Techniques (PDF)
http://en.wikipedia.org/wiki/Microwave_digestion

## Slide 13: microwave digestion
3 main approaches to microwave dissolution:
focused open-vessel
low-pressure closed-vessel
high-pressure closed-vessel.
Notes: Microwave Digestion (PDF)
Sample Dissolution Techniques (PDF)
http://en.wikipedia.org/wiki/Microwave_digestion

## Slide 14: microwave digestion
Operation:
Expose a sample to a strong acid
Raise the pressure and temperature through microwave irradiation.
  This increase in temperature and pressure of the low pH sample medium thereby increases both the speed of thermal decomposition of the sample, and the solubility of heavy metals in solution.
Once these heavy metals are in solution, it is possible to quantitate or quantify the sample through elemental techniques.
Notes: Microwave Digestion (PDF)
Sample Dissolution Techniques (PDF)
http://en.wikipedia.org/wiki/Microwave_digestion