## Slide 1: Precision Ag - Lab 1 Visualizing One Acre
Developed by Dr. Larry Everett
Director, Ohio Center for Precision Agriculture
Clark State Community College

## Slide 2: Items Needed For Each Team
2 – 100’ Tape Measures
4 – Stake Flags
Access to a Land Lab
  Minimum Size 100’ X 150’

## Slide 3: How Big is One Acre?
What is an acre?
How do we use acres in agriculture?
  Land prices - $/Acre
  Fertilization - #/Acre
  Yield measurement – Bu./Acre
  Can you think of other examples?

## Slide 4: Bonus Exercise
Divide students into groups
  Provide each group with 4 flags
  Instruct each group to mark the corners of 1/10th acre
  Leave the flags, to determine how accurate each group was at the completion of this lesson

## Slide 5: How Big is One Acre?
What measurement do other countries use?
  Hectares (metric system of area)
    10,000 m2 (100 Meters X 100 Meters)
  One hectare = 2.47 acres
  OR One acre = 0.405 hectares

## Slide 6: How Big is One Acre?
ARE - Confusing similarity
  One Are is a metric term meaning 100 m2
  Or 10 meters X 10 meters
  Or 1/100th of a hectare

## Slide 7: How Big is One Acre?
Acre
  Unit of Land used in the Imperial and US customary systems.
  Defined as the area of 1 Chain by 1 Furlong
  About the size of a US football field

## Slide 8: How Big is One Acre?

## Slide 9: How Big is One Acre?
One Acre = One Chain by One Furlong
  One Chain = 66 Feet or 4 Rods
  One Furlong* = 1/8 of a mile or 660 Feet or 10 Chains or 40 Rods
    * Distance a team of oxen could plow before resting
One acre =
  66 Feet X 660 Feet or 43,560 ft2
  1 Chain X 10 Chains or 10 chain2
  4 Rods X 40 Rods or 160 rod2

## Slide 10: How Big is One Acre?
If one Acre = 43,560 ft2
How many feet long would each side of an acre laid out in a “Square”?
Side
Side

## Slide 11: How Big is One Acre?
Area of a Rectangle = Length X Width
Area of a Square = Side X Side OR Side2
  Therefore the length of a “Square” Acre side
  = the square root of 43,560 = 208.7103 feet
  To convert 0.7103 from a decimal to inches multiply by 12 inches/ft.
    0.7103 feet X 12 inches/foot = 8.52 inches or 8 ½” rounded.
  Thus one “Square” Acre = 208’ 8 ½” X 208’ 8 ½”

## Slide 12: How Big is One Acre?
Layout of a Rectangular Acre
  We know that one acre = 66 feet X 660 feet
  For this lab we will use 100’ Tape Measures.
    Lets reduce the size to accommodate our measurement devices.
    Let’s use 1/10 Acre.
      66 feet X 660 feet/10 = 66’ X 66’
66'
66'

## Slide 13: 1/10 Acre Layout
Your instructor may divide you into teams of 3 – 5 students
Each team will obtain the necessary equipment to complete the lab
  Your task:
    Layout 1/10 of an acre in a square.
    Each side will be 66’ in length
    To ensure that the layout is square, the diagonal measurements must be the same.
    What should the diagonals measure?

## Slide 14: 1/10 Acre Layout
b
a
a

## Slide 15: 1/10 Acre Layout
Pythagorean Theorem: a2 + b2 = c2
For our lab side a and side b = 66’
Therefore 662 + 662 = 4,356 ft2 + 4,356 ft2 = 8,712ft2
Find the square root of 8,712ft2 to find the length of the diagonal (hypotenuse)
The diagonal (hypotenuse) = 93.34 feet
  93 feet + O.34 feet x 12 inches/foot = 93 feet 4 inches

## Slide 16: 1/10 Acre Layout
Step 1
Insert a Stake Flag at a logical starting point (point A)
A

## Slide 17: 1/10 Acre Layout
Step 2
Measure 66’ and insert a Stake Flag to establish Point B
A
B

## Slide 18: 1/10 Acre Layout
Step 3
Do NOT move Point A or Point B from this point forward
Necessary adjustments will be made to Point C and/or Point D

## Slide 19: 1/10 Acre Layout
Step 4
Measure 66’ from Point A to Point C with tape 1
Measure 93 feet 4 inches from Point B to Point C with tape 2
Point C will be at the intersection of tape 1 and tape 2
A
C
B

## Slide 20: 1/10 Acre Layout
Step 5
Measure 66’ from Point B to Point D with tape 2
Measure 93 feet 4 inches from Point A to Point D with tape 1
Point D will be at the intersection of tape 1 and tape 2
A
C
B
D

## Slide 21: 1/10 Acre Layout
Step 6
Verify that side CD is 66’ in length
Verify that the diagonals are of equal length
If adjustments are needed move ONLY Point C and/or Point D

## Slide 22: 1/10 Acre Layout – Post Analysis
What lessons did each group learn during the lab?

## Slide 23: 1/10 Acre Layout – Post Analysis
If the yield on this plot was 160 bu/A?
  How many bushels would be harvested on 1/10th Acre?

## Slide 24: 1/10 Acre Layout – Post Analysis
If the yield on this plot was 160 bu/A?
  How many bushels would be harvested on 1/10th Acre?
  160 bu/A ÷ 10 = 16 bu/A
  If our 1/10 Acre plot were divided into 1/4ths, how many bushels would be harvested in each 1/4th?

## Slide 25: 1/10 Acre Layout – Post Analysis
16 bu ÷ 4 = 4 bu

## Slide 26: 1/10 Acre Layout – Post Analysis
If each of those 1/4th sections were divided into fourths, what would the yield be in each of these smaller sections?

## Slide 27: 1/10 Acre Layout – Post Analysis
4 bu ÷ 4 = 1 bu
16.5’ x 16.5’ = 1 rod2
Or 6 – 30” rows, 16.5’ long
¼ x ¼ x 1/10 = 1/160
To review, there are 160 rod2/A

## Slide 28: Other Acre “Fun Facts”
640 Acres = 1 Square Mile
1 Square Mile = 1 Section
6 miles x 6 miles = 1 Township
½ Section = 320 Acres
  IE E ½ of Section 16….

## Slide 29: Other Acre “Fun Facts”

## Slide 30: Other Acre “Fun Facts”
Determine the number of Acres in the following legal description:
"The north 1/2 of the southeast quarter of the southwest quarter of section 24, township 32 north, range 18 east."

## Slide 31: Other Acre “Fun Facts”
Determine the number of Acres in the following legal description:
"The north 1/2 of the southeast quarter of the southwest quarter of section 24, township 32 north, range 18 east."

## Slide 32: Other Acre “Fun Facts”
640 A ÷ 4 = 160A (¼ Section)
160A ÷ 4 = 40A (¼ of ¼ Section)
40A ÷ 2 = 20A ( ½ of ¼ of ¼ Section)

## Slide 33: 1/10 Acre Layout - Quiz
The following quiz consists of 10 questions
Select the best answer

## Slide 34: 1/10 Acre Layout - Quiz
One acre is equal to the area of:
  One football field
  One hectare
  One furlong by one chain
  One rod by one link

## Slide 35: 1/10 Acre Layout - Quiz
2) One acre is equal to the area of:
  66 feet X 66 feet
  1/8 mile x 1/8 mile
  34,650 square feet
  43,560 square feet

## Slide 36: 1/10 Acre Layout - Quiz
3) The term “ _____/acre” is commonly used to indicate:
  Land Value
  Yield in bushels
  Pounds of fertilizer required
  All of the above

## Slide 37: 1/10 Acre Layout - Quiz
4) The Pythagorean theorem is expressed as:
  a + b = c
  a2 + b2 = c2
   r2
  None of the above

## Slide 38: 1/10 Acre Layout - Quiz
5) A rectangle measures 30 feet by 40 feet, the total area is:
  120 feet
  1,200 feet
  120 sq. ft.
  1,200 sq. ft.

## Slide 39: 1/10 Acre Layout - Quiz
6) A rectangle measures 30 feet by 40 feet, the distance across the diagonals is:
  50 feet
  50 square feet
  120 feet
  1,200 square feet

## Slide 40: 1/10 Acre Layout - Quiz
7) Horse racing distances are measured in furlongs. A race distance that is 8 furlongs is:
  One mile
  ¾ mile
  ½ mile
  ¼ mile

## Slide 41: 1/10 Acre Layout - Quiz
8) If there are 5,280 feet/mile, there are ______ acres in one square mile.
  80
  160
  320
  640

## Slide 42: 1/10 Acre Layout - Quiz
9) If a producer can plant an average of 20 acres/hour, how many acres can be planted in one 8-hour day?
  16
  20
  160
  200

## Slide 43: 1/10 Acre Layout - Quiz
10) If the producer can plant 20 acres/hour and averages an 8-hour day, how many acres can be planted in one week?
  800
  1,120
  1,400
  8,000

## Slide 44: 1/10 Acre Layout - Quiz
Raise your hand if you answered all the questions correctly.
Let’s see…..

## Slide 45: 1/10 Acre Layout - Quiz
One acre is equal to the area of:
  One football field
  One hectare
  One furlong by one chain
  One rod by one link

## Slide 46: 1/10 Acre Layout - Quiz
2) One acre is equal to the area of:
  66 feet X 66 feet
  1/8 mile x 1/8 mile
  34,650 square feet
  43,560 square feet

## Slide 47: 1/10 Acre Layout - Quiz
3) The term “ _____/acre” is commonly used to indicate:
  Land Value
  Yield in bushels
  Pounds of fertilizer required
  All of the above

## Slide 48: 1/10 Acre Layout - Quiz
4) The Pythagorean theorem is expressed as:
  a + b = c
  a2 + b2 = c2
   r2
  None of the above

## Slide 49: 1/10 Acre Layout - Quiz
5) A rectangle measures 30 feet by 40 feet, the total area is:
  120 feet
  1,200 feet
  120 sq. ft.
  1,200 sq. ft.

## Slide 50: 1/10 Acre Layout - Quiz
6) A rectangle measures 30 feet by 40 feet, the distance across the diagonals is:
  50 feet
  50 square feet
  120 feet
  1,200 square feet

## Slide 51: 1/10 Acre Layout - Quiz
7) Horse racing distances are measured in furlongs. A race distance that is 8 furlongs is:
  One mile
  ¾ mile
  ½ mile
  ¼ mile

## Slide 52: 1/10 Acre Layout - Quiz
8) If there are 5,280 feet/mile, there are ______ acres in one square mile.
  80
  160
  320
  640

## Slide 53: 1/10 Acre Layout - Quiz
9) If a producer can plant an average of 20 acres/hour, how many acres can be planted in one 8-hour day?
  16
  20
  160
  200

## Slide 54: 1/10 Acre Layout - Quiz
10) If the producer can plant 20 acres/hour and averages an 8-hour day, how many acres can be planted in one week?
  800
  1,120 – There are seven days in a week
  1,400
  8,000

## Slide 55: Questions
Are there questions?
How could you do this lab indoors?
  Brainstorm by group and report back…..

## Slide 56: Indoor Lab Ideas
Use 66” x 66” Instead of feet
How could you show 1 Acre accurately scaled in the classroom?

## Slide 57: Thank You!