## Slide 1: BioMems overview
Southwest Center for Microsystems Education
BioLOC's CD-Enzyme Linked Immunosorbent Assay (ELISATM) [Printed with permission]
Insulin pump for drug delivery system
[Printed with permission from Debiotech SA]
Scme-nm.org

## Slide 2: BioMEMS
BioMEMS is a subset of MEMS (microelectromechanical systems).
BioMEMS have a biological component and/or biomedical functions and applications.

## Slide 3: Objectives
Provide an operational definition of bioMEMS.
Describe five basic categories of bioMEMS.
List at least five applications of bioMEMS devices.

## Slide 4: What You Will Learn
A bioMEMS definition including the distinction between MEMS devices used for biological procedures (e.g., drug delivery) and those that use biological molecules in their operation (e.g., virus detection).
The importance of bioMEMS in advancing global health and applications necessary for understanding biological systems.
Broad applications for bioMEMS technology.

## Slide 5: Why You Need to Learn It
This knowledge is important because the use of microelectronics, particularly MEMS, is changing the medical fields of
detection,
diagnostics,
monitoring,
drug delivery,
analysis,
therapeutics and
others.

## Slide 6: MEMS vs. bioMEMS
MEMS use micro-sized components such as sensors, transducers, actuators, and electronic devices.
Many of the MEMS used in the medical field perform the same tasks as those used in other applications such as environmental, aerospace and consumer products.
For example, the MEMS inertial sensor found in airbag deployment mechanisms is also found in a pacemaker.

## Slide 7: MEMS vs. bioMEMS
Another category of MEMS used in the medical field incorporates biological molecules as an integral part of the device.
For example, a microcantilever transducer (graphic right) may be coated with antibodies (green spheres) that capture a virus (red sphere) in a blood sample while ignoring the other components in the sample.
Therefore, bioMEMS are MEMS that have biological and/or biomedical functions or applications.
Micro and nano-sized cantilevers used to identify a virus (red sphere) in a sample. The capture biomolecules are specific antibodies (green particles) [Image generated by and courtesy of Seyet, LLC].

## Slide 8: Glucose Monitor with Microtransducer
MEMS used for medical applications include devices to detect disease, monitor chemicals, and deliver drugs.
An example is the glucose sensor (see figure). This blood glucose sensor works on the basis of a glucose oxidize reaction with blood plasma.
The transducer at the end of the sensor stick is 1 mm long by 200 μm wide about the size of the “T” in TRUST on a penny. Newer glucose sensor use even smaller transducers.
Blood Glucose Monitor
[The MEMS transducer is at the end of the sensor. A droplet of blood is placed on top of the transducer, voltage is applied and a chemical reaction takes places. The current produced by the chemical reaction is measured indicating the amount of glucose in the blood sample.

## Slide 9: MEMS Glucose Monitor and Micropump
The figure to the right shows a complete glucose monitoring and drug delivery system.
The glucose is constantly monitored using an in vivo (implanted) chemical transducer (C).
A micropump in (A) delivers insulin via a cannula (B) on an as-needed basis .
D is the transmitter that relays the information from the glucose sensor (C) to the computer (A).
MiniMed Paradigm[R] REAL-Time System from Medtronic Diabetes
[Printed with permission from Medtronic Diabetes]

## Slide 10: Microcantilever Sensors
BioMEMS can use the properties of biological molecules to actuate a small machine.
For example, microcantilevers are used to detect a variety of analytes such as DNA, proteins, and antigens (see graphic).
The analytes attach to a probe surface layer of biomolecules. This load induces surface stress causing the cantilever to bend.
Biomolecules are produced by living cells. All known forms of life are comprised solely of biomolecules. These microcantilevers are designed to use biomolecules to detect and capture other specific biomolecules. This is accomplished with a functionalized cantilever surface. In this case a probe surface layer of biomolecules whose function is to capture the target molecules is deposited on the cantilever’s surface. This probe layer can be as thin as a monolayer (one molecule thick).

## Slide 11: In Vivo Devices
Another distinction of bioMEMS is between implantable devices (in vivo) and devices used outside of the body (in vitro).
Biocompatibility and biofouling are of great concern for implantable devices.
The body presents a harsh environment which can cause implantable devices to be rejected due to an inflammatory response. This response indicates bio-incompatibility between the host and the device.
BioMEMS device functions can also be affected by biofouling, a biological response by the host that interferes with the functioning of the device.

## Slide 12: The Evolution of bioMEMS
The evolution of MEMS technologies coupled with advances in the understanding of genomics, proteomics, and biotechnology techniques permit new opportunities for advancing the applications of bioMEMS devices.
BioMEMS will enable new modes of biosensing, molecular identification and monitoring, and futuristic biomedical and biological systems that use MEMS technology.

## Slide 13: Advancing Technologies
New areas of biotechnology have provided opportunities to refine bio techniques using MEMS technology.
DNA sequencing
ELISA (Enzyme Linked Immunosorbent Assay) (see figure)
Sequencing of the human and other genomes
New advancers in drug discovery and delivery
Increased emphasis on homeland security
Environmental monitoring
BioLOC's CD-Enzyme Linked Immunosorbent Assay (ELISATM)
[Printed with permission]

## Slide 14: Applications of bioMEMS
Areas that would benefit from the development of bioMEMS to enhance current methods include the following:
Sample preparation
Screening
Diagnostics
Monitoring
Drug delivery
Individualized treatment
Less invasive surgical procedures

## Slide 15: What’s Out There Now?
BioMEMS provide the opportunity to improve upon current methods, develop new ones, and potentially lower the cost of medical care.
Examples of bioMEMS devices already available include a
tiny insulin pump for diabetics,
DNA microarray and protein array chips (see figure), and
various biosensors.
Biochip slide for testing protein arrays
Each biochip has hundreds to thousands of gel drops on a glass, plastic or membrane support. The biochip system can identify infectious disease strains in less than 15 minutes when testing protein arrays and in less than two hours when testing nucleic acid arrays.
[Image courtesy of Argonne National Laboratories]

## Slide 16: Shrinking Technologies
The potential for miniaturized devices provides obvious advantages, whether in vivo or in vitro.
Such advantages include reduced manufacturing cost, smaller sample size, and small amount of reagents.
The physical space savings of using microdevices rather than large pieces of lab equipment is also cost effective.

## Slide 17: Improving the Quality of Life
For the diabetic, a small monitoring (C/D) and insulin delivery (A/B) device greatly contributes to the ease of disease regulation (see figure).
Persons undergoing invasive tests such colonoscopies or endoscopies appreciate a smaller detection device.
Portability of small test devices makes testing in remote areas where clinical labs are not available possible.
Glucose Monitoring and
Insulin Deliver System
[MiniMed Paradigm[R] 522 insulin pump, with MiniLinkTM] transmitter and infusion set. Printed with permission from Medtronic Diabetes]

## Slide 18: Enabling Technologies
MEMS is an enabling technology for applications in the life sciences. New biotechnologies are enabling technologies for the applications of MEMS.
New possibilities are created by merging our knowledge of biological systems into existing research tools.
These possibilities could lead to providing better health care, identifying key molecules, delivering targeted therapy, and creating possibilities for small point of care tools.

## Slide 19: The Current Market
There are several bioMEMS devices already on the market.
Some are very promising for commercialization within the next five years.
Some are in the research phase with an unknown commercialization date, but holding great promise for the future of bioMEMS applications.

## Slide 20: Point of Care Devices
Rugged small diagnostic microfluidic devices that can withstand harsh conditions present attractive alternatives to current laboratory tests.
Such medical diagnostic systems hold promise for portable point-of-care (POC) testing in the developing countries where sophisticated laboratories do not exist.
The development of inexpensive, accurate, and durable diagnostic tools that do not require highly trained medical technicians and that can be used on-site, have cost-saving benefits for everyone.

## Slide 21: Oh - The Possibilities!
BioMEMS are being researched for possible applications in a variety of areas, but have already led to multiple applications in the following areas:
Detection
Analysis
Diagnosis
Therapeutics
Drug delivery
Cell culture
Detection
Analysis
Diagnostics
Drug Delivery
Cell Culture
New Emerging
Therapeutics

## Slide 22: Lab-on-a-Chip (LOC)
In research and clinical laboratories, the μTAS (micro-total-analysis systems) and LOC (lab-on-a-chip) devices are the most successful applications for bioMEMS. LOCs are designed to analyze samples as small as a picoliter. They are also point-of-use devices; in other words, they can be used in the field, at the site of an accident, or in remote areas where medical laboratories are non-existent.
The figure is an example of an LOC.
Lab-on-a-Chip (LOC)
[Printed with permission. From Blazej,R.G.,Kumaresan,P. and Mathies, R.A. PNAS 103,7240-7245 (2006)]

## Slide 23: BioMEMS for Detection
Sensors for chemical detection
Bacterial, fungal, and viral detection
Antibody detection
Disease detection
Examination devices (such as endoscopes and catheters)
Home Pregnancy Test
(Detection of protein
in the urine of a pregnant woman)

## Slide 24: BioMEMS for Analysis
Bacterial identification and antibiotic susceptibility
Clinical laboratory medicine (clinical chemistry)
DNA analysis for forensics identification (See graphic)
Identifying complementary DNA through the hybridization process
Graphic illustrates what happens in a biochip: The target single-strand DNA attaches to a complementary capture probe or a matching DNA single strand.

## Slide 25: BioMEMS for Diagnostics
Disease identification
Protein isoform identification (used to assist in prescribing appropriate drugs for personalized medicine)
Antibody identification using MEMS chemical transducers and sensors (See graphic)
Chemical Sensor Arrays (Can detect, identify and determine the amount of an analyte in solution for the purpose of diagnosis)

## Slide 26: BioMEMS for Monitoring
Blood glucose level for diabetics
Antibody level monitoring for HIV patients
Blood cell concentrations for patients undergoing chemotherapy
Continuous monitoring of high-risk patients (The graphic illustrates an electrocardiogram (ECG) patch which monitors patients for arrhythmias day and night. )
Illustration of a MEMS electrocardiogram (ECG) patch monitor. Such a device is being developed by Belgium's IMEC for monitoring a patient's arrhythmias all day and night.

## Slide 27: BioMEMS for Drug Delivery
Antibiotic administration
Intravenous nutritional supplementation
Pain medication
Insulin pump for drug delivery system
[Printed with permission from Debiotech SA]
Update on this insulin pump:
In February 2009 STMicroelectronics and Debiotech Announced First Prototypes of Disposable Insulin Nanopump. The Nanopump is less than one fourth the size of existing insulin-pump devices and can be worn as a nearly invisible patch on the skin.
(Reference: Hearst Semiconductor Applications. February 03, 2009)

## Slide 28: BioMEMS for Cell Culture
Cell separation and counting
Microenvironments for growing cells in vitro and analysis (see above graphics)
MEMS Cell Culture Array. This array creates a microenvironment for growing cells in vitro and in parallel, allowing for the analysis of multiple cell growth conditions. A diagram of how it works is on the left. The constructed array is shown with a SEM image on the right.
[Developed at and courtesy of BioPOETS, UC-Berkeley.]

## Slide 29: Emerging Applications
There are additional categories but these six areas provide a core from which we can launch a discussion about the types of MEMS devices and how they are currently being used or developed for bioMEMS.
Hopefully, advances in these six areas will encourage further interest in emerging applications of MEMS technologies for medicine and life sciences.

## Slide 30: Miniaturization
Processes that have been miniaturized:
PCR, polymerase chain reaction: A method used to amplify DNA samples used in forensics and other applications.
DNA sequencing: A process for identifying the order of the molecular components of the DNA molecules that contain the genetic blueprint for heredity.
Chromatography: Molecular separation based on size, charge, or other properties.
ELISA, enzyme-linked immunosorbent assay: Used in common tests such as HIV and pregnancy tests.
Partial output of a Colorimetric Sensor Array used to analyze the makeup of a gas mixture. This array can detect up to 15 pathogens in a sample concentration.

## Slide 31: Food For Thought
The relatively new areas of bioMEMS technology have opened exciting opportunities to refine bio-technology applications. In discovering the possibilities of bioMEMS applications think about answers to the following questions.
What are the benefits of miniaturizing existing techniques?
How could MEMS technologies be used effectively for bioMEMS?
What concerns need to be addressed in order to make bioMEMS applications successful?

## Slide 32: Summary
BioMEMS is a subset of MEMS (microelectromechanical systems). It refers to any MEMS used in a biological application. BioMEMS utilize micro-sensors, transducers, actuators, and electronic components. Some bioMEMS incorporate biomolecules as an integral part of the device.
BioMEMS are being researched and developed for possible applications in a variety of medical areas. Much of this research has already lead to the commercialization of many devices in the following medical areas. (See next slide)

## Slide 33: Areas of bioMEMS Applications
Detection
Analysis
Diagnostics
Drug Delivery
Cell Culture
New Emerging
Therapeutics

## Slide 34: Disclaimer
The information contained herein is considered to be true and accurate; however the Southwest Center for Microsystems Education (SCME) makes no guarantees concerning the authenticity of any statement. SCME accepts no liability for the content of this unit, or for the consequences of any actions taken on the basis of the information provided.

## Slide 35: Acknowledgements
Copyright by the Southwest Center for Microsystems Education and The Regents of the University of New Mexico.
Southwest Center for Microsystems Education (SCME)
800 Bradbury Drive SE, Suite 235
Albuquerque, NM 87106-4346
Phone: 505-272-7150
Website: www.scme-nm.org email contact: mpleil@unm.edu
and
Bio-Link
Website: www.bio-link.org
The work presented was funded in part by the National Science Foundation Advanced Technology Education program, Department of Undergraduate Education grants: 0830384 and 0402651.