## Slide 1: Personal Protective equipment (PPE)
SCME Personal Protective Equipment Learning Module

## Slide 2: Unit Overview
When manufacturing microsystems in a cleanroom environment there are many hazardous materials involved. This unit provides information on the Personal Protective Equipment (PPE) necessary to work with these materials.
  Why PPE is important in microsystems manufacturing
  Types of PPE used in microsystems manufacturing
  How to use the PPE appropriately

## Slide 3: Objectives
  State why PPE should be used when handling hazardous materials.
  State the types of PPE commonly used in microsystems manufacturing.
  Describe the appropriate use of PPE for a specific situation.

## Slide 4: Why Do You Need to Know About PPE?
  There are many chemical processes involved in the manufacturing of microsystems
  Large amounts of acids, bases, and solvents are used
  Chemical use can be dangerous
  When working with chemicals, PPE must be used
PPE required for acids, corrosives
[Picture courtesy of Bob Willis]

## Slide 5: The Shape of Hazardous Materials
Hazardous materials can be in the following forms:
Liquids
Solids
Gases
Vapors
Fumes
Mists
Fibers
Dust
Types of Hazardous Materials used in Microsystems Fabrication
Use the appropriate PPE when working with any
hazardous chemical or equipment.

## Slide 6: Hazards Present in Microsystems Manufacturing
Common hazards in a microsystems manufacturing environment:
  Health Hazard - Exposure to dangerous chemicals may cause acute or chronic health effects.
  Physical Hazard - A violent change occurs when subjected to external factors such as heat, vibration, or oxygen, or in some cases, normal temperature and pressure.
  Equipment Hazard - Exposure to dangerous equipment and/or equipment supplies or tools.

## Slide 7: Specific Hazards
What are some chemicals that could be a health hazard?
What are some chemicals that create physical hazards?
What are some types of equipment hazards?

## Slide 8: Specific Hazards
What are some types of chemicals that could be a health hazard?
  Carcinogens, corrosives, poisons, irritants, teratogens
What are some types of chemicals that create physical hazards?
  Flammables, explosives, radioactive, oxidizers
What are some types of equipment hazards?
  Electrical, mechanical movement, radiation, hot surfaces

## Slide 9: Routes of Entry
Hazardous chemicals may cause bodily damage by one or more of the following routes of entry:
  Inhalation - breathing it in
  Dermal (Absorption) - penetrating or irritating the skin or eye
  Ingestion - swallowing

## Slide 10: Health Hazards
Common health effects caused by exposure to a hazardous chemical.
  Irritant - irritating effect
  Sensitizer - allergy developed over time
  Asphyxiant - suffocation
  Carcinogen - cancer causing
  Mutagen - changes genetic makeup
  Teratogen - affects developing fetus

## Slide 11: Common PPE
PPE includes clothing and other accessories designed to protect against hazards during work and/or play. Here are some examples of PPE:
  Bullet proof vests
  Fire protective gear
  Oven mitts
  Helmets
PPE makes working and playing safer and more productive.

## Slide 12: Your Turn
What are some common PPE that you use on a regular basis?

## Slide 13: PPE Used in Microsystems Manufacturing
OSHA has PPE Standard
  PPE OSHA Standard - 29 CFR 1910.132-138
  Employers must establish and administer proper PPE, a PPE program and PPE training
PPE is available for the following parts of the body:
  Respiratory system
  Hands
  Eyes and face
  Feet
  Body

## Slide 14: Atmospheric Hazards
Atmospheric hazards may exist in these forms:
  Fumes
  Gases
  Vapors
  Particles
Fumes
  Contain both gases (vapors) and dusts
  Require more careful attention than dusts or vapors
  Need to control the generation of fumes
  Use fume hoods and other engineering controls

## Slide 15: PPE for the Respiratory System
What is a Respirator?
  A respirator is used when ventilation controls are not available
  A respirator is worn over the nose and mouth
  Two types of respirators which will be discussed:
  Air Purifying Respirators (left picture)
  Supplied Air Respirators (right picture)
Air Purifying Respirator and Supplied Air Respirator
[Pictures courtesy of MATEC]

## Slide 16: How to Use a Respiratory
Concerns Before Using a Respirator
  Using a respirator requires the lungs and the heart to work harder
  If you have heart or lung conditions, a respirator may be dangerous
  Facial hair prevents the respirator from making a proper seal
  Shave any facial hair that touches the edge of the respirator
Properly Fitting a Respirator
  You must be fit-tested by a qualified person at least once a year
  A seal check must be performed every time a respirator is used

## Slide 17: How to Perform a Seal Check
  Firmly cover the exhalation ports on the mask with the palms of your hands
  Inhale and exhale more strongly than usual
  If no air flows in or out of the respirator's seal is detected, then the respirator fits properly.

## Slide 18: PPE for Hands
Hand protection is required when handling acids or solvents. It is important to wear "acid gloves" when working with acids and "solvent gloves" when working with solvents.
Acid Gloves and Solvent Gloves

## Slide 19: Proper Use of Acid and Solvent Gloves
  Wear over cleanroom disposable gloves
  Acid gloves - thick rubber based composites (nitrile rubber, butyl rubber, natural rubber)
  Solvent gloves - commonly made of thick nitrile
  Make a 2" cuff to prevent chemical from running down the arm
  When removing, pull from the cuffs, turning the gloves inside out.
  Place into the respective acid or solvent waste container
[Pictures courtesy of Bob Willis]

## Slide 20: PPE for Hand (Continued)
Leak Test
Acid gloves and solvent gloves must be checked for holes or leaks
  Test Method 1: Seal the edges of the glove to your mouth with your hand, blow into it like a balloon. Listen for air leaks.
  Test Method 2: Inflate with nitrogen and submerse in water. Watch for bubbles.
If a leak is detected, dispose of the glove. Perform the leak test with a new pair of gloves. Repeat this process until no leaks are found.

## Slide 21: PPE for Eyes
Safety Glasses and Eye Goggles
  Eye goggles and/or safety glasses are common gowning attire
  Safety glasses and goggles must have side shields
  Contact lenses are discouraged when working in a cleanroom; therefore, goggles or safety glasses are generally made to fit over eye glasses
  Eye goggles and safety glasses can be made with prescription lenses

## Slide 22: PPE for Face
Face Shield
  A special face shield must be worn when working with acids and solvents
  Safety goggles or glasses must be worn to cover the eyes at all time
  The face shield is worn over the goggles or glasses

## Slide 23: PPE for the body
Acid Aprons
  Extra protection is required above and beyond a cleanroom smock or bunnysuit when using acids or solvents
  In the case of a splash or spill, acid aprons can be removed quicker than a bunnysuit or smock
  Acid aprons are commonly made from a rubber based composite
  Aprons should be removed carefully to prevent any chemicals on the aprons from contaminating other areas

## Slide 24: More PPE for the Body
Chemical Resistant Splash Suits
  Chemical resistant splash suits offer a high degree of protection against a wide range of chemical contaminants
  They are commonly used when cleaning hazardous material spills
  They are commonly made from Neoprene or a rubber based composite

## Slide 25: PPE for the Feet
  PPE protects the feet from chemical spills and dropped objects
  Cleanroom booties do not provide adequate protection
  Non-porous, closed toe shoes with a closed heel must be worn under the booties
Chemical Resistant Boots
  Worn when cleaning up hazardous chemical spills

## Slide 26: Summary
  Manufacturing microsystems involves hazardous materials
  It is essential to understand the dangers involved and the proper PPE
  This SCO discussed the hazards in the workplace and the PPE needed to protect from any bodily injury
  When using PPE, it is also important to ensure that it is being used properly

## Slide 27: Disclaimer
The information contained herein is considered to be true and accurate; however the Southwest Center for Microsystems Education (SCME) makes no guarantees concerning the authenticity of any statement. SCME accepts no liability for the content of this unit, or for the consequences of any actions taken on the basis of the information provided.

## Slide 28: Acknowledgements
Made possible through grants from the National Science Foundation Department of Undergraduate Education #0830384, 0902411, and 1205138.
Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and creators, and do not necessarily reflect the views of the National Science Foundation.
Southwest Center for Microsystems Education (SCME) NSF ATE Center© 2009 Regents of the University of New Mexico
Content is protected by the CC Attribution Non-Commercial Share Alike license.
Website: www.scme-nm.org
Revision – March 2017