## Slide 1: Control Charts
A JIT on-line process tool
Detects assignable causes
Shows “inherent” variation of the process
Looks @ “controllable” parameters
Shows the capability of the process

## Slide 2: Control Charts
Used to reduce variability
Used to determine process capability
Prevents system tampering
Provides diagnostic information
Tells what the process is doing NOW and has done in the past
Used to predict the future

## Slide 3: Control Charts
Technicians use control charts “hourly”, everyday to keep track of what the process “is doing”.
Engineers used control charts periodically to see what the process “has done”, the estimate what the process is “capable” of doing.

## Slide 4: Control Charts
UCL
UWL
TARGET
LWL
LCL

## Slide 5: Western Electric Rules
Rule 1:
One point outside the UCL or LCL.
UCL
LCL
Target

## Slide 6: Western Electric Rules
Rule 2:
2 of 3 consecutive points between 2 and 3 Sx from the target.
UCL
LCL
Target
2 Sx
1 Sx
1 Sx
2 Sx

## Slide 7: Western Electric Rules
Rule 3:
4 of 5 consecutive points beyond +/- 1Sx from the target.
UCL
LCL
Target
2 Sx
1 Sx
1 Sx
2 Sx

## Slide 8: Western Electric Rules
Rule 4:
8 consecutive points on one side of target.
UCL
LCL
Target
2 Sx
1 Sx
1 Sx
2 Sx

## Slide 9: Western Electric Rules
Rule 5:
Approx. 14+ points high/low/high/low without interruption.
UCL
LCL
Target
2 Sx
1 Sx
1 Sx
2 Sx

## Slide 10: Western Electric Rules
Rule 6: (Trends)
7 consecutive points increasing or decreasing.
UCL
LCL
Target
2 Sx
1 Sx
1 Sx
2 Sx

## Slide 11: Western Electric Rules
Rule 7:
15+ points within +/- 1 Sx either above or below center line.
UCL
LCL
Target
2 Sx
1 Sx
1 Sx
2 Sx

## Slide 12: Western Electric Rules
Rule 8:
8 consecutive points on both sides of the Target and outside +/- 1 Sx..
UCL
LCL
Target
2 Sx
1 Sx
1 Sx
2 Sx

## Slide 13: Western Electric Rules
Rule 9:
A tendency of one chart to follow another.
X-bar chart
R - chart

## Slide 14: Patterns
Cyclic or oscillatory patterns
Sawtooth

## Slide 15: Patterns
Trends

## Slide 16: Patterns
Mixtures
Shift in Process