## Slide 1
Using MEMS Processes to Teach a 6-Step Approach to Solving Problems
MJ Willis
Instructional Developer
Southwest Center for Microsystems Education

## Slide 2: Project Definition
Using a process from the microtechnology or MEMS
manufacturing industry, students are
required to solve a process problem
or production problem
using a systematic approach to
problem solving.

## Slide 3: Project Criteria
Select a MEMS process
Develop a process flow chart with process steps and quality checks.
Identify quality criteria
Identify equipment requirements
Determine throughput times for each process step and for the total process.

## Slide 4: 6-Steps to Problem Solving
Recognize the a problem exists
Analyze the problem (Collect information)
Identify possible causes to the problem
Evaluate possible causes
Develop an action plan to correct the problem and take action.
Verify that the problem has been corrected.

## Slide 5: Student Example
Process: Silicon wafer manufacturing
Process start @ raw materials
Process end @ finished silicon wafer
300 mm process
Projection of 17,000 wafers / week

## Slide 6: Process Flowchart

## Slide 7: Process Flowchart

## Slide 8: Quality Criteria
QC1: Oxygen content, purification check
QC2: Purification
QC3: Handling temperature
QC4: Resistivity, dimensions
QC5: Flatness, chemical contamination, particle count

## Slide 9: Quality Criteria (con’t)
QC6: Edge damage, chemical contamination, particle count
QC7: Thickness, uniformity, chemical contamination, particle count
QC8: Chemical contamination, defect distribution, particles
QC9: Particles, dimensions, roughness, flatness, crystal defects, resistivity, contamination, oxygen content

## Slide 10: Equipment List
Furnace
Fluidized - Bed Reactor
Deposition
Crusher
Crystal puller
Diameter Grinder
End Remover
Wire Saw
Scribe Machine
Wafer Cleaner
Edge Grinder
Lapping Machine
Etcher
Edge Polisher
Surface Polisher
Wafer scrubber

## Slide 11: Problem Statement - Step 1
The winter of 2012-2013 showed a 45% decrease in the sell of silicon worldwide and projections for the remainder of 2013 show a continued decrease in sells of about 5% per quarter.
In an effort to show a positive revenue for 2013, company management has calculated that it needs to decrease its production by 25% of its current output and decrease its current defect rate from 16% to 8%.

## Slide 12: Deliverable
Management has asked you to present an action plan that shows how the production team will decrease the defect rate from 16% to 8% and decrease production by 25% by the September of 2013.
(Assume this project was assigned May 1, 2013 for the purpose of your timeline. You have been given 3 weeks to develop a plan and put it in place by June 1.)

## Slide 13: Analyze the Problem - Step 2
What are the specific defects? See defect analysis
When are they happening? See % scrap rate chart
Where are the defects happening?(at what stage)
See defect analysis
Did we lose customers or are they ordering less product? Ordering less product
Is the defect in the same area?
See the %scrap rate chart and defect analysis
Did we change to our backup equipment?
Because of the decrease in orders, you did not use your backup equipment

## Slide 14: Analyze the Problem
Did we change our routine?(specs, raw materials, suppliers, personnel) You added a chemical supplier
Are the quality checks being done properly? Step 3
Is there possible storage of materials or product? Step 3
Are the quality checks precise enough? Step 3
Are there possibilities for a merger or sell out?
No, not if you save your yearly revenues by decreasing defects and coming up with an efficient way of reducing production costs

## Slide 15: Defect Analysis (%scrap)

## Slide 16: Defect Analysis (Defects)

## Slide 17: Analysis of contamination
What is the particle count at each checkpoint on the wafer? Is particle count a problem?
Is our cleanroom still functioning correctly? Step 3
When did we add our new chemical supplier? December 2012
Are we still using chemicals from other suppliers? Yes
Are the chemicals from the new supplier being used on all machines? No, just one
Did the problem start when we added this new supplier? Yes - as seen on %scrap

## Slide 18: Analysis of wafer thickness
How many lapping machines were we using and how many how we now using?
You were using 4 machines and in October, you shut one down and produced all orders on 3 lapping machines.
Are the wafers too thick / thin? Too thick
What is the deviation from the standard?
Average of 10 microns (out of contr0l)
Are the defective wafers found on all lapping machines? No, just one

## Slide 19: Identify possible causes - Step 3
Wafers Too
thick (out of control)
Methods
Materials
Equipment
Personnel
Incorrect measuring of wafers
Incorrect placement of wafers
Wrong concentration of slurry
Use of incorrect chemicals
Faulty machine
Not enough pressure
Poor calibration
All vs. one machine
Wire saw cutting wafers too thick
Slow rotation
High absentee rate
Incorrect placement of wafers
Incorrect measurements
Incorrect programming
Incorrect monitoring of process
Wrong recipe
Bad Slurry
New
Employees

## Slide 20: Evaluate possible causes - Step 4
Are the defects happening during a specific shift (day/night)? No
What does the attendance of the techs look like?
You don't have an absentee problem
Are any of the operators new? No
Are the new employees being properly trained? Yes
Is the slurry recipe correct? Yes
Were the right chemicals used in the lapping machine? Yes

## Slide 21: Evaluate possible causes - Step 4
When were the lapping machines last calibrated?
All lapping machines are calibrated quarterly
When were the measuring tools last calibrated?
Daily - Analytical tools are calibrated at the beginning of each shift
Are the wafers being placed in the lapping machine properly? Yes
Have the machines been properly programmed? Yes
Is the program correct? Yes

## Slide 22: Evaluate possible causes - Step 4
Are the machines receiving proper maintenance and cleaning?
All preventative maintenance procedures are being completed as scheduled
Are the chemicals being replaced as often as they should be? Yes
Is the spin speed too slow? Yes
Do we have a problem with our rpm transducer? Yes

## Slide 23: Action Plan - Step 5
Contamination
Work with chemical company to set up a new SPC system
  Who? Process Engineering
  When? 3 months
Audit the chemical company regularly
  Who? Technicians (Trained as auditors)
  When? Quarterly

## Slide 24: Action Plan - Step 5
Wafer Thickness
Rotate lapping machine out of production
  When? Immediately
Replace transducer
  Who? Equipment technicians
Test
  Who? Equipment technicians and calibration technicians

## Slide 25: Verification - Step 6
Contamination
Audit the supplier quarterly to ensure highest standards
Wafer Thickness
Incorporate rpm check to quarterly calibration
QC wafers from individual machines instead of random wafer check

## Slide 26: Project Presentation
Students defend their solution and action plan to the Management Team.
The Management Team is composed of other students, instructors, and industry representatives.