## Slide 1: Wheatstone Bridge Overview
Micro Pressure Sensors & The Wheatstone Bridge Learning Module

## Slide 2: Unit Overview
This Wheatstone Bridge Overview provides information on the electronic circuitry of a Wheatstone bridge.
This overview will help you to understand how a Wheatstone bridge is used for sensing changes in pressure when used in a micro pressure sensor.

## Slide 3: Objectives
Define the variable components of the Wheatstone bridge
Describe how the Wheatstone bridge works

## Slide 4: Introduction to Wheatstone Bridge
An electrical circuit design dating back to early 1800's
Named for its most famous user, Sir Charles Wheatstone who
  never claimed to have invented it, but did develop multiple uses for it
  called the circuit a “Differential Resistance Measurer”
Sir Charles Wheatstone
National Portrait Gallery, London
  Invented by Samuel Hunter Christie (1784-1865)
  One of the most sensitive and precise methods of measuring small changes in resistance through its use of transducers.
  Widely used today in macro and micro-sized sensors

## Slide 5: The Wheatstone Bridge
A simple circuit used to measure small changes in resistance of a transducer.
Classic configuration consists of four resistors
  Three fixed value and one variable value
  Variable resistor is the sensing element (transducer) (See R4 in diagram below)
  Resistance of the variable resistor changes due to a change in an environmental factor such as stress, pressure, or temperature
Basic Wheatstone bridge Configuration with one transducer or sensing element (R4)

## Slide 6: The Wheatstone Bridge – 2 Variable Resistors
Maximized effect of the input
Provides the largest voltage variation as a function of the changing input
Has 2 fixed resistors & 2 variable resistors (transducers/sensing elements)
DC voltage source (Vin) such as a battery or power supply
Output voltage (Vg) represents the difference in the transducers’ resistance values to the reference resistance of the bridge configuration
Design allows for the measurement of very small changes in the environmental factor that affects the transducers while greatly suppressing electrical noise and thus improving the “signal to noise ratio”
Basic Wheatstone Bridge Configuration with two transducers or sensing elements (R1 and R4)

## Slide 7: Background Circuits
There are three concepts discussed here which are needed to understand Wheatstone bridges:
  Resistor voltage dividers
  Ohm’s Law (I=V/R)
  Kirchoff’s Circuit Laws

## Slide 8: Resistor Voltage Dividers
Diagram below is made up of two resistors labeled R1, R2, and a power supply Vin (battery).
Electron flow or current Iin (measured in Amperes (A)) travels from the negative terminal of the battery through the resistors to the positive terminal of the battery.
Resistive Voltage Divider

## Slide 9: Ohm’s Law
Ohm's Law determines the voltage drop across a resistor if the resistance R and current I are both known.
Ohm's Law states: V = IR
  where V is the voltage across a resistor R that has current I flowing through it
In the Resistive Voltage Divider circuit to the right, the voltage drop, V1 across resistor R1 is
  V1 = IinR1
The voltage drop, V2 across resistor R2 is
  V2 = IinR2.
  A voltmeter measures across R2 with one lead at ground and the other connected between R1 and R2
Resistive Voltage Divider

## Slide 10: Ohm’s Law cont…
Let's put some numbers to this Voltage divider circuit and check out our calculations.
Using Ohm's Law, calculate Iin,V1 and V2
Now try it!
Iin is the current which flows through the circuit
Vin is the voltage applied to the circuit
Rt is the total resistance that the current flows through

## Slide 11: Ohm’s Law cont…
Let’s see how you did:
The total circuit resistance Rt = R1 + R2
The voltage drop, V1 across resistor R1 is
V1 = IinR1 or 10mA*500 W = 0.01A*500 W =5V
The voltage drop, V2 across resistor R2 is
V2 = IinR2 or 10mA*500 W = 0.01A*500 W =5V

## Slide 12: Kirchoff’s Law
Kirchhoff’s voltage law, states that the sum of the voltage drops across a collection of resistors arranged in series within a circuit is equal to the applied voltage (Vin).
Notice that the previous problem shows this to be true:
10 v (Vin) = 5 v + 5v
or

## Slide 13: Kirchoff’s Law cont…
The voltage drop across a specific resistor in series with other resistors is the fraction of that resistor to the sum of the series resistors, multiplied by the applied voltage.
The formula is derived on the right.
Applying the values of the previous circuit, we get:

## Slide 14: Kirchoff’s Law cont…
Wheatstone bridge has two such voltage dividers connected in parallel
Analysis of the resistive voltage divider circuit can be applied to the Wheatstone bridge circuit.
Identify the two voltage divider circuits in the circuit below,
Wheatstone bridge with 2 variable resistors

## Slide 15: Wheatstone Bridge and Difference Voltage
This figure shows the schematic circuit diagram of a Wheatstone bridge. The resistor pair R1 and R2 is a resistive voltage divider and resistors R3 and R4 form another voltage divider in parallel with R1 and R2.
Wheatstone bridge with one variable resistor

## Slide 16: Wheatstone Bridge and Difference Voltage cont…
The circuit is sensitive to the difference in voltage between node-a and node-b. Va and Vb can be explained by:
Wheatstone bridge with one variable resistor

## Slide 17: Wheatstone Bridge and Difference Voltage cont…
Bridge is balanced when Vab = 0 volts
This occurs when R1/R2 = R3/R4
In a typical sensing device, a variable resistor R4 (RS) is used
Other three resistors are fixed
Wheatstone bridge is initially balanced with all of the R’s having the same resistance value by design, including RS (the resistance of the sensing element).
Value of RS changes when the external environment changes thus affecting Vab as

## Slide 18: One Variable Resistor
Assuming the transducer resistance RS is initially 100 W, and R1 = R2 = R3 = 100 W, then Vab can be plotted versus RS.
Bridge is balanced when
RS = 100 W
Vab=0 volts
Changes in the environment affects resistance creating an unbalanced bridge
This results in a voltage proportional to resistance change

## Slide 19: Two Variable Resistors
Adding another variable resistor results in a more sensitive circuit
Where R1 and R4 are both variable resistors
If the R1 and R4 resistors are both variable and react in the same manner to an external environmental change, then the effect on the output voltage, Vab is multiplied!
Wheatstone bridge with two variable resistors

## Slide 20: Two Variable Resistors
Graphing Vab as a function of the variable resistances of R1 and R4 (in this case changing by the same amount while the other two, R2 and R3 remain constant at 100Ω) results in the following graph.

## Slide 21: Wheatstone Bridge as a Micro Pressure Sensor
When the Wheatstone bridge is used in a micro pressure sensor, the resistors are oriented such that R1 and R4 are variable under the stress of a flexible membrane on which they are made.
Wheatstone bridge as a Pressure Sensor
Micro Pressure Sensor illustrating the Wheatstone bridge and the Silicon Nitride Membrane (Diaphragm)
Membrane
(Diaphragm)

## Slide 22: Calibration
To calibrate a Wheatstone bridge as a pressure transducer, a series of known pressure differences is applied to the sensing element(s).
The output voltage (Vab) is measured using a voltmeter
Vab versus pressure is plotted
When an unknown pressure is applied and the output voltage read, the calibration curve of Vab vs. Pressure can be used to determine the actual pressure.

## Slide 23: Summary
Wheatstone bridge is a simple circuit used to measure transducer responses by measuring changes in voltage.
Basic circuit analysis is used to determine the resistance when the bridge is balanced.
Any changes in transducer resistance cause the bridge to be unbalanced providing a voltage roughly proportional to the change in resistance and corresponding to the change in pressure.
A voltmeter measures the output of the Wheatstone bridge which can be equated to a corresponding pressure.
In a micro pressure sensor where the Wheatstone bridge is the sensing circuit, its output can be amplified and processed to send information or to initiate a mechanical response.

## Slide 24: Acknowledgements
Made possible through grants from the National Science Foundation Department of Undergraduate Education #0830384, 0902411, and 1205138.
Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and creators, and do not necessarily reflect the views of the National Science Foundation.
Southwest Center for Microsystems Education (SCME) NSF ATE Center
© 2012 Regents of the University of New Mexico
Content is protected by the CC Attribution Non-Commercial Share Alike license.
Website: www.scme-nm.org
Revised Feb 2017