## Slide 1: BioMems applications Overview
BioMEMS Applications Learning Module
Biochip slide for testing protein arrays
[Image courtesy of Argonne National Laboratories]

## Slide 2: Unit Overview
Imagine a device that restores sight when implanted on the retina of the eye, or a "skin patch" capable of detecting an invading microorganism before symptoms develop.
These are two possible future applications of bioMEMS devices.
This unit explores several current and future applications of bioMEMS.

## Slide 3: Objectives
  Summarize at least three (3) areas of applications for bioMEMS devices.
  Describe specific examples within at least three (3) areas of applications for bioMEMS devices.
  Analyze advantages and possible disadvantages of bioMEMS devices.

## Slide 4: BioMEMS Market
BioMEMS products include
  DNA and protein analysis chips (microarrays)
  Lab-on-a-chip (LOC) devices
  Miniaturized sensors for smart catheters
  Chemical and biological sensors
  Optical devices for medical imaging
"..over the past few years, bioMEMS devices have become the largest and most diverse applications of MEMS devices." (R&D Magazine)
MicroCHIPS Subcutaneous Activie Drug Delivery System contains a reservoir, microprocessor, and sensor feedback system allowing for a controlled release of a drug.
[Figure reproduced by permission of MicroCHIPS, Inc.]

## Slide 5: What You Will Learn?
This unit answers the questions
  Where might you encounter bioMEMS devices?
  How will bioMEMS impact your life?

## Slide 6: The State of bioMEMS
Applications for bioMEMS devices exist in clinical medicine and environmental, biological, and chemical analysis.
Applications can be
clinical diagnostics and therapeutics,
environmental applications including Homeland Security,
food safety, and
bioprocessing.
In addition, there are basic research applications that inform and drive applications in other areas.
BioMEMS is expected to revolutionize the field of medicine.

## Slide 7: BioMEMS Sensor Placement
BioMEMS sensor placement depends on the device and its application.
A sensor can be
  topical (applied to skin or placed in the mouth)
  externally connected (in vitro or external with in vivo or internal device)
  implanted devices (totally in vivo)

## Slide 8: Topical Sensors
Topical sensors are those that are applied to skin or placed in the mouth.
One familiar device is the thermometer used for measuring body temperature.
Thick-film disposable thermistors and infrared ear thermometers have largely replaced the mercury thermometer.
Infrared Ear Thermometer
[Image courtesy of NASA Jet Propulsion Laboratory)

## Slide 9: Externally Connected bioMEMS
Externally connected sensors are devices that contain both an in vivo part and an external part.
An example of such a device is the cochlear implant (see figure).
These devices contain a microphone, a speech processor, a transmitter and receiver/stimulator, and an electrode array.
The implant gives a deaf person a useful representation of his environment.
Cochlear Implant
[Modified from image courtesy of National Institute of Health]

## Slide 10: Other Externally Connected bioMEMS
The MiniMed system (shown above) uses an in vivo glucose sensor that transmits its results to a micropump that delivers insulin continuously to the body
The One Touch© PingTM uses skin sensors to measure blood sugar without a poke or a prick.
GlucoDay® S consists of a micro-pump and a microfiber biosensor inserted under the skin.
MiniMed Paradigm[R] 522 insulin pump, with MiniLinkTM transmitter and infusion set. [Printed with permission from Medtronic Diabetes]
Glucometers and Drug Delivery Systems

## Slide 11: Implantable bioMEMS
The third category of sensor is the fully implanted device. This area of bioMEMS has numerous possibilities, but few of these devices have made it to market. Implantable bioMEMS that have been on the market for years are defibrillators and pacemakers (see graphics below).
(Left) Implantable Defibrillator (used to control dangerous irregular heartbeats)
(Right) Implantable Pacemaker (used to control less-dangerous irregular heartbeats or to beat the heart in cases of second and third-degree heart block)
[Courtesy of National Heart Lung and Blood Institute – National Institute of Health]

## Slide 12: Implantable bioMEMS
Other emerging applications for implantable devices include the following:
Neural implants
Spinal cord stimulators to treat intractable pain and spasticity.
Pressure sensors for cardiovascular monitoring, glaucoma monitoring, and monitoring of intracranial pressure
It may take years for more of these devices to get FDA approval due to the regulations for proof of concept to prototype to FDA approval.

## Slide 13: Biological Molecules Sensors
Biological molecules have the ability to detect and recognize other biomolecules. This characteristic has enabled the development of biosensors that detect, capture and analyze specific analytes.
An example - The home pregnancy test kit that employs antibodies as biosensors. The antibodies have an attached reporter group which detects a protein produced during pregnancy and present in the urine.
Home Pregnancy Test

## Slide 14: Glucometer
The glucometer is a diagnostic biosensor that monitors blood glucose levels of diabetics from a single drop of blood.
It contains a strip impregnated with enzymes that react with glucose, and an electrode which tracks chemical changes through fluctuations in current.
This is an external glucometer that requires the patient to place a drop of blood on the MEMS sensor. To get the blood sample, the patient must prick a finger.
The glucose in the blood reacts with the enzymes on the coating of the biosensor. Gluconolactone is produced releasing an electron.

## Slide 15: Implantable Glucometer
Implantable devices cross the boundary into therapeutics and contain an actuator or micropump that administers the necessary glucose. The implantable glucometer (C) shown in the picture
monitors the glucose (C) and
delivers insulin on an as-needed basis using a micropump (A) and cannula (B).
D is the transmitter that relays the information from the glucose sensor (C) to the computer (A).
MiniMed Paradigm[R] REAL-Time System from Medtronic Diabetes [Printed with permission from Medtronic Diabetes]

## Slide 16: BioMEMS Microfluidics
Microfluidics are integrated microchips that allow separations, chemical reactions, and calibration-free measurements to be directly performed with minute quantities of complex samples (blood, environmental gases).
Microfluidics applications are used in remote locations for clinical diagnostics and environmental sensing.
Lab-on-a-Chip (LOC) systems enable the design of small, portable, rugged, low-cost, easy to use, yet extremely versatile and capable diagnostic instruments.
Lab-on-a-chip (LOC)
[Printed with permission from Blazej,R.G.,Kumaresan,P. and Mathies, R.A. PNAS 103,7240-7245 (2006)]

## Slide 17: ELISA
BioLOC developed a LOC to perform ELISAs (Enzyme-linked Immunosorbent Assays) on a polymeric compact disk (shown in the figure).
ELISAs use antibodies as biosensors for applications such as
  medical diagnostics and research
  drug screening
  food safety
  environmental monitoring
BioLOC's CD-ELISATM
[Printed with permission of BioLOC LLC]

## Slide 18: DNA and bioMEMS
DNA microarrays are tools used to analyze and measure the activity of genes as well as detect and identify specific genes and gene mutations.
The DNA microarray in the graphic uses single-stranded DNA probes to identify the target DNA in a sample.
Identifying specific DNA through the hybridization process
(Graphic illustrates what happens in a DNA microarray: The target single strand DNA in the test samples bond with a complementary DNA probe on the substrate creating a hybrid and enabling the identification of the target DNA as well as its quantity and/or activity in the sample.)

## Slide 19: DNA and bioMEMS
Microarrays measure changes in gene expression (activity) and thereby identify how cells respond to a disease, a drug or drug dosage, or another stimuli.
Gene expression microarrays measure tens of thousands of genes on a single array and provide scientists the data to understand regulatory processes at the cellular level.
Gene expression values from microarray experiments can be represented as heat maps or optical maps to visualize the results of data analysis. The green represents activity between probe DNA on the array and target DNA in the control sample. Red represents activity between probe DNA and DNA in the test sample. The black areas represent no activity with either the control or test sample.
[This image is public domain. Image source: Wikipedia: Gene Expression Profiling]

## Slide 20: Protein and bioMEMS
Like DNA microarrays, protein microarrays
  allow for the simultaneous analysis of thousands of proteins
  provide a high throughput study of protein abundance and function
  allow for the creation of antigen microarrays for vaccine development and the diagnosis of infectious diseases.
Biochip slide for testing protein arrays
[Image courtesy of Argonne National Laboratories]
The picture shows a biochip slide developed at Argonne National Laboratories. Each biochip has hundreds to thousands of gel drops on a glass, plastic or membrane support. The biochip system can identify infectious disease strains in less than 15 minutes when testing protein arrays and in less than two hours when testing nucleic acid arrays.

## Slide 21: Therapeutics: Drug Delivery Systems
Pumps delivering insulin in implantable devices are examples of a drug delivery system (see figure).
Other examples include the Medtronic SynchroMed Pump that administers morphine within the spine, and piezoelectrically activated pumping devices used for various drug delivery applications.
Insulin pump for drug delivery system
[Printed with permission from Debiotech SA]
In 2014 Debiotech introduced its JewelPUMP Insulin delivery platform with smartphone remote control for diabetic patients. The JewelPUMP is a patch containing a reservoir that holds a week’s worth of insulin, a MEMS pump-chip, canula and nano-sized needle.

## Slide 22: Microchips
Microchips are being developed that contain arrays of micro-reservoirs each of which can contain combinations of drugs, biosensors, or reagents/chemicals.
Such an example is the MicroCHIPS drug delivery system in the figure.
Microspheres or beads are also being exploited in drug delivery systems where they function as carriers of drugs.
Microspheres can stay in the bloodstream or at the site for prolonged periods of time, providing slow release of the drug. (Some of these devices are still in development as of 2014.)
MicroCHIPS Subcutaneous Active Drug Delivery System
This technology is unique in its use of wireless signaling, its system of reservoirs allowing precise, efficient delivery of solids, liquids or gels, and its small size.
[Figure reproduced by permission of MicroCHIPS, Inc.]

## Slide 23: Environmental Applications
Environmental applications are a growing part of the bioMEMS field.
One example adds a gene from a firefly to mammalian cells so that the cells glow when exposed to the toxin dioxin (see figure).
As the amount of dioxin increases, the cells glow more brightly.
This assay provides a quick and simple test for dioxin.
The figure shows how the firefly luciferase reporter gene luminesces to test for the presence of dioxin in environmental samples.
Firefly luciferase reporter gene
[National Institute of Environmental Health Sciences, NIH, Photo credit: Michael Dension
Printed with permission]

## Slide 24: Environmental Applications
Rapid detection and identification of bacteria and other pathogens.
Researchers are working on microdevices for detecting pathogens in a sample concentration. A working example is the surface acoustic wave (SAW) sensor array developed by Sandia National Labs. This device provides portable, rapid detection and early warning of the presence of pathogens in air or water.
The eight-sensor MicroChemLab surface acoustic wave (SAW) based sensor system-on-a-chip is capable of near simultaneous detection of a wide variety of chemical compounds. It is about the size of dime. [Image courtesy of Sandia National Laboratories]
ORANGE YOU TINY? -- Some 30 individual chips with acoustic wave sensors make up this quarter of a wafer, which fits nicely on an orange slice. [Image courtesy of Sandia National Laboratories]

## Slide 25: Additional Applications
Many other bioMEMS applications have been developed and are emerging:
  point-of-care clinical diagnosis
  neural probes
  nerve regeneration
  retinal implants
  tissue engineering (see figure)
  olfactory sensors
Artificial Kidney Tissue
[© The Charles Stark Draper Laboratory, Inc. All rights reserved. Reprinted with permission]

## Slide 26: What Do You Think?
  Why do biological molecules provide an approach to the development of specific biosensors?
  What are some examples of bioMEMS that have been approved for commercialization during the past 5 years?
  How have bioMEMS impacted your life?

## Slide 27: Summary
Based on the numerous applications and application possibilities, it seems safe to say that bioMEMS devices will impact every aspect of our lives, from medical devices to food and environmental screening. Ultimately these systems promise to significantly improve medical care on a global scale.

## Slide 28: Disclaimer
The information contained herein is considered to be true and accurate; however the Southwest Center for Microsystems Education (SCME) makes no guarantees concerning the authenticity of any statement. SCME accepts no liability for the content of this unit, or for the consequences of any actions taken on the basis of the information provided.

## Slide 29: Acknowledgements
Made possible through grants from the National Science Foundation Department of Undergraduate Education #0830384, 0902411, and 1205138.
Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and creators, and do not necessarily reflect the views of the National Science Foundation.
Southwest Center for Microsystems Education (SCME) NSF ATE Center
© 2010 Regents of the University of New Mexico
Content is protected by the CC Attribution Non-Commercial Share Alike license.
Website: www.scme-nm.org
This Learning Module was developed in conjunction with Bio-Link, a National Science Foundation Advanced Technological Education (ATE) Center for Biotechnology @ www.bio-link.org.
August 2017