## Slide 1: biomems and their applications
Southwest Center for Microsystems Education
Capsule for Endoscopy and Colonscopy
Scme-nm.org

## Slide 2: MEMS and bioMEMS
MEMS (Microelectromechnical Systems) use micro-sized components for transducers, sensors, transducers, and electronic components.
MEMS used in the medical field are called bioMEMS.
Notes: MEMS (Microelectromechnical Systems) use micro-sized components for sensors, transducers, actuators, and electronic devices.
Many of the MEMS used in the medical field perform the same tasks as those used in other applications such as environmental, aerospace and consumer products.
For example, the MEMS inertial sensor found in airbag deployment mechanisms is also found in a pacemaker
MEMS used in the medical field are called bioMEMS

## Slide 3: BioMEMS Currently on the Market
24/7 Therapeutics for diabetics
[Printed with permission from Medtronic Diabetes]
Cochlear Implant
Notes: BioMEMS currently on the market include this 24/7 therapeutics system for diabetics that not only monitors glucose levels with an internal sensor shown here at location C, but provides a precise amount of insulin when needed via a cannula and micro-sized needle inserted below the skin. There are also systems in use that help monitor and maintain a healthy heart rate such as pacemakers and defibrillators and systems that improve the hearing for those who can not hear. This cochlear implant uses an electrode array implanted inside the ear to stimulate the eardrum when it receives audio vibrations from an external transmitter. The implant gives a deaf person a useful representation of his environment.

## Slide 4: BioMEMS in the Future
Artificial Kidney Tissue
[© The Charles Stark Draper Laboratory, Inc. All rights reserved. Reprinted with permission]
Liposome Vesicle
Filled with a drug to be used for selective treatment
Notes: The possibilities for bioMEMS in the future is endless. Tissue engineering is a huge field that is working toward the development of artificial organs and organ tissue to help alleviate some of the problems surrounding organ failure and organ donation. This image shows artificial kidney tissue developed by The Charles Stark Draper Laboratory.
The development of drug delivery systems that can identify specific tissue or cells is another huge market. Microtechnology is already developing and producing some types of in vivo drug development system, but is still working on the perfecting systems with high selectivity and specificity, such as using micro-sized liposome vesicle to carry drugs through the bloodstream to a specific cancerous tissue where is attaches to the tissue and releases a drug that kills the cancerous tissue. A number of lipsomes microparticles are already on the market such as those being used to delivery antimicrobial drugs for diseases such as tuberculosis, and there are many more being tested in clinical trials for the delivery of cancer drugs, anti-inflammatories, antibiotics and even for cosmetic applications.

## Slide 5: What are BioMEMS?
BioMEMS are MEMS that have biological and/or biomedical functions or applications.
Defibrillators and Pacemakers [Image sourtesy of National Heart Lung and Blood Institute – National Institute of Health]
Notes: So what exactly are bioMEMS? In general, bioMEMS are MEMS that are used in the medical field. For example, pacemakers and defibrillators are bioMEMS that use the same MEMS accelerometers that are found in cars, iphones and cameras. Such MEMS perform a medical application or function.
Other types of bioMEMS use biological components to perform a medical function or application. These cantilevers use biomolecules to identify and grab hold of other specific biomolecules. For example, our bodies produce antibodies when they sense invading antigens such as viruses and bacteria. These antibodies can be placed on the surface of biological sensors such as these cantilevers, to identify a specific virus or bacteria in a small sample of blood or other bodily fluid.

## Slide 6: The State of bioMEMS
Detection
Analysis
Diagnostics
Drug Delivery
Cell Culture
New Emerging
Therapeutics
"..over the past few years, bioMEMS devices have become the largest and most diverse applications of MEMS devices.“
(R&D Magazine)
Notes: Applications for bioMEMS devices exist in clinical medicine and environmental, biological, and chemical analysis.
Applications can be
clinical diagnostics and therapeutics,
environmental applications including Homeland Security,
food safety, and
bioprocessing.
In addition, there are basic research applications that inform and drive applications in other areas.
BioMEMS is expected to revolutionize the field of medicine.

## Slide 7: BioMEMS Sensor Placement
BioMEMS sensor placement depends on the device and its application.
A sensor can be
  topical (applied to skin or placed in the mouth)
  externally connected (in vitro or external with in vivo or internal device)
  implanted devices (totally in vivo)

## Slide 8: Topical Sensors
Applied to skin or placed in the mouth.
  Thermometer used for measuring body temperature.
  Thick-film disposable thermistors and infrared ear thermometers
Infrared Ear Thermometer
[Image courtesy of NASA Jet Propulsion Laboratory)
Notes: Applied to skin or placed in the mouth.
One familiar device is the thermometer used for measuring body temperature.
Thick-film disposable thermistors and infrared ear thermometers have largely replaced the mercury thermometer.

## Slide 9: Externally Connected bioMEMS
Devices that contain both an in vivo and in vitro part.
Retinal Prosthesis
Notes: Externally connected sensors are devices that contain both an in vivo part and an external part.
An example of such a device is the retinal prosthesis. This bioMEMS contains a micro-sized electrode array that is implanted on the retinal tissue in the back of the eye. The patient wears glasses that contain a video camera, receiver and transmitter that sends signals to the array, stimulating individual electrodes on the array which in turn, stimulate the cells below the retina. This stimulation travels up the optic nerve to the brain which interprets the signal and provides a “rough visual”. This bioMEMS has given some blind people a somewhat useful representation of they are looking at – “it’s better than nothing” as one might say.

## Slide 10: Implantable or In Vivo bioMEMS
Pill Cam (Capsule Endoscopy)
A small pill that is swallowed by the patient and gives the physician high resolution images of the patient’s gastrointestinal tract, particularly the small intestines.
Has an eight hour battery life
Can supply up to 57,000 images at 2 frames/second.
Notes: The third category of bioMEMS is the fully implanted device or in vivo device. This area of bioMEMS has numerous possibilities, but few of these devices have made it to market. Implantable bioMEMS that have been on the market for years are defibrillators and pacemakers we mentioned earlier. Such devices have been around since the 1970’s. Another in vivo bioMEMS currently on the market is this pill used for endoscopy and colonscopies. This pill, about the size of a calcium pill contains its on light source, battery, camera, lens and transmitter. The patient swallows the pill in the morning and goes about his daily routine. During the day, the pill travels through the entire gastrointestinal or GI track – the esophagus, stomach, small intestine and large intestine – recording color images at a rate of 2 frames per second. The images are transmitted to a receiver that the patient wears on his belt. At the end of the day the patient returns the receiver to the clinic where the images are downloaded and analyzed. The pill is expelled and flushed within 12 hours.
Source of specifications: http://www.eetimes.com/document.asp?doc_id=1281134

## Slide 11: Other Implantable bioMEMS
Neural probes (right)
Various probes for internal use (below)
Notes: Other emerging applications for implantable devices include the following:
Neural implants and probes, Spinal cord stimulators to treat intractable pain and spasticity.
Pressure sensors for cardiovascular monitoring, glaucoma monitoring, and monitoring of intracranial pressure
It may take years for more of these devices to get FDA approval due to the regulations for proof of concept to prototype to FDA approval.

## Slide 12: Biological Molecules Sensors
Home Pregnancy Test
Glucometer
Notes: Biological molecules have the ability to detect and recognize other biomolecules. This characteristic has enabled the development of biosensors that detect, capture and analyze specific analytes.
An example - The home pregnancy test kit that employs antibodies as biosensors. The antibodies have an attached reporter group which detects a protein produced during pregnancy and present in the urine.
The glucometer is a diagnostic biosensor that monitors blood glucose levels of diabetics from a single drop of blood.
It contains a strip impregnated with enzymes that react with glucose, and an electrode which tracks chemical changes through fluctuations in current. This is an external glucometer that requires the patient to place a drop of blood on the MEMS sensor. To get the blood sample, the patient must prick a finger.
The glucose in the blood reacts with the enzymes on the coating of the biosensor. Gluconolactone is produced releasing an electron.

## Slide 13: BioMEMS Lab-on-a-Chip (LOC)
Lab-on-a-chip (LOC)
[Printed with permission from Blazej,R.G.,Kumaresan,P. and Mathies, R.A. PNAS 103,7240-7245 (2006)]
Notes: Microfluidics are integrated microchips that allow separations, chemical reactions, and calibration-free measurements to be directly performed with minute quantities of complex samples (blood, environmental gases). . One such microfluidic device is the lab-on-a chip or LOC. The previous two bioMEMS – the pregnancy test and the glucometer – are types of LOCs. Lab on a chip is a general term for a micro-size devices that can test for the presence of biological molecules or analytes. Some devices test for one or a few analytes, such this LOC that test for HIV and heptitis C and B from the same sample. Such applications of LOCs allow for remote testing and home based testing. Still in the design and development phase are the LOCs that can accurately test for many analytics from one small sample. One day, a person may only need to provide a drop of blood to get a complete blood analysis, rather than several vials. The image on the right is just such a device. You can see the numerous fluidic channels through which the sample flows. In each channel the sample is tested for a different analyte.
Lab-on-a-Chip (LOC) systems enable the design of small, portable, rugged, low-cost, easy to use, yet extremely versatile and capable diagnostic instruments that can be used in remote locations for clinical diagnostics as well as environmental sensing.

## Slide 14: DNA and bioMEMS
The single strand DNA target in the test samples bond with a complementary DNA probe on the microarray creating a hybrid and enabling the identification of the target DNA as well as its quantity and/or activity in the sample.
Notes: DNA microarrays are tools used to analyze and measure the activity of genes as well as detect and identify specific genes and gene mutations.
The DNA microarray in the graphic uses single-stranded DNA probes called oligonucleotides to identify the target DNA in a sample. One DNA microarray can consist of thousands of addresses, with each speicific address consisting of hundreds of identical probes. This image illustrate a DNA microarray here at the base and it expands to illustrate a single address. Notice that all of the probes on this address are identical.
To identify the presence or activity of DNA in a sample (like the DNA from a cancer patient), copies of the patient’s DNA are made into single-stranded DNA copies which are the targets. When the base pairs of a target match up with the base pairs of a probe, a double-stranded DNA hybrid is formed. The green and red tags at the top of the targets help to identify specific hybridization during the interpretation process.

## Slide 15: MEMS Cell Culture Array
Grows cell in vitro and in parallel
Developed by and images courtesy of BioPOETS Lab, UC-Berkeley
Notes: BioPOETS at the Univerity of California Berkeley has developed a MEMS cell culture array. This array uses microfluidics to create an optimal micro-environment for cell cultivation. This array creates a microenvironment for growing cells in vitro and in parallel, allowing for the analysis of multiple cell growth conditions. The inset shows the microenvironment of each array component.

## Slide 16: Summary
Detection
Analysis
Diagnostics
Drug Delivery
Cell Culture
New Emerging
Therapeutics
Notes: Based on the numerous applications and application possibilities, it seems safe to say that bioMEMS devices will impact every aspect of our lives, from medical devices to food and environmental screening. Ultimately these systems promise to significantly improve medical care on a global scale.

## Slide 17: © Southwestern Center for Microsystems Education
For more information about BioMEMS, please visit our website:
www.scme-nm.org
Click on Educational Materials to view and download our series of learning modules on BioMEMS.
This video was made possible through a grant from the National Science Foundation DUE#1205138.