## Slide 1: Safety Data Sheets (SDS)
SCME Safety Data Sheets Learning Module
Chemical
Safety LLC
Safety Data Sheet
Composition, Information on Ingredients
Component: Boron Trichloride (BCL3)
CAS Number: 10294-34-5
Percent: 100.0%
Hazard Classification: Corrosive

## Slide 2: Unit Overview
To work safely in a facility that manufactures MEMS devices, you must understand the purpose of a SDS. You must also be able to extract information about a specific chemical from its SDS. This unit provides information on how to locate and interpret a SDS.
Allow at least 15 minutes to review this material.

## Slide 3: Learning Module Objectives
Interpret the contents of at least three SDSs for specific chemicals.
Identify the applications of at least three chemicals in microtechnology fabrication processes.
Define the basic terms used by a SDS to describe a chemical’s hazards

## Slide 4: Introduction
A Safety Data Sheet (SDS) is a document that provides the necessary information about a chemical to all personnel that
  use it,
  transport it,
  store it, or
  work around it in any manner.
SDS Section 1
Chemical
Safety LLC
Product and Company Information
Boron Trichloride
Product ID: Boron Trichloride
Date of SDS: 01/10/2014
Technical Review Date: 08/1/2014
Manufacturer: Chemical Safety LLC
555 Our Chemical St.
Safety, NC 00099-3333
Emergency Phone #: (111) 000-2222
Trade Names/Synonyms: BCL3, Boron Chloride, TriChloroboron
Chemical Family: non-metallic, halides

## Slide 5: Availability Requirement
A SDS is required by Federal law to be prepared for each chemical imported or produced in this country.
It is the chemical manufacturer’s responsibility to prepare the SDS.
It is the responsibility of the employer to maintain an updated SDS for all chemicals on the premises and to make them readily accessible to all employees.

## Slide 6: What is in a SDS?
Examples of information contained in a SDS
  Hazards associated with a chemical
  Physical properties
  Handling information
  Emergency procedures for spills or human contact
  Flammability and reactivity properties
  Toxicity

## Slide 7: When should you review a SDS?
Before storing, handling or working with a chemical in any manner, you should become familiar with the information provided in the chemical's SDS.
Working with Chemicals

## Slide 8: OSHA Requirements
OSHA’s* Hazardous Communication Standard (29 CFR 1910.1200) requires sixteen (16) sections that must be on a SDS.
These sections are explored in this learning module.
Additional sections are optional.
*U.S. Occupational Health and Safety Administration (OSHA), an agency of the U.S. Department of Labor.

## Slide 9: SDS Terminology
Much of the terminology found on a SDS is related to hazardous material, such as toxicity, flashpoint, and reactivity.
There are SDS glossaries that provide definitions for many of these terms.
The SDS Hyperglossary is a great reference.

## Slide 10: A few SDS Acronyms
LEL and UEL (Lower and upper explosive limits) –
  The minimum/maximum concentration of a liquid’s vapor in air above which a flame does not occur.
TLV (Threshold Limit Value) –
  The airborne concentration of a chemical.
PEL (Permissible Exposure Limit) –
  Similar to TLV, but set by OSHA
PPE – Personal Protective Equipment

## Slide 11: Requirements of a SDS
  Product Identification
  Hazards(s) Identification
  Composition / information on ingredients
  First-aid measures
  Fire-fighting measures
  Accidental Release measures
  Handling and storage
  Exposure controls/personal protection

## Slide 12: Requirements of a SDS (continued)
  Physical and chemical properties
  Stability and reactivity
  Toxicological information
  Ecological information
  Disposal considerations
  Transport information
  Regulatory information
  Other information including date of preparation

## Slide 13: Product Identification
  Date of SDS
  Chemical Manufacturer's Name, address, and emergency telephone numbers
  Product Name
  Chemical Name
  Generic Name, Synonyms
  Hazard Classification
Chemical
Safety LLC
Product and Company Information
Boron Trichloride
Product ID: Boron Trichloride
Date of SDS: 01/10/2014
Technical Review Date: 08/1/2014
Manufacturer: Chemical Safety LLC
555 Our Chemical St.
Safety, NC 00099-3333
Emergency Phone #: (111) 000-2222
Trade Names/Synonyms: BCL3, Boron Chloride, TriChloroboron
Chemical Family: non-metallic, halides

## Slide 14: Question
Which of the following would be considered a product name?
a. Isopropyl Alcohol
b. Fingernail polish remover
c. Acetone
d. Chlorine

## Slide 15: Hazard(s) Identification
  Classification
  Hazard statement/symbol, precautionary statement
  Potential Hazards
Chemical
Safety LLC
Safety Data Sheet – BCL3
Hazard(s) Identification
NFPA Ratings: Health 3 Fire 0 Reactivity 2
Color: colorless
Physical Form: fuming liquid, gas
Odor: pungent odor
May cause respiratory tract burns, skin burns, eye burns, mucous membrane burns.
Containers may rupture or explode is exposed to heat.
Releases toxic, corrosive, flammable or explosive gas

## Slide 16: Exposure Controls/Personal Protection
  Significant animal studies which determine the chemical's toxicity
  Toxicity data
  Legal Exposure Limits (PEL, TLV)
  Appropriate engineering controls (e.g., eye wash – top image)
  Individual protection measures (PPE) (e.g., acid gloves)

## Slide 17: Physical and Chemical Properties
  Appearance and Odor
  Boiling Point and Freezing Point
  Melting Point
  Vapor Pressure
  Vapor Density
  Solubility in Water
  Evaporation Rate
  Specific Gravity
Physical Properties of BCl3

## Slide 18: Fire and Explosion Data
  Flammability Data
  Flashpoint
  LEL (Lower Explosive Limit)
  UEL (Upper Explosive Limit)
  Fire Fighting Comments
  Fire fighting procedures
  Extinguishing media
  Unusual fire hazards
Fire / Explosion Hazards of BCl3

## Slide 19: Stability and Reactivity
  Chemical stability
  Reactivity
  Possibility of hazardous reactions
  Conditions to avoid
  Incompatible materials
  Hazardous decomposition byproducts
Reactivity Data of BCl3

## Slide 20: Question
What are LEL and UEL?

## Slide 21: Question
What are LEL and UEL?
  Answer: The LEL and the UEL are the lower and upper explosive limits. Permissible exposure limits are the PEL and TLV. Both are legal limits expressed in ppm.

## Slide 22: Other Information on SDSs
  Precautions for handling this chemical
  Conditions for safe storage, including any incompatibles
  Toxicological Information
    Routes of exposure
    Delayed and immediate effects of exposure
    Measures of toxicity
  Disposal considerations (non-mandatory)
  Transport information (non-mandatory)

## Slide 23: Summary
A SDS is your information source about a chemical. Before working with or around a chemical, you should always study the appropriate SDS. Know where the SDS notebook or resource is located.

## Slide 24: Acknowledgements
Made possible through grants from the National Science Foundation Department of Undergraduate Education #0830384, 0902411, and 1205138.
Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and creators, and do not necessarily reflect the views of the National Science Foundation.
Southwest Center for Microsystems Education (SCME) NSF ATE Center© 2012 Regents of the University of New Mexico
Content is protected by the CC Attribution Non-Commercial Share Alike license.
Website: www.scme-nm.org
Revision – Jan 2017