## Slide 1: Basic Controls I Control Loops & Controller Hardware
Gina Becker
Presented to
MATC HVAC Students
10/7/19 & 10/10/19

## Slide 2
Outline: What is a Control Loop
TOPICS
  Sensors
  Automated Devices
  Process
  Control Loop
  Control Strategies
  Controller Hardware

## Slide 3
Overview of Controllers
SENSORS
Sensor: A device that detects & measures a physical property:
Sensor | Physical Property
Thermistor/ Thermocouple | Temperature
Pressure Sensor | Pressure
Motion Sensor | Movement
Flow Meter | Flow Rate
Scale | Weight
Light Detector | Light Level
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA
Notes: Pressure sensors include pressure transducers, transmitters, and switches.

## Slide 4
CONTROLS RESEARCH ACTIVITY 01: TEMPERATURE SENSORS
Useful References:
  Controls Research Activity_01Temp Sensors.docx
  Internet searches on temperature sensors
  Temperature Sensor Output tables
    https://www.bapihvac.com/sensor-specs/
Complete the Controls Research Activity 01

## Slide 5
What is an automated device?
Automated device: A device that is adjusted by computer-controlled mechanisms
NOTE: Devices often require an actuator (motor, relay, piston) to convert an electrical or pneumatic signal into motion.
Automated Device | Adjusted to Change…
Control Valve | Flow Rate/ Pressure/ Temperature
Pump | Flow Rate/ Pressure
Blower | Flow Rate/ Air Speed/ Pressure
Heating element | Temperature
Switch | On/ Off
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA-NC
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA
Notes: This Photo is licensed under CC BY-SA (Photos in presentation were inserted through ppt feature. Free licenses. No author given for attribution.

## Slide 6
What is an Automated Process?
Automated Process: A series of automated procedures, including chemical, physical, electrical or mechanical steps, to achieve a desired end.
Automated Process | Desired End
Toy Ball Production | Discrete manufacturing of toy balls
Chemical Production | Continuous production of chemicals
HVAC System | Continuous control of environmental conditions
Packaging | Packaging of manufactured items
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 7
Process Variables
Process Variable: Measured / monitored physical properties of a process
Water-Loop Process Variables | Units
Inlet Water Temperature | F
Outlet Water Temperature | F
Water Flow Rate | GPM
Valve Position | %
Air-Loop Process Variable | Units
Return Air Temperature | F
Make-up Air Temperature | F
Mixed Air Temperature | %
Return Air Flow Rate | SCFM
Make-up Air Flow Rate | SCFM
Supply Air Flow Rate | SCFM
Blower Speed | RPM
Damper Opening | %
Pressure Drop Across Filter | psi
Damper 1 Position | %
Supply Air
(to bldg rooms)
Mixed Air
Heat Exchanger
Filter
Blower
Return Air

## Slide 8
Controllers & Control Loops
Controller: A computer that directs equipment in a process.
  Gathers data from sensors (“Input”)
  Makes decisions/ calculations based on data & programming
  Sends instructions to devices or actuators (“Output”)
Controller
INPUT
OUTPUT
Process
Adjustment
Measurement
Control Loop

## Slide 9
Electrical Signals in a Control Loop
SENSOR:
Motion detector
Level sensor
Light detector
Pressure sensor
Temperature sensor
Flow meter
CONTROLLED DEVICE:
Pump
Dimmer
Valve
Lamp
Lock
Controller
Input Signal
(sensor reading)
Input Signal
(current status or position)
Output Signal
User Interface:
Computer
Input screen
Input Signal
Error = (Setpoint – Sensor Reading)
CONTROLLED PROCESS
Adjustment
Measurement
Feedback
Setpoint
Notes: Basic flow path of air. Role of heat exchangers and how they work. Role of filter. Ventilation. Role of dampers in air conditioning and ventilation. Mention humidification and fans.

## Slide 10
Overview of Controllers
SENSORS
Active Sensor: Requires an external power source
Example: Thermistor
Must pass current through it
      A resistor used to measure temperature
      Resistance changes with temperature
        Hotter = lower resistance
        Cooler = higher resistance
        Known correlation
      Electrical effect converted and scaled to a signal that a controller can read:
        4 - 20 ma
        0 – 5 V
Involves:
Transducer: Converts a signal of one form into another (e.g. Temperature  Electrical).
Transmitter: Transmits electromagnetic waves that carry a signal (data).
Notes: Pressure sensors include pressure transducers, transmitters, and switches.

## Slide 11
Overview of Controllers
SENSORS
Passive Sensor: Generates its own current
Example: Thermocouple
Generates its own current
      Two different conductive metal wires
      Joined at one end
      Produces a temperature-dependent voltage
      Electrical effect converted, conditioned, and scaled to a signal that a controller can read:
        4 - 20 ma
        0 – 5 V
Involves:
Transducer: Converts a signal of one form into another (e.g. Temperature  Electrical).
Transmitter: Transmits electromagnetic waves that carry a signal (data).
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA
Notes: Pressure sensors include pressure transducers, transmitters, and switches.

## Slide 12
What is an actuator?
Actuator: A device that converts energy (e.g. electrical or pneumatic) into motion:
  Motor Receives electrical signal Changes position of a valve
  Piston Receives pneumatic signal Changes position of a valve

## Slide 13
CONTROLS RESEARCH ACTIVITY 02: ACTUATORS
Useful References:
  Controls Research Activity_02 Actuators.docx
  Internet searches on temperature sensors
Complete the Controls Research Activity 02

## Slide 14
Can you identify the control loop components?
PLC
thermocouple
Hot Plate
Sensor reading = 80F
Setpoint Temperature = 110F
Stirrer
This Photo by Unknown Author is licensed under CC BY-SA
Notes: What is happening in this process? What is the sensor? What is a setpoint? What is the controlled device? What is the controller? What is the error? What type of signals (input/output)? What signal is the PLC sending to the hot plate? What types of calculations might be required?

## Slide 15
Can you identify the control loop components?
PLC
level sensor
valve
motor

## Slide 16
Exhaust Air
(to outside)
Return Air
(from bldg. rooms)
Supply Air
(to bldg rooms)
Outdoor Air
(from outside)
Mixed Air
Dampers
Heat Exchanger
Filter
Blower
Can you suggest control loops & components?
This Photo by Unknown Author is licensed under CC BY-SA
Notes: What is happening in this process? What types of sensors would there be? What types of controlled devices? What types of setpoints? What types of calculations by the controller?

## Slide 17
Controller Hardware
TOPICS
  Types of Controllers
  Controller Connections
  Signals & Controller
  Wiring a controller

## Slide 18
  PLC = Programmable Logic Controllers
  Application
  Supervisory
  Building Automation System
  Industrial
Types of Controllers

## Slide 19
Controller Connections
INPUTS:
Universal Inputs (UI)
  Analog: 0-10VDC, 0-20 mA
  Thermistors: Type II or Type III
  Resistance: 1 k Ω to 100 kΩ
  Contact closure
  Pulse input accumulators
Binary Inputs (BI)
  Contact closure
OUTPUTS:
Analog Outputs (AO)
  0-10V
Binary Outputs (BO)
  Normally Open (NO) switches
  Supply external power
  Low voltage only (24V)

## Slide 20
Controller Connections
Power Input: 24 VAC

## Slide 21
Controller Connections
Cat5e Ethernet Cable
Optional internet connection
Talk to other controllers

## Slide 22
Thermistor Connection

## Slide 23
Controller Wiring Activity
Research each part via internet searches for product specifications and instructions
  Thermistor
  Push Button
  Panel Indicator LED Lamp
Wire each part to the controller (power off)
Test the wiring via the programming software
Write programming to control the lamp via the push button

## Slide 24
Truth Tables

## Slide 25
Take Control of the AC
Replace the Thermostat with the Controller
Develop a wiring diagram
Write a sequence of operations (Light, CFM, EFM)
Wire the Light, CFM, EFM to the controller
Write a program to control the temperature

## Slide 26
https://www.ccontrols.com/basautomation/bastools.php
Download Sedona Software
Can Sedona be downloaded onto anyone’s tablet?