## Slide 1
Type of Material: Instrumentation Review
ACADs (08-006) Covered
Keywords
Direct ionization, indirect ionization, radiation, radiation detection, gas filled detection chambers, anisotropic, Simple Energy spectroscopy, proportional counters, GM tubes, gas ionization, ion chambers.
Description
This PowerPoint presentation is a review of instrumentation.
Supporting Material
1.1.8.1.3 | 3.2.2.1 | 3.2.3.8.1 | 3.2.3.8.2 | 3.2.3.8.4
3.3.3.1 | 4.4.1 | 4.11.1 | 5.4.1.5a | 5.4.1.5.b
5.4.1.5c | 5.4.1.5d |  |  | 

## Slide 2: Instrumentation Review

## Slide 3: Direct and Indirect Ionization
Direct - Charge particles that strip away electrons from atoms
Indirect - uncharged that have to interact with electrons in order to remove them from the atom, these electrons go on to cause ionization.
Notes: Most damage that is done in biological systems is done by indirect ionization.

## Slide 4: Ionization
Theory of operation
  Radiation enters the active volume of the detector
    Several gasses can be used
  Radiation causes ionization of gas
  Negative half of the ion pair (electron) is attracted to the anode wire
    Anode wire is positively charged
  Wire is monitored by electronics and current is measured
  Change in electron density around wire will change current flow

## Slide 5: Radiation Detection Gas Filled Detectors
Air or Other Gas
Incident Ionizing Radiation
Electrical
Current
Measuring
Device
+
-
Cathode -
Anode +
+
+
+
-
-
-
+
-
Voltage Source
Notes: The most common type of instrument is a gas filled radiation detector. This instrument works on the principle that as radiation passes through air or a specific gas, ionization of the molecules in the air occur. When a high voltage is placed between two areas of the gas filled space, the positive ions will be attracted to the negative side of the detector (the cathode) and the free electrons will travel to the positive side (the anode). These charges are collected by the anode and cathode which then form a very small current in the wires going to the detector. By placing a very sensitive current measuring device between the wires from the cathode and anode, the small current measured and displayed as a signal. The more radiation which enters the chamber, the more current displayed by the instrument.

## Slide 6: Gas Filled Detectors
Ion Chambers
Proportional Counters
GM tubes
Notes: Many types of gas-filled detectors exist, but the two most common are the ion chamber used for measuring large amounts of radiation and the Geiger-Muller or GM detector used to measure very small amounts of radiation.

## Slide 7: GAS IONIZATION
Notes: The area at the left of the graph is called the recombination zone and the area on the right is the spontaneous discharge zone. The same detector set up can be used in each of these areas depending on the voltage applied to the detector.

## Slide 8: Ion Chambers
Good agreement between measurements and actual radiation level
Constant response curve
Slow response
Low voltage
Advantage- not energy dependant
Disadvantage- subject to environmental changes, slow
Notes: Ion chambers have a fairly constant response curve which means that the actual reading is very close to the reading on the meter. This is very important if you are trying to calculate dose to someone standing in this field.
Since the ion chamber reacts only to the average number of electrons that are collected on the cathode the response time of the ion chamber is somewhat slow. Also this instrument is used for high levels of radiation and is not good for low level readings.

## Slide 9: Response Curve
Energy (MeV)
0.5
1.0
2.0
Meter reading
Actual reading
1
Notes: Response curve is relatively flat over the usual range of energies that the meter is used for.

## Slide 10: Ion Chambers
Notes: Many manufactures make ion chambers in a variety of forms

## Slide 11: Uses
Survey unknown radionuclides
Survey unknown levels
Survey if you are going to use info for dose estimates

## Slide 12: Proportional Counters
Highly directional (anisotropic)
Simple Energy spectroscopy
Very good at detecting charged particles
Medium Voltage
Able to detect Neutrons
Avalanche- when electrons produced by primary ionization produce ionization themselves as they are accelerated toward the anode
Notes: Proportional counters are a specialized detector and rarely used in portable instruments.

## Slide 13: Proportional Counters
To be able to detect a single particle, the number of ions produced must be increased.
As voltage is increased into the proportional region, the primary ions acquire enough energy to cause secondary ionizations (gas amplification) and increase the charge collected.
These secondary ionizations may cause further ionization
In this region, there is a linear relationship between the number of ion pairs collected and applied voltage.
A charge amplification of 104 can be obtained in the proportional region.

## Slide 14: Proportional Counters

## Slide 15: Proportional Counters
By proper functional arrangements, modifications, and biasing, the proportional counter can be used to detect alpha, beta, gamma, or neutron radiation in mixed radiation fields.
To a limited degree, the fill-gas will determine what type of radiation the proportional counter will be able to detect.
Argon and helium are the most frequently used fill gases and allow for the detection of alpha, beta, and gamma radiation.
When detection of neutrons is necessary, the detectors are usually filled with boron-triflouride gas.

## Slide 16: Proportional Counters
Notes: Various types of proportional counters

## Slide 17: GM Tubes
Most sensitive gas-filled
High voltage
Able to detect gammas, med-high energy betas, and alphas
Can detect charged particles in a gamma background
Overcompensation
Saturation ( not usually worry about)

## Slide 18: Overcompensation
Energy (MeV)
0.5
1.0
2.0
Meter reading
Actual reading
1
Notes: Interactions of low energy photons create an over reaction of the tube at those energies

## Slide 19: Uses
General area survey
Can be used to determine radiation type
Can be used to contamination surveys
Industrial gauging devices
Emergency response

## Slide 20: GM Tubes

## Slide 21: GM Tubes
Notes: Many designs of GM tubes