## Slide 1
ACADs (08-006) Covered
Keywords
Buildup factor
Description
Explain various interactions of ratiation with matter.
Supporting Material
INTERACTIONS OF RADIATION WITH MATTER
4.11.8 |  |  |  |  |  |  | 

## Slide 2: Buildup factor
Any of the common gamma interaction processes may result in secondary photons that have a finite probability of reaching the dose point.
The extent to which such secondary photons add to the fluence or dose at the dose point is usually described through the use of an appropriate buildup factor.
Buildup factors may refer to various quantities of interest, such as photon fluence, photon energy fluence, exposure, or dose, and the values among all are somewhat different.
Notes: shielding_of_gamma_radiation (PDF)
http://hps.org/documents/shielding_of_gamma_radiation.pdf

## Slide 3: Buildup factor
The dose buildup factor is a dimensionless quantity that represents the ratio of total dose (including the dose from secondary photons) at the dose point to primary photon dose at the same point.
The primary photon dose naturally comes from original photons that have penetrated the shielding material without interacting.
Magnitudes of buildup factors vary widely, ranging from a minimum of 1.0 to very large values, depending on source and shield characteristics.
Notes: http://hps.org/documents/shielding_of_gamma_radiation.pdf

## Slide 4: Buildup factor
The ratio of the total photons at a point to the number arriving there without being scattered
In the passage of radiation through a medium, the ratio of the total value of a specified radiation quantity at any point to the contribution to that value from radiation reaching the point without having undergone a collision.
Notes: http://ns.ph.liv.ac.uk/~ajb/radiometrics/glossary/buildup_factor.html
http://www.nucleonica.net/wiki/index.php?title=Buildup_factor
Reference:
Y. Harima, AN HISTORICAL REVIEW AND CURRENT STATUS OF BUILDUP FACTOR CALCULATIONS AND APPLICATIONS, Radiat. Phys. Chem. Vol. 41, No.4/5, pp. 631-472, 1993.